## Slide 1: WF on BS demodulation performance requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20th – 30th Apr., 2020
R4-2005555

## Slide 2: Agreements (1) - General
RAN4 BS demodulation does not impose any restriction on the use of 2-step RACH with respect to cell size
Requirements related to timing offset (TO) is performance, not functional
  TO estimation is up to BS implementation, e.g., preamble or PUSCH DMRS based
Focus on performance requirements for single user case according to the scope of the WID

## Slide 3: Agreements (2) – Introduction of BS demodulation performance requirements for 2-step RACH
MsgA demodulation differs from normal PUSCH demodulation in the following aspects:
  No HARQ for MsgA PUSCH, Target for msgA is missed detection rate, while in normal PUSCH demodulation 70% of maximum throughput is assume for the PUSCH performance requirements
  No TO impact on normal PUSCH performance requirements
  Payload size of MsgA
RAN4 define BS demodulation requirements for 2-step RACH in order to ensure reliable MsgA demodulation performance

## Slide 4: Way forward (1)
RAN4 Discuss and select typical TO values associated with the selected typical UE-gNB distances for performance evaluation and requirement definition

## Slide 5: Way forward (2)
Whether or not TO compensation is assumed when specifying BS performance requirements
  Option 1: Yes
  Option 2: No
  Option 3: Yes, only for Medium/Wide area BS

## Slide 6: Way forward (3)
Whether or not to exclude Local Area BS for BS demodulation requirements for 2-step RACH
  Option 1: Yes
  Option 2: No
    Option 2a: Setting TO = 0 for local area BS

## Slide 7: Way forward (4)
Setup for performance evaluation
  Payload size 56 bits
  Performance metric BLER 0.01
  TO up to 0.9 us for MsgA PUSCH SCS 15 and 30 kHz
  …

## Slide 8: Way forward (5) – work plan
RAN4#95
  Initial simulation configurations and FRC for 2-step RACH MsgA payload
RAN4#96:
  Simulation setup
  Initial simulation results collection and alignment
RAN4#96bis:
  Final round of simulation results collection and alignment
  Draft CR frameworks for introducing BS demodulation requirements for 2-step RACH MsgA payload
RAN4#97:
  CR for TS 38.104 Demodulation performance requirements for 2-step RACH Msg A payload
  CR for TS 38.141-1 Conducted conformance tests for 2-step RACH Msg A payload
  CR for TS 38.141-2 Radiated conformance tests for 2-step RACH Msg A payload

## Slide 9: Appendix(For information only)
Parameter | Values
Preamble format | 0, A2
Waveform | CP-OFDM
Subcarrier spacing for PUSCH | FR1: 15kHz, 30kHz FR2: 60kHz, 120 kHz
PUSCH Mapping type | FR1: A FR2: B
Number of symbols | FR1: 14 FR2: 10
Number of PRBs | 1 PRB, 2 PRBs
TBS | - 56 bits as starting point for minimum payload size - Other values are not precluded
DMRS | 1+1+1
UE antenna configuration | 1Tx
gNB antenna configuration | 2Rx
Propagation channel & UE velocity | TDL-A 30ns, TDL-C 300ns, 3km/h
TO | 15 kHz: 6.77, 1.92, 0.77 us 30 kHz: 1.92, 0.77, 0.38 us 60 kHz: 0.77, 0.38 us 120 kHz: 0.38, 0.19 us Other options are not precluded
Test metric | BLER of MsgA when preambles are correctly detected - Option 1: 0.01 - Option 2: 0.1 - Other values are not precluded
Companies are encouraging to provide simulation results for evaluation in next meeting with the following setup: