## Slide 1: WF on TR/TS structures and common terminology for NR V2X UE
Qualcomm, [vivo]...
3GPP TSG-RAN WG4#95-e Meeting R4-2008446
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Applicability of General Requirements
Sub-topic #2-1
Sub-topic description: TR/TS structure and common terminology for NR V2X UE
Open issues and candidate options before e-meeting:
Issue #2-1-1: General part in TS
Proposals
  Option 1
    General requirements shall apply to V2X communication unless otherwise stated the requirements.
    Consistent with existing 36.101/38.101 spec structure and eliminates multiple single-line references to general requirements
    General requirements apply to V2X (suffix E) unless otherwise stated, so V2X requirements (suffix E) are written only when the requirement differs from the general. This eliminates suffix E clauses.
  Option 2
    General requirements will be applied for smart phone type V2X UE. The UE shall satisfy the general and suffix ‘E’ UE
    The Vehicle type UE only satisfy the Suffix ‘E’ requirement for V2X UE.
    The option is aligned with LTE V2X approach
    Each V2X (suffix E) requirement is explicitly stated in a suffix E clause, including requirements identical to the general. This requires multiple suffix E clauses referring to general requirements
    RAN4 define V2X RF core requirements in general part and suffix E. General part & Suffix E requirements will be applied to Pedistrian-V2X UE (e.g smart phone).
    Suffix E requirements will be applied to Vehicular UE supporting NR V2X sidelink only.
Company preferences/comments
  Option 1 – Vivo, Qualcomm
  Option 2- LGE
  Other companies?
Proposed WF
  Companies please choose between option 1 and 2

## Slide 3: Applicability of General Requirements
Issue #2-1-2: Whether or merge the Coexistence part of chapter 5 and chapter 6 in TR
Proposals
  Option1: Keep the current TR structure since chapter 5 is for adjacent channel inter-device coexistence and chapter 6 is for indevice coexistence analysis for self de-sense problems.
  Option2: Merge Chapter 5 and Chapter 6 as one chapter for co-existence evaluation in TR 38.886.
Company preferences
  Option 1 – LGE, Futurewei, CATT, Huawei
  Option 2 – Vivo
Proposed WF
  Option 1

## Slide 4: Applicability of General Requirements
Issue #2-1-3: Whether or switch the chapter arrangement between Operating bands and Coexistence study
Proposals
  Option1: Keep the current TR structure.
  Option2: Exchange the chapter arrangement between operating band and coexistence study in TR.
Company preferences
  Option 1 – LGE, Futurewei, Huawei
  Option 2 – Vivo
Proposed WF
  Option 1

## Slide 5: Applicability of General Requirements
Issue #2-1-4: Align the clause title for TS and TR for NR V2X
Proposals
  Option1: ‘XXX for V2X Communication’
  Option2: ‘XXX for V2X’
  Option3: ‘XXX for NR V2X UE’
  Option4: ‘XXX for NR V2X’
Company preferences
  Option 1 – Vivo, Qualcomm
  Option 2 – LGE, CATT
  Option 4 – Huawei
Proposed WF
  Companies please choose between option 1 and 2