## Slide 1: WF on intra-band contiguous UL CA MPR and A-MPR remaining issues
Skyworks, Nokia, [Huawei, HiSilicon], [Qualcomm]
R4-2008466
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: WF on contiguous UL CA architecture and capabilities
Baseline architecture for Rel16 use one transmit chain for both BW class B and C UL CA
1TX chain is the default assumption (ie assumed if not signaling of architecture)
if UL MIMO is supported in single CC mode it is supported in CA mode
a single DC location is declared
2PA architecture is not precluded for BW class C
2TX chain signaling is needed to cover:
  Declaration of two DC location instead of one
  UL MIMO support or not
  Potential MPR improvements in future releases

## Slide 3: Background on ACLR MBW position
Agreed measurement bandwidth in last meeting:
where MBWACLR,low and MBWACLR,high are the single-channel ACLR MBWs for channel bandwidths BWChannel(low) and BWChannel(high), respectively, as specified in TS 38-101-1, Table 6.5.2.4.1-1.
Proposed shift in [1]: Difference between of ACLR MBW center and BWChannel_CA center is:
However, the center of aggregated channels corresponds to nothing concrete and may not correspond to TXLO in most of the cases. Fc,low is a better reference as illustrated below
GBlow
MBWaclr,low
Rest of ACLR MBW
MBWaclr,high
GBhigh
FC,low
FC,high
Foffset,high
Foffset,low
MBWACLR,low/2
MBWACLR_CA/2
MBWACLR_CA
BWChannel_CA

## Slide 4: WF on ACLR MBW position
For unambiguous position and validity for multiple CC the ACLR MBW shift is thus reffered to the first CC carrier FC,low :
UL CA ACLR MBW can be captured as in the table below
 | ACLR / Measurement bandwidth
CA ACLR | 30 dB
CA Measurement bandwidth (NOTE 1) | Nominal channel space+ MBWACLR,low/2+ MBWACLR,high/2
Adjacent channel centre frequency offset (in MHz) | + BWChannel_CA / - BWChannel_CA
Difference between ACLR MBW center and Fc,low | MBWshift= (MBWACLR_CA - MBWACLR,low)/2
NOTE 1: MBWACLR,low and MBWACLR,high are the single-channel ACLR measurement bandwidths specified for channel bandwidths BWchannel(low) and BWchannel(high) in 6.5.2.4.1, respectively. | 
Table 6.5A.2.4.1.1-1: General requirements for intra-band contiguous CA ACLR

## Slide 5: Background on Inner and outer contiguous allocation definitions
Inner allocation reuses the same concept than single CC allocation of inner half allocation but applied to the 15kHz SCS equivalent aggregated contiguous allocation

## Slide 6: WF on Inner and outer contiguous allocation definitions
Contiguous allocation definition(lower channel is CC1): RBStart1 + LCRB1 = NRB1, and RBStart2 = 0
In contiguous CA, a contiguous allocation is an inner allocation if
RBStart,Low ≤ RBStart_CA ≤ RBStart,High, and NRB_alloc ≤ ceil(NRB,agg /2),
where
RBStart,Low = max(1, floor(NRB_alloc /2)) , RBStart,High = NRB,agg – RBStart,Low – NRB,alloc,
with
NRB_alloc= (NRB1 - RBStart1)∙ 2^µ1 + (RBStart2 + LCRB2 ) ∙ 2^µ2, NRB,agg=NRB1∙2^µ1+ NRB2∙2^µ2.
If LCRB1 =0, RBStart_CA = NRB1∙2^µ1+ RBStart2∙2^µ2,
else,
RBStart_CA = RBStart1∙2^µ1.
A contiguous allocation that is not an Inner contiguous allocation is an Outer contiguous allocation

## Slide 7: Background on Inner and outer contiguous allocation MPR for Class B and C
Left table is based on [4,5,6] with 3 company inputs for QPSK, two companies for 16/64/256QAM and only one company for Pi/2 BPSK, For comparison LTE table is provided on the right
  NR class B DFT-s-OFDM Outer is at least 1.5dB higher MPR than worst case LTE class C
  Outer for CP-OFDM QPSK is inconsistent
  Some companies show a significant difference (>3dB) between class B and class C for outer allocations while inner allocations have a smaller offset
  Two PA implementations for class C should have lower MPR as shown in [4]
Modulation | CA bandwidth Class B and C / Smallest Component Carrier Transmission Bandwidth Configuration |  |  |  | MPR (dB)
 | 25 RB | 50 RB | 75 RB | 100 RB | 
QPSK | > 8 and ≤ 25 | > 12 and ≤ 50 | > 16 and ≤ 75 | > 18 and ≤ 100 | ≤ 1
QPSK | > 25 | > 50 | > 75 | > 100 | ≤ 2
16 QAM | ≤ 8 | ≤ 12 | ≤ 16 | ≤ 18 | ≤ 1
16 QAM | > 8 and ≤ 25 | > 12 and ≤ 50 | > 16 and ≤ 75 | > 18 and ≤ 100 | ≤ 2
16 QAM | > 25 | > 50 | > 75 | > 100 | ≤ 3
64 QAM | ≤ 8 and allocation wholly contained within a single CC | ≤ 12 and allocation wholly contained within a single CC | ≤ 16 and allocation wholly contained within a single CC | ≤ 18 and allocation wholly contained within a single CC | ≤ 2
64 QAM | > 8 or allocation extends across two CC's | > 12 or allocation extends across two CC's | > 16 or allocation extends across two CC's | > 18 or allocation extends across two CC's | ≤ 3
256 QAM | ≥ 1 |  |  |  | ≤ 5
Modulation |  | MPR for bandwidth class B [dB] |  |  |  | MPR for bandwidth class C [dB] |  |  | 
 |  | inner | Avg | outer | Avg | inner | Avg | outer | Avg
DFT-s-OFDM | Pi/2 BPSK | TBD | 0 | TBD | 1.5 | TBD | na | TBD | 6
 | QPSK | [0-1.5] | 1 | [2-4] | 3.5 | 2.5 | 2.5 | [5-8] | 6.5
 | 16QAM | [1-2] | 1.5 | [3-4] | 3.5 | 2.5 | 2.5 | [6-8] | 7
 | 64QAM | [2.5-4] | 3 | [3.5-4] | 4 | 5 | 5 | [6-8] | 7
 | 256QAM | [6-6.5] | 5.5 | [6-6.5] | 6 | [6.5-7] | 7 | [6.5-8] | 7.5
CP-OFDM | QPSK | [1.5-2] | 2 | [3-5.5] | 4.5 | [3-3.5] | 3.5 | [6-8] | 7
 | 16QAM | [2-2.5] | 2.5 | [3-4] | 3.5 | 3.5 | 3.5 | [6-8] | 7
 | 64QAM | [3.5-4] | 3.5 | [3.5-4] | 4 | 5 | 5 | [6-8] | 7
 | 256QAM | [6-6.5] | 6.5 | [6-6.5] | 6.5 | [6.5-7] | 7 | [6.5-8] | 7.5

## Slide 8: WF on Inner and outer contiguous allocation MPR for Class B and C
This table is applicable to
  1PA architecture for BW class B
  1PA and 2PA architecture for BW class C in Release 16,
  Improved BW class C MPR for 2PA is FFS in future release
  Pi/2 BPSK data is extrapolated from QPSK assuming same ACLR limitation
Modulation |  | MPR for bandwidth class B [dB] |  | MPR for bandwidth class C [dB] | 
 |  | inner | outer | inner | outer
DFT-s-OFDM | Pi/2 BPSK | 1.0 | 3.5 | 2.5 | 7
 | QPSK | 1.0 | 3.5 | 2.5 | 7
 | 16QAM | 1.5 | 3.5 | 2.5 | 7
 | 64QAM | 3.0 | 4.0 | 5 | 7
 | 256QAM | 5.5 | 6.0 | 7 | 7.5
CP-OFDM | QPSK | 2.0 | 4.0 | 3.5 | 8
 | 16QAM | 2.5 | 4.0 | 3.5 | 8
 | 64QAM | 3.5 | 4.0 | 5 | 8
 | 256QAM | 6.5 | 6.5 | 7 | 8

## Slide 9: Background on Inner, outer1 and outer2 non-contiguous allocation definitions
Non-contiguous allocation MPR is driven by the location of the allocation in with regard to the SEM mask
Inner allocations are such that IMD3 fall within BW_CA of the wanted signal and thus IMD5 falls within BW_CA adjacent to the wanted signal => IMD5 needs to meet -13dBm/MHz
Outer1 allocations are such that IMD3 and IMD5 falls within BW_CA adjacent to the wanted signal => IMD3 needs to meet -13dBm/MHz
Outer2 allocations are such that IMD3 falls within BW_CA adjacent to the wanted signal and IMD5 falls within BW_CA second-adjacent to the wanted signal => IMD5 needs to meet -30dBm/MHz
Lower guard BWGB,low
Minimum unallocated RBStart,Low ∙0.18MHz
Allocation & gap NRB_alloc ∙0.18MHz + BWgap
Unallocated
Maximum unallocated RBStart,High ∙0.18MHz
Allocation & gap NRB_alloc ∙0.18MHz + BWgap
Upper guard BWGB,high
Lower guard BWGB,low
Upper guard BWGB,high
Unallocated
Lowest allocation position
Highest allocation position
Required BW between allocation and channel CA edge (Inner)
Required BW between allocation and channel CA edge (Inner)
Required BW between allocation and channel CA edge (Inner)
Required BW between allocation and channel CA edge (Inner)
This illustrates the Inner RBstart,low and high concepts and other parameters used in the allocation definition in following pages
BWChannel_CA

## Slide 10: WF on non-contiguous allocation definitions: Inner allocation
Non-contiguous allocation definition: RBStart1 + LCRB1 < NRB1, or RBStart2 > 0
In contiguous CA, a non-contiguous RB allocation is a non-contiguous Inner RB allocation if the following conditions are met:
RBStart,Low ≤ RBStart_CA ≤ RBStart,High and NRB_alloc ≤ ceil((BWChannel_CA / 3 – BWgap ) / 0.18MHz),
where
NRB_alloc = (NRB1 - RBStart1)∙ 2^µ1 + (RBStart2 + LCRB2 ) ∙ 2^µ2, RBStart_CA = RBStart1∙2^1
RBStart,Low = max(1, floor(NRB_alloc + (BWgap – BWGB,low)/0.18MHz))
RBStart,High = floor((BWChannel_CA – 2 ∙ BWgap – BWGB,low)/0.18MHz – 2 ∙ NRB_alloc)
BWGB,low =Foffset,low – (NRB1∙12+1)∙SCS1/2
BWgap is the bandwidth of the gap between NRB1 and NRB2 possible allocations of CC1 and CC2 respectively.

## Slide 11: WF on non-contiguous allocation definitions: Outer1 and Outer 2 allocations
In contiguous CA, a non-contiguous RB allocation is a non-contiguous outer 1 RB allocation if the following conditions are met:
RBStart,Low ≤ RBStart_CA ≤ RBStart,High and NRB_alloc ≤ ceil((3 BWChannel_CA / 5 – BWgap) / 0.18MHz)
where
RBStart,Low = max(1, 2 ∙ NRB_alloc – floor( (BWChannel_CA – 2 ∙ BWgap + BWGB,low)/0.18MHz)),
RBStart,High = floor((2 ∙ BWChannel_CA – 3 ∙ BWgap – BWGB,low) / 0.18MHz – 3 ∙ NRB_alloc)
NRB_alloc , RBStart_CA , BWgap and BWGB,low are as defined for the Inner region.
In contiguous CA, a non-contiguous allocation is an Outer 2 allocation if it is neither an non-contiguous Inner allocation nor an Outer 1 allocation.

## Slide 12: Background on Inner and outer non-contiguous allocation MPR for Class B and C
Below table is based on 3 company inputs
For UE power class 3 intra-band contiguous carrier aggregation bandwidth class C with non-contiguous resource allocation, the allowed Maximum Power Reduction (MPR) for the maximum output power in Table 6.2.2A-1 is specified as follows
MPR = CEIL { min(MA, MIM5), 0.5}
Where MA is defined as follows for QPSK, 16 QAM and 64 QAM
MA = 8.2; 0 ≤ A < 0.025
9.2 - 40A ; 0.025 ≤ A < 0.05
8 – 16A; 0.05 ≤ A < 0.25
4.83 – 3.33A ; 0.25 ≤ A ≤ 0.4,
3.83 – 0.83A; 0.4 ≤ A ≤ 1,
and MIM5 is defined as follows
MIM5 = 4.5 ; DIM5 < 1.5 * BWChannel_CA
6.0; 1.5 * BWChannel_CA ≤ DIM5 < BWChannel_CA/2 + FOOB
MA; DIM5 ≥ BWChannel_CA/2 + FOOB
Modulation |  | MPR for bandwidth class B [dB] |  |  |  |  |  | MPR for bandwidth class C [dB] |  |  |  |  | 
 |  | inner | Avg | Outer1 | Avg | Outer2 | Avg | inner | Avg | Outer1 | Avg | Outer2 | Avg
DFT-s-OFDM | Pi/2 BPSK | TBD | 2 | TBD | 5.5 | TBD |  | TBD | 2.5 | TBD | 6 | TBD | 
 | QPSK | [0-3] | 2 | [4.5-6] | 5.5 | [9-13] | 10.5 | [0-5] | 2.5 | [4.5-7] | 6 | [9.5-14] | 11.5
 | 16QAM | [1-4] | 2.5 | [4.5-6] | 5.5 |  |  | [1-5] | 3 | [4.5-7] | 6 |  | 
 | 64QAM | [2.5-6] | 4.5 | [4.5-6] | 6 |  |  | [2.5-7] | 5 | [4.5-7] | 6 |  | 
 | 256QAM | [6.5-7] | 6 | [6.5-7] | 6.5 |  |  | [6.5-8] | 6.5 | [6.5-8] | 6.5 |  | 
CP-OFDM | QPSK | [1.5-4] | 2.5 | [5.5-8] | 6.5 |  |  | [1.5-5] | 3.5 | [5.5-8] | 7 |  | 
 | 16QAM | [2-4] | 3 | [5.5-8] | 7 |  |  | [2-5] | 3.5 | [5.5-8] | 7 |  | 
 | 64QAM | [3.5-6] | 5 | [5.5-8] | 7 |  |  | [3.5-6] | 5 | [5.5-8] | 7 |  | 
 | 256QAM | [6.5-8] | 7.5 | [6.5-8] | 7.5 |  |  | [6.5-8] | 7.5 | [6.5-8] | 7.5 |  | 
Left table is based on [4,5,6] with 3 company inputs for QPSK, two companies for 16/64/256QAM and only one company for Pi/2 BPSK, For comparison LTE equation is provided on the right
  NR class B DFT-s-OFDM Outer2 is at least 2dB higher MPR than worst case LTE class C
  Two companies propose that outer1 and outer 2 have MPR dependant on aggregated allocation bandwidth since MPR is dominated by 1RB+1RB IMDs failing SEM, more conservative MPR is acceptable if MPR is reduced at larger BW
  Two PA implementations for class C should have lower MPR as shown in [4]

## Slide 13: WF on Inner and outer non-contiguous allocation MPR for Class B and C
This table is applicable to
  1PA architecture for BW class B
  1PA and 2PA architecture for BW class C in Release 16,
  Improved BW class C MPR for 2PA is FFS in future release
  Pi/2 BPSK data is extrapolated from QPSK assuming same ACLR limitation
Modulation |  | MPR for bandwidth class B [dB] |  |  | MPR for bandwidth class C [dB] |  | 
 |  | Inner | Outer11 | Outer22 | Inner | Outer11 | Outer22
DFT-s-OFDM | Pi/2 BPSK | 2 | 5.5 | 11.5 | 2.5 | 6 | 13
 | QPSK | 2 | 5.5 |  | 2.5 | 6 | 
 | 16QAM | 2.5 | 5.5 |  | 3 | 6 | 
 | 64QAM | 4.5 | 6 |  | 5 | 6 | 
 | 256QAM | 6 | 6.5 |  | 6.5 | 6.5 | 
CP-OFDM | QPSK | 2.5 | 6.5 | 12 | 3.5 | 7 | 14
 | 16QAM | 3 | 7 |  | 3.5 | 7 | 
 | 64QAM | 5 | 7 |  | 5 | 7 | 
 | 256QAM | 7.5 | 7.5 |  | 7.5 | 7.5 | 
NOTE 1: Outer 1 MPR is reduced by 3dB for aggregated allocation bandwidth > 10MHz NOTE 2: Outer 2 MPR is reduced by 4.5dB for aggregated allocation bandwidth > 10MHz |  |  |  |  |  |  | 

## Slide 14: Background on AMPR for NS04 and NS27
NS-04 and NS27 -13dBm/MHz OOB requirement is such that:
  It is covered by contiguous Inner and outer allocations MPR automatically since they meets -13dBm/MHz
  It is covered by non-contiguous Inner and outer1 allocations MPR automatically since IMD3 and IMD5 meets -13dBm/MHz
NS-04 -25dBm/MHz OOB requirement is such that:
  It is covered by non-contiguous outer2 allocations MPR when IMD3 falls within the -13dBm/MHz OOB region (IMD5 meets -30dBm/MHz then)
NS-27 -40dBm/MHz OOB requirement is such that:
  All MPR cannot cover for IM3/5 falling in -40dBm/MHz region
  Only outer2 non-contiguous allocation MPR may cover for IMD7 falling in -40dBm/MHz region

## Slide 15: WF on AMPR for NS04 and NS27
A-MPR for NS-04 and NS27 -13dBm/MHz OOB requirement is studied for channel and allocation positions when outer2 non contiguous allocation fall in this region
A-MPR for NS-04 -25dBm/MHz OOB requirement is studied for channel and allocation positions when:
  Contiguous outer IMD3 spectrum overlaps with this region
  Non-contiguous outer1 IMD3 spectrum overlaps with this region
A-MPR for NS-27 -40dBm/MHz OOB requirement is studied for channel and allocation positions when:
  Contiguous inner and outer IMD3 spectrum overlaps with this region
  Non-contiguous allocation IM3/5/7 fall in this region

## Slide 16
References in this meeting
References on Bandwidth definitions
[1] R4-2008010 ACLR measurement center frequency for NR FR1 contiguous CA, Nokia, Nokia Shanghai Bell
[2] R4-2008202 Intra-band Contiguous ULCA MBW and ACLR Offset, Qualcomm Incorporated
[3] R4-2008255 [NR FR1 ULCA] Class B and C Bandwidth Verification, Skyworks Solutions Inc.
References on MPR and A-MPR
[4] R4-2008207 Intra-band Contiguous ULCA MPR, Qualcomm Incorporated
[5] R4-2008148 on FR1 UL CA MPR requirement Rel-16, Huawei, HiSilicon
[6] R4-2006638 [NR FR1 ULCA] Class B and C UL CA MPR Proposals and A-MPR Evaluation, Skyworks Solutions Inc.
References on Allocation definition
[7] R4-2006637 [NR FR1 ULCA] Contiguous Intra-band ULCA Allocation Definitions, Skyworks Solutions Inc.