## Slide 1: WF on NR V2X RRM requirements
LG Electronics, MediaTek
3GPP TSG-RAN WG4 #95e
Electronic Meeting, 25 May – 5 June, 2020
R4-2008587

## Slide 2
Part1
  Issue 3-1: Interruption for sync source change between gNB and eNB
    Define this interruption requirement for UE supporting both gNB and eNB as synchronization reference source.
    Capture the spec. as follow.
      When a UE supports both gNB and eNB as synchronization reference source, UE is allowed to drop NR V2X SL transmission or reception for up to 1 ms when synchronization source is changed:
        From gNB
          to eNB
        From eNB
          to gNB
  Issue 3-2: Interruption for switching between LTE SL and NR SL
    Introduce scheduling restriction instead of interruption due to switching between LTE SL and NR SL. The RRM requirements for switching between LTE SL and NR SL shall be aligned with RF conclusion.
  Issue 3-3-2 & 3-3-3: Whether a UE supporting NR SL only is not required to sync to gNB or eNB & Whether to differentiate a UE supporting NR SL only and a UE supporting both NR SL and NR WAN in interruption requirement due to synchronization reference source change
    Introduce applicability rule to interruption requirement due to synchronization source change.
    Capture the spec. as follow.
      When a UE supports NR V2X sidelink only, the UE is allowed to drop NR V2X SL transmission or reception for up to 1 ms when synchronization source is changed:
      …
      When a UE further supports both gNB and eNB as synchronization reference source, the UE is also allowed to drop NR V2X SL transmission or reception for up to 1 ms when synchronization source is changed:
      …
Information for 1st round agreements

## Slide 3
Part 1
  Issue 3-3-4: Whether to introduce when the interruption(1ms) occurs due to sync source change happens
    Keep current spec. unchanged. Related test case will not be defined.
  Issue 3-3-6 : Whether to define interruption requirement on NR SL due to LTE SL sync source is changed
    Do not define interruption requirement on NR SL due to LTE SL sync source is changed
Part 2
  Issue 3-1: Absolute accuracy of PSBCH-RSRP measurement
    Define PSBCH absolute accuracy of ±4.5dB with SNR = -6dB
  Issue 3-2 : Relative accuracy of PSBCH-RSRP measurement
    Define PSBCH relative accuracy of ±2.0dB with SNR = -3dB
Information for 1st round agreements

## Slide 4
RAN4 complete Rel-16 NR V2X core requirements in RAN4#95e.
Newly raised issues in this RAN4#95e meeting do not affect completion of NR V2X RRM core requirements.
The newly raised issues will be further discussed in maintenance part in next RAN4#96e meeting.
  Sync./async. assumption between NR Uu and SL in interruption requirements
  [Whether to differentiate the different type of NR communication in interruption requirement due to synchronization reference source change]
  Whether to define interruption requirement on NR WAN due to switching between LTE SL and NR SL
Whether to define interruption requirement on LTE WAN due to switching between LTE SL and NR SL
  Do not define in Rel-16 because this band combination is not defined in RF session.
Whether to define interruption requirement on LTE SL due to NR SL sync source is changed
  If RAN1 makes agreement related to this issue until this RAN4#95e meeting, RAN4 will further discuss it in maintenance part in next RAN4#96e meeting.
  Otherwise, RAN4 does not define this requirement in R16.
WF

## Slide 5
Interruption for switching between LTE SL and NR SL.
  Capture in spec.
    12.9 Scheduling availability
      This clause contains the requirements related to the scheduling restriction on V2X sidelink due to switch between E-UTRA V2X sidelink and NR V2X sidelink on dedicated carrier. For the NR V2X sidelink, the assumed number of configured symbol in a slot is 14.
      When switch from E-UTRA V2X sidelink to NR V2X sidelink occurs in NR slot ‘n’,
      - UE is not expected to transmit or receive NR V2X sidelink on the slot ‘n’.
      When switch from NR V2X sidelink to E-UTRA V2X sidelink occurs in NR slot ‘n-1’,
      - UE is not expected to transmit or receive NR V2X sidelink on the slot ‘n-1’
      When switch from NR V2X sidelink to E-UTRA V2X sidelink occurs in E-UTRA subframe ‘n’,
      - UE is not expected to transmit or receive E-UTRA V2X sidelink on the subframe ‘n’.
      When switch from E-UTRA V2X sidelink to NR V2X sidelink occurs in E-UTRA subframe ‘n-1’,
      - UE is not expected to transmit or receive E-UTRA V2X sidelink on the subframe ‘n-1’.
  RAN4 assume that 14 symbols(ld=13) in a slot is configured for NR V2X on a dedicated carrier.
WF

## Slide 6
Whether to capture general re-evaluation behavior in RAN4 spec.
  Capture in spec.
    The UE physical layer shall be capable of performing the L1 SL-RSRP measurements on the carrier operating V2X sidelink communication for determining the subset of resources to be excluded in PSSCH resource selection in sidelink transmission mode 2. The L1 SL-RSRP measurement period corresponds to one slot and the measurement shall meet the L1 SL-RSRP measurement accuracy requirement in Section 10. After resource (re-)selection procedure, re-evaluation is performed on the reserved resources by L1 SL-RSRP measurements before transmission of SCI with reservation when the conditions specified in TS 38.214[26] are satisfied.
  Re-evaluation procedure is captured as part of measurement related procedure in this clause for completeness.
  Whether to define test case related to re-evaluation will be discussed in perf. Part.
Absolute accuracy of L1 SL-RSRP measurement
  Define +/- [4.5]dB as working assumption in this RAN4#95e meeting.
  Decide final one value between {4.5, 5.0} in next RAN4#96e meeting.
WF