## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #95-e Meeting
Electronic Meeting, 25th May - 5th Jun 2020
R4-2008679

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | No
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | No
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | No
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | No
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | Yes
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | No
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | No

## Slide 3: Agreement
Define requirement for BC bit-0 UE.
  Requirement for BC bit-0 UE is FFS.
Not to define delay requirement when PUSCH/PUCCH and SRS associated with different QCL-Type A(or C) DL-RSs in one slot

## Slide 4: Way Forward
Whether UE should meet initial transmit timing accuracy requirements after UL spatial relation switch?
  Option 1: No
  Option 2: Yes
Whether to consider timing tracking when associated DL-RS?
  Sub1. Whether to consider timing tracking when associated DL-RS is known but QCLed with a different qcl-Type1 RS?
    Option 1: No
    Option 2: Yes
    Option 3: No requirement will be defined.
    Option 4:
      No for SRS spatial relation changes
      Yes for PUCCH spatial relation changes
  Sub2. Whether to consider timing tracking when associated DL-RS is an unknown DL RS?
    Option 1: No
    Option 2: Yes
    Option 3: No requirement will be defined

## Slide 5: Way Forward
When the UL signal has spatial relation to an unknown DL RS,
  Option 1: UE transmits using previous TX beam
  Option 2: Drop UL transmission until TCI state is known
  Option 3: Up to UE implementation and no need to be specified.

## Slide 6: Way Forward
How to deduce the delay requirement for UE which only supports BC Bit-0 when spatial relation is associated with DL RS?
  Option 1: The same delay requirement as BC Bit-1 UE
  Option 2: Always plus the SRS beam sweeping duration compared to BC Bit-1 UE
  Note: The BC Bit-0 UE doesn’t need to meet the same accuracy requirement with Bit-1 for active spatial relation switch.

## Slide 7: Way Forward
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known spatial relation but the DL RS is not in the active TCI list
  Option 1: THARQ +3ms
  Option 2: THARQ +3ms + time for time tracking if applicable
For unknown spatial relation
  Option 1: THARQ + 3ms+ TL1-RSRP
  Option 2: THARQ + 3ms+ TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 8: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known spatial relation but the DL RS is not in the active TCI list
  Option 1: TRRCprocessing
  Option 2: TRRCprocessing + time for time tracking if applicable
For unknown spatial relation
  Option 1: TRRCprocessing + TL1-RSRP
  Option 2: TRRCprocessing + TL1-RSRP + time for time tracking if applicable
  Option 3: No requirements will be defined
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes