## Slide 1: Way forward on FR2 inter-band CA RRM requirements
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #95-e
Online, 25th May – 05th June, 2020
Agenda: 6.15.1.10
R4-2008998

## Slide 2
For a FR2 inter-band CA combination with using independent beam management, the existing interruption requirements for inter-band CA can be applied.
The following options are considered on how to define the interruption requirements for FR2 inter-band CA with CBM.
    Option 1: the existing interruption requirements of intra-band CA can be applied.
    Option 2: the interruption requirements can be defined as the current interruption with adding a SMTC duration which is the longest SMTC duration among all the serving cells in this FR2 band pair.
    Option 3: RAN4 RRM need feedback on the RF architectures of common beam UEs from RF session, e.g. in different band combinations.
Agreements on interruption requirements

## Slide 3: Agreement on beam management requirements
Beam management resource configuration for CBM UE:
    It is left to network to decide whether to configure BFD/CBD measurements on SCell
Beam management requirements for CBM UE:
    For BFD/CBD on PCell/PSCell
      R15 BFD/CBD measurement requirements in FR2 can be applied for FR2 inter-band CA scenario.
    For BFD/CBD on SCell
      RAN4 to use SCell BFD/CBD requirements as being defined in eMIMO WID as baseline.
    For L1-RSRP reporting.
      R15 L1-RSRP measurement requirements in FR2 can applied for FR2 inter-band CA scenario.

## Slide 4: Agreement on scheduling restriction requirements
Scheduling restriction requirements for IBM UE
    Under the conditions that network does not configure simultaneous UL/DL or mixed numerology if the UE does not have such capability of simultaneousRxTxInterBandCA or simultaneousRxDataSSB-DiffNumerology or supportedSubCarrierSpacingDL.
      There are no scheduling restrictions on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band.
      The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is no scheduling restriction if UE uses independent beam.
FFS whether to define the scheduling restrictions for the following cases for both IBM and CBM.
    Case 1: network configures simultaneous UL/DL between two FR1 bands or between two FR2 bands if the UE does not have the capability of supporting simultaneousRxTxInterBandCA.
    Case 2: network configures mixed numerology on two CCs if the UE does not have the capability of supporting simultaneous reception of with different numerologies in CA.
    Case 3: network configures mixed numerology between SSB and data on two bands if the UE does not have the capability of simultaneousRxDataSSB-DiffNumerology.

## Slide 5: Agreement on measurement restriction requirements
For CBM UEs in FR2 inter-band CA, the existing measurement restriction requirements for FR2 is applied for the RLM/BFD/CBD/L1-RSRP measurements being performed on different FR2 bands.
Measurement restriction requirement for FR2 inter-band CA with IBM
    Under the conditions that network does not configure simultaneous UL/DL or mixed numerology if the UE does not have such capability of simultaneousRxDataSSB-DiffNumerology or supportedSubCarrierSpacingDL.)
      There are no measurement restrictions for the RLM/BFD/CBD/L1-RSRP measurements being performed on different FR2 bands.
FFS whether to define the measurement restrictions for the following cases for both IBM and CBM.
    Case 1: network configures mixed numerology on two CCs if the UE does not have the capability of supporting simultaneous reception of with different numerologies in CA.
    Case 2: network configures mixed numerology between SSB and CSI-RS on two bands if the UE does not have the capability of simultaneousRxDataSSB-DiffNumerology.

## Slide 6: Agreement on SCell activation delay requirements
SCell activation requirement for case 2: SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2
    For CBM UEs in the Case 2, if the target SCell is known, the existing known SCell requirement in the case of“SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1” shall be applied.
    For CBM UEs in the Case 2, if the target SCell is unknown, FFS the SCell activation delay requirements.
      Option 1: the existing SCell activation delay requirements for FR1+FR2 CA without L1-RSRP measurement delay can be reused.
      Other options are not precluded.

## Slide 7: For Informations
RAN4 needs to further study on the following open issues
    The interruption requirements for CBM UE.
    The scheduling restrictions and measurement restrictions due to incorrect network configuration
    The unknown SCell activation requirement for CBM UE in case2.
      Case 2: SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2.