## Slide 1: WF on PC2 EN-DC FDD+TDD HPUE Moderator(China Unicom)
3GPP TSG-RAN WG4 Meeting #95-e R4-2008907
Electronic Meeting, May 25– Jun. 05, 2020

## Slide 2: Backgrounds
The scope of the WI is as following
Target on finishing this WI is in RAN#88.
The objective of this WI is to specify the standard needed for Power Class 2 (PC2) high power UE for EN-DC for 1 LTE FDD band and 1 NR TDD band (23dBm LTE + 23dBm NR and 23dBmLTE + 26dBm NR). The scope of this WI is the example band combination DC_3A_n78n. Specifically, it includes the following aspects:
Design the UE capability report signalling and facilitate SAR compliance based on the outcomes of the studies in TR 37.815
Standardize RF requirements
Evaluate any additional impact to the requirements due to the high power on UL.
Note: RAN4 needs to discuss whether existing RAN2 signalling can be reused to solve the issues in this WI. If there is RAN2 signalling impact then RAN4 will send LS to RAN2 to inform the solution. No RAN2 TUs are requested for this WI.

## Slide 3: Way Forward
Considering this is the last meeting for Rel-16 and WI shall be finalized, and it is unlikely to reach a consensus on “blind” scheme. Two questions are proposed:
  Is it agreeable to set the duty cycle based solution (conclusion in SI) as the baseline to finalize WI, and further treat “blind” scheme as enhancement in TEI or Rel17?
  Is it agreeable to treat vivo’s R4-2008264 as baseline CR?

## Slide 4: Way Forward – Subtopic 1-3
Issues on “blind” scheme (scheme of reducing LTE FDD power)
  Option 1: Not to include “blind” scheme at current stage. (Samsung, Xiaomi, Qualcomm, ZTE, CHTTL, Huawei, OPPO, CU, vivo)
  Option 2: Introduce the “blind” scheme as the baseline. (Ericsson, Vodafone, T-mobile)
  Option 3: Introduce a new item in UE signalling to indicate if “Reduce_FDD_power” is supported. ([vivo])
  Option 4: Introduce “blind” scheme as an option, and UE-based SAR management described in R4-2006654 as the default UE behavior baseline.
  The benefits and the impacts on UE side when introducing the “blind” scheme as the baseline had been further discussed in two meetings, but companies cannot reach consensus.

## Slide 5: Way Forward – Subtopic 1-1
Choosing “default value” or “blind scheme” when capability parameters are absent
  Option 1: Using default value of maxNRDuty for two cases of LTE and NR power combination (Samsung, Xiaomi, Qualcomm, ZTE, [Huawei], CU, vivo)
  Option 2: Following “blind” scheme by reduced power (PLTE) and use of the common UL-DL patterns on the TDD CG (Ericsson, Vodafone, T-mobile)
  Option 3: Assume “Full duty support” when capability parameters are missing(Huawei, OPPO)
  Option 4: Assume “UE-based” SAR management when capability parameters are absent.

## Slide 6: Way Forward – Subtopic 1-2
Choosing “PC fallback” or “blind scheme” when the UL EN-DC scheduling exceeds the UE capability
  Option 1: UE should fallback to PC3 (Samsung, Xiaomi, Qualcomm, ZTE, [CHTTL], Huawei, OPPO, CU, vivo)
  Option 2: “Blind” scheme should be followed (Ericsson, Vodafone, T-mobile)
  Option 3:UEs fallback to PC3 when UL EN-DC scheduling exceeds the UE capability, but add a conditional statement for 100% UL percentage with an upper limit of the UL power setting on the LTE side for each fixed LTE reference configuration. (CHTTL, [vivo])
  Option 4: UE-based scheme followed when the UL EN-DC scheduling exceeds the UE capability.