## Slide 1: WF on remaining issues for NR V2X system parameters
vivo, LGE, Qualcomm,...
3GPP TSG-RAN WG4#95-e Meeting R4-2009166
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background
In this meeting, the progress for the following open issues is captured in this WF.
  Band and channel bandwidths for NR V2X
    Band proposal from the operator
    Channel bandwidths for NR V2X licensed bands
  licensed bands partially used for SL transmission
    UE operations for licensed bands partially used for SL transmission
    RF architecture for V-UE operating in licensed bands partially used for SL
    The core RF requirements
    The synchronization issues for simultaneous SL and Uu transmission

## Slide 3: Sub-topic 1-1 Band and channel bandwidths for NR V2X
Issue 1-1-1: Band proposal from the operator
Proposals
  Option 1: Introduce the entire n79 licensed band for NR-V2X SL operation.
  (Supporting companies :LGE, Huawei, CATT, CMCC, vivo, Qualcomm)
  Option 2: Do not introduce the entire n79 licensed band for NR-V2X SL operation.
Recommended WF
  Option 1.

## Slide 4: Sub-topic 1-1 Band and channel bandwidths for NR V2X
Issue 1-1-2: Channel bandwidths for NR V2X licensed bands
Proposals
Restriction for introducing the channel bandwidths for NR licensed bands
For NR V2X communication, the maximum channel bandwidth for a single SL carrier is 40MHz; for NR V2X con-current operation, the maximum channel bandwidth is 60MHz (40MHz for SL carrier and 20MHz for Uu carrier).
  Option 1: Follow the above restriction in Rel-16.
  Option 2: Do not follow the above restriction in Rel-16. (LGE, Huawei, CATT, CMCC, Qualcomm)
Recommended WF
  Option 2.
FFS
  However, if the licensed band is used for SL, the max CBW should be aligned with that in ITS band, i.e. 40MHz. For con-current operation, Uu channel bandwidths follow the supported CBW defined in NR licensed band and NR SL CBW follow SL supported CBW (up to 40MHz).

## Slide 5: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-1: UE operations for licensed bands partially used for SL transmission
Proposals
  Option 1: In Rel-16, introduce licensed bands partially used for SL on the condition that NR V2X UE can only support PC5 interface accessing the licensed bands partially used for SL transmission. (LGE,CMCC,vivo,Qualcomm)
  [Another way to put Option1:In Rel-16, RAN4 does not consider Uu and SL concurrent operation on the same band by TDM or FDM even if SL only partially uses the license band.]
  Option 2: Deprioritize the synchronization scenario for licensed bands in Rel-16. (CATT, Huawei)
  [Another way to put Option 2: From RAN4 perspective we defer this scenario to a later release]
  Option 3: RAN4 allow single transmission between V2X SL operation and Uu uplink transmission in intra-band con-current V2X operation. (Futurewei)
  [Another way to put Option 3:In Rel-16, RAN4 considers does not prevent Uu and SL concurrent operation on the same band by TDM, but not by FDM at the same time, if SL only partially uses the license band]
Recommended WF
  Option 1 and Option 2 has similar meaning. FFS. Defer the scenario to Rel-17 as mechanism of timing alignment and requirements need further study.

## Slide 6: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-2: RF architecture for V-UE operating in licensed bands partially used for SL
Proposals
  Option 1: n79 FDM UL and SL operation could reuse the same RF structure and related RF component capability of the n79 2UL intra-band CA.
  Option 2: For NR V2X UE, if only SL transmission is allowed for the licensed bands partially used for SL, the RF architecture is assumed as single RF chain(LGE,CMCC,vivo)
  Option 3: For NR V2X UE, if only SL transmission is allowed for the licensed bands partially used for SL, the RF architecture is assumed dual RF chain due to support 2UL intra-band n79 or TDM manner without switching period between NR Uu and NR SL in licensed band.(LGE,CMCC,)
  Option 4: FFS. (Qualcomm)
Recommended WF
  FFS. It can also be further studied when to define the requirements.

## Slide 7: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-3: The core RF requirements
Proposals
  Option 1: RF requirements of the n79 2UL intra-band CA could apply to the synchronized UL and SL FDM operation in licensed band n79.
  Option 2: RF requirements for single carrier operation for NR V2X apply for the NR V2X UE in the scenario where licensed bands partially used for SL transmission under the condition that intra-band con-current operation is excluded in Rel-16.(LGE,Huawei,CATT, CMCC,vivo)
  Option 3: FFS. (Qualcomm)
Recommended WF
  FFS.

## Slide 8: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-4: The synchronization issues for simultaneous SL and Uu transmission
The synchronization reference source
Proposals
  Option 1: For the synchronous operation between Uu and SL in the same licensed TDD bands, NR SL should use network as the synchronization reference source.
  Option 2: The specific synchronization reference source that should be used in different scenarios has already been defined in RAN1 and RAN4 RRM session. RAN4 should follow the guidelines set by RAN1 and agreement in RAN4 RRM session. (Qualcomm)
Recommended WF
  Option1 will be chosen since RAN4 agreed that NR Uu and NR SL shall be synchronous operated in licensed band due to eliminate interference between NR SL transmission and NR Uu reception based on the conclusion of co-existence evaluation
  Align with RAN1 decision and RAN4 RRM agreement

## Slide 9: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-4: The synchronization issues for simultaneous SL and Uu transmission
Transmission timing between Uu and SL
Proposals
  Option 1: SL transmission timing should be aligned with the UL timing of NR Uu not the DL timing.
  Option 2: This is in RAN1 scope and is currently being discussed in RAN1.(Qualcomm)
Recommended WF
  Option 1:In RRM session, RAN4 already decided the transmission timing between Uu and SL. Is it possible to revert the agreement at this moment? It will be further discussed in Rel-17 or maintenance of 5G V2X WI.
  Option2:This is in RAN1 scope and is currently being discussed in RAN1.

## Slide 10: Sub-topic 1-2 licensed bands partially used for SL transmission
Issue 1-2-4: The synchronization issues for simultaneous SL and Uu transmission
The frequency separation between Uu and SL
Proposals
  Option 1: RAN4 carefully check the frequency separation between V2X SL operation and Uu uplink transmission in n79 for con-current V2X operation. Then, the V2X_n79-n79 can support in Rel-17.
  Option 2: The frequency separation between Uu and SL should be based on the results of a Uu/SL coexistence study.(Qualcomm)
Recommended WF
  Both options mentioned that the frequency separation will be studied in Rel-17.

## Slide 11: References
[1] R4-2006762, Discussion the remaining issues for n79 NR-V2X, CMCC
[2] R4-2008220, On synchronization scenario for NR V2X in licensed band, Huawei, HiSilicon
[3] R4-2007092, Further discussion on the synchronization mechanism between SL and Uu in the same TDD licensed band, vivo
[4] R4-2006757, Discussion on SL-Uu simultaneous transmission in a UE in licensed band in rel-16, LGE