## Slide 1: WF on Power Amplifier Model in 60 GHz
Skyworks Solutions Inc.
3GPP TSG-RAN WG4 Meeting #96-e R4-2011840 e-Meeting, August 17-28 2020

## Slide 2: Background
Many companies provided their view [1-5] on potential UE PA models valid for 52.6 to 71 GHz range.
There is general agreement that:
  PA model including Rapp is not needed for RAN1 work and that there is no agreed RAN4 parameters for a PA model
  PA model choice is left to the companies for RAN4 work but that study of Rapp, IEEE (Rapp also) or other types of models can be done during the SI
  There is no agreement in RAN4 about PA models covering memory effects but in some cases measurements are needed to verify the behavior especially when there are tight emission requirements due to higher order IMDs

## Slide 3: WF on UE PA model for RAN4
For FR2 Rapp or AM/PM (simulated/measured curves) or even measurements have been used in RAN4, and they can be can be used for 52.6-71GHz range MPR/A-MPR evaluation
Other models are not precluded, including assessment on impact of memory effect
When presenting results companies should clarify which model is used, how it has been calibrated and discuss potential limitations
In absence of fixed requirement in 52.6-71GHz range, FR2 calibration waveform and MPR can be used as the basis for comparison. This can also be used to compare technology capability.

## Slide 4: WF on other UE aspects for MPR/A-MPR
Beyond the intrinsic PA performance and its modeling, other aspects should be considered:
  IQ and DC impairments and their impact to IBE and EVM, and via intermodulation of those with the wanted signal, OOB emissions
  Assumption on number of antennas and beam forming errors (phase shift errors and/or PA to PA pulling) have an influence on how to calibrate the PA output power and margin needed for a given EIRP and emission requirement
Companies are encouraged to provide their view on feasible DC and IQ impairments in the 52.6 to 71 GHz range and report these assumption when providing results.
Companies are encouraged to provide their view on practical number of antennas and beamforming errors in the 52.6 to 71 GHz range and report these assumption when providing results.

## Slide 5: References
[1] R4-2009757 On phase noise and PA models in 52.6 – 71 GHz, Intel Corporation
[2] R4-2009921 Key technology considerations relating to 52-71GHz specification work, Ericsson
[3] R4-2009946 Initial considerations on 60 GHz PN and PA models, Apple Inc.
[4] R4-2010292 Discussion on RF impairments for B52.6G, vivo
[5] R4-2011494 On PN model for 52.6~71GHz, Huawei, HiSilicon