## Slide 1: WF on NR-U RRM Requirements (Part 2) (All agreements in RAN4#96e in email thread #207)
MediaTek inc.
3GPP TSG-RAN WG4 Meeting #96e R4-2012091
Electronic Meeting, 17 August – 28 August, 2020
Agenda Items: 7.1.5.2, 7.1.5.7, 7.1.5.8, 7.1.5.9, 7.1.5.12

## Slide 2
Agreements from the 1st round
Agreement from GTW session
Agreements from the 2nd round

## Slide 3: Topic #1: Cell re-selection (AI 7.1.5.2)
Max number of unavailable SMTC occasions during measurement before UE detects the cell again
  For a cell that is already identified, after N unsuccessful measurement attempts due to exceeding the max number of unavailable SMTC occasions, UE needs to detect the cell again.
    N = 2
Definition of unavailable SMTC/SSB
  Discussion moved to Email thread [208]

## Slide 4: Topic #2: Active BWP switching (AI 7.1.5.7)
The ending point of UL BWP switching delay upon detection of consistent UL LBT failure
  (Moderator: subject to the outcome of GTW)
  Include delay uncertainty due to RACH transmission in the active BWP switch delay under LBT failure/recovery procedure

## Slide 5: Topic #3: RLM (AI 7.1.5.8)
Indication period
  FFS: whether to extend the indication period of out-of-sync and in-sync due to the not available SSB occasions
UE assumption on transmit power
  Define the RLM requirements, taking into account that the UE can assume that NZP CSI-RS or SS/PBCH block (for L1-RSRP, RLM, BFD, CBD and RRM) is transmitted with the same transmit power across different occasions during the measurement period, as in Rel-15

## Slide 6: Topic #3: RLM (AI 7.1.5.8)
Definition of SNREST
  (Moderator: subject to the outcome of GTW)
  Purpose of this SNR
    Option 1: Determine which requirement (fix or dynamic) should be followed by UE
    Option 2: Determine whether the SSB is transmitted by gNB
  SNREST is the side condition Es/Iot
  How to deal with multiple samples (with and without LBT failure)
    Option 1: Last available SSB before the evaluation period starts
    Option 2: Current SSB SINR estimate
    Option 3: Averaged SINR over the evaluation period at UE side
    Option 4: The smallest SINR value over the evaluation period
SINR (Es/Iot) threshold for whether UE is able to distinguish the unavailable RLM-RS (X dB)
  X = -7dB

## Slide 7: Topic #3: RLM (AI 7.1.5.8)
OOS evaluation period when Es/Iot ≤ X dB
  Extend the evaluation period using a fixed factor L
    L = 14 for max(TSSB, TDRX) ≤ 40 where TDRX=0 for non-DRX,
    L = 10 for 40 <Max(TSSB, TDRX)≤320
    L = 6 for TDRX >320.
OOS evaluation period when Es/Iot > X dB
  Moderator: subject to the outcome of GTW
  Option 1: depends on Lout (Lout ≤ Lout,max), where Lout is the number of SSBs not available at the UE during TEvaluate_out_SSB (ZTE, Nokia, Ericsson)
    Lout,max = 14 for max(TSSB, TDRX) ≤ 40 where TDRX=0 for non-DRX,
    Lout,max = 10 for 40 <Max(TSSB, TDRX)≤320
    Lout,max = 6 for TDRX >320.
  Option 2: Extend the evaluation period using a fixed factor L (MTK, QC, Apple, Intel, Huawei, [Nokia])
    L = 7 for max(TSSB, TDRX) ≤ 40,
    L = 5 for 40 <Max(TSSB, TDRX)≤320
    L = 3 for TDRX >320.
  Do not define requirements for the case of OOS evaluation period when Es/Iot > X dB in case no decision on Option 1 and 2 is made

## Slide 8: Topic #3: RLM (AI 7.1.5.8)
UE behaviour upon exceeding Lout,max of OOS evaluation period when Es/Iot > X dB
  The same as if the radio link quality for this RLM-RS resource were below Qout
Whether to define CSI-RS based RLM requirements in Rel-16
  Do not define CSI-RS based RLM requirements in Rel-16

## Slide 9: Topic #4: Beam management (7.1.5.9)
Evaluation period for SSB based BFD
  The Evaluation period for SSB based BFD follows the same approach as that in the OOS evaluation period for SSB based RLM
Measurement period for L1-RSRP
  RAN4 should wait for LS response from RAN1 on the UE behavior when UE cannot transmit HARQ-ACK for MAC CE deactivation for semi-persistent CSI reporting. RAN4 should continue the discussion in the RRM maintenance in case RAN4 does not receive the LS response from RAN1 during RAN4#96-e

## Slide 10: Topic #5: Timing (AI 7.1.5.12)
UE behaviour when SCell is unavailable
  Clarify in the specification that the UE is not precluded to go back to use PSCell or PCell as reference timing cell, in case the reference timing cell, which is a SCell, is deactivated or becomes unavailable for 160 ms
Definition of an available reference cell
  FFS: whether a reference cell is available at the UE provided at least one SSB is available at the UE during the last 160 ms; otherwise it is unavailable at the UE