## Slide 1: WF on MR-DC RRM requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #96e
E-meeting, August 17th – 28th, 2020
R4-2012111
Document for: Approval

## Slide 2: Background
During the RAN4#96e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Agreements made during the meeting are captured in this WF.
Summary of the discussions during RAN4#96e meeting (round 1 and round 2) is captured in R4-2012212.
  Ageements based on the discussions are captured in same document.
  Additional ageements may be captured in chairman meeting minutes.

## Slide 3: Agreements Topic #1: NR measurements for EMR (38.133)
Issue 1-2-2-1: Number of non-overlapping EMR carriers:
  The number of non-overlapping inter-frequency EMR carriers is ≤7
Issue 1-2-2-2: Number of non-overlapping EMR carrier when the total number limit is exceeded:
  RAN4 will not define requirements for number of non-overlapping EMR carrier when the total number limit is exceeded
Issue 1-2-3-1: NR inter-frequency beam-level measurement capability:
  RAN4 agree following related to NR inter-frequency beam-level measurement capability:
    FR1: 7 SSBs with different SSB index and/or PCI per inter-frequency layer
    FR2: 10 SSBs with different SSB index and/or PCI per inter-frequency layer

## Slide 4: Agreements Topic #1: NR measurements for EMR (38.133)
Issue 1-2-5-1: For overlapping EMR carriers:
  For overlapping EMR carriers, the UE measurement accuracy requirements for carriers configured for EMR:
    RAN4 to define relaxed NR measurement requirements for overlapping carrier compared to existing NR inter-frequency requirements in terms of SNR and accuracy
    LTE inter-RAT measurement requirements for overlapping carrier follows existing LTE inter-frequency requirements for CA Idle mode measurements for overlapping carrier

## Slide 5: Agreements Topic #2: NR measurements for EMR (36.133)
Sub-topic#2-1: s-NonIntraSearch thresholds and EMR carriers:
  s-NonIntraSearch thresholds and NR inter-RAT EMR carriers follow agreements for NR measurements for EMR.
Sub-topic#2-2: Capturing the UE capability:
  Capture the UE capability according to the proposed applicability text in 36.133 (R4-2010569) with necessary name correction.
Sub-topic#2-3: Number of NR Inter-RAT EMR carriers to measure:
  UE should be able to measure up to 8 overlapping and non-overlapping inter-RAT NR EMR carriers in total:
    Overlapping NR inter-RAT carriers: ≤8
    Non-overlapping NR inter-RAT carriers: ≤2

## Slide 6: Agreements Topic #2: NR measurements for EMR (36.133)
Sub-topic#2-4: Measurement requirements for non-overlapping NR inter-RAT EMR carrier:
  Measurement requirements for non-overlapping NR inter-RAT carriers are defined same as overlapping NR inter-RAT carriers.
Sub-topic#2-5: Measurement accuracy requirements for NR Inter-RAT EMR carrier:
  For Measurement accuracy requirements for NR Inter-RAT EMR carrier same principles as in Issue 1-2-5-2 will be applied.
Sub-topic#2-6: Beam level measurement capability:
  For NR inter-RAT EMR, the UE beam-level measurement capability requirements for EMR is the same as the number of beams in the existing Rel-15 inter-frequency requirements for RRC_CONNECTED state:
    FR1: 7 SSBs with different SSB index and/or PCI per inter-frequency layer
    FR2: 10 SSBs with different SSB index and/or PCI per inter-frequency layer

## Slide 7: WF on Topic #1: s-NonIntraSearch thresholds and EMR carriers (38.133)
Tentative agreement:
  Option 1:
    UE applies EMR carrier measurements disregards whether the signal exceeds the configured s-NonIntraSearch thresholds
    UE will follow conventional measurement interval for both overlapping and non-overlapping EMR carrier measurements when s-NonIntraSearch thresholds are configured
      Note: conventional measurement interval is the measurement period used for cell reselection purpose
  Option 2:
    No requirements defined for the case s-NonIntraSearch thresholds are configured
  Other options are under email discussion.

## Slide 8: WF on Sub-topic#1-3 beam-level measurement requirements (38.133)
Issue 1-2-3-3: beam-level measurement requirements:
Tentative agreement:
  RAN4 agree to allow UE additional time period in measurement requirement for UE who supports the beam level EMR reporting:
  TtimeIndex,NR_Inter = [X]* Tmeasure,NR_Inter,
    where X is TBD
    X is under email discussion and may depend search threshold discussion.

## Slide 9: WF on Sub-topic#1-6 Conditions for ‘actively measured’ (38.133)
Conditions for ‘actively measured’
  Option 1: EMR carriers are actively measured for EMR while T331 is running
  Option 2: RAN4 to discuss how to account ‘actively measure’ conditions for mobility in definition of overlapping and non-overlapping carriers after measurement requirements for EMR are settled
Tentative agreement:
  EMR carriers are actively measured for EMR while T331 is running

## Slide 10: WF on Sub-topic#1-7 Other (38.133)
Definitions of overlapping and non-overlapping EMR carriers
  Option 1: Follow the agreed definitions of overlapping and non-overlapping EMR carriers
  Option 2: Based on search thresholds and carrier priority
  Option 3: While T331 is running:
    overlapping carrier: a carrier configured for EMR and mobility.
    non-overlapping carrier: a carrier configured for EMR only.
  Option 5: No need for differentiation (added by Moderator)
Tentative agreement:
  If no agreement regarding topic #1 regarding search threshold discussion, at least option 2 is not needed.

## Slide 11: Sub-topic#2-3 Number of NR Inter-RAT EMR carriers to measure (36.133)
UE shall be able to measure at least 1 NR inter-RAT carrier for EMR per FR.
  Option 1: yes
  Option 2: no
Tentative agreement:
  Option 2.

## Slide 12: Sub-topic#2-5 Measurement accuracy requirements for NR Inter-RAT EMR carrier (36.133)
Agreement in sub-topic 2-5 was covering non-overlapping EMR carriers.
RAN4 also need to define measurement accuracy for overlapping NR inter-RAT EMR carriers.
  Option 1: follow the agreement for overlapping EMR carriers in sub-topic 1-5 Issue 1-2-5-1
  Option 2: other
Tentative agreement:
  Option 1.

## Slide 13: Sub-topic#2-7 Beam level measurement requirements (36.133)
Conclusion from first round was not captured as agreement.
Agree on the conclusion from 1st round and follow agreements in 1-2-3-3:
  Option 1: yes
  Option 2: no
Tentative agreement:
  Option 1.