## Slide 1: Way forward on FR2 inter-band CA RRM requirements
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #96-e
Online, 17th– 28th August, 2020
Agenda: 7.13.1.5
R4-2012161

## Slide 2
No CBM-specific RRM requirements will be specified in Rel-16.
Agreements on FR2 inter-band CA requirements with CBM

## Slide 3: Agreement on FR2 inter-band CA requirements with IBM
Assumption for IBM UE in Rel-16:
    Assumption of deployment and band pair for IBM UE should follow the RF session conclusions, and no restriction on deployment and band pair shall be assumed in RRM requirement right now unless RF session concluded on those restrictions.
Beam management requirements for IBM UE:
    To follow the conclusions in NR eMIMO on how to perform BFD/CBD measurements.
  Tentative agreement FFS:
  SCell activation delay requirements for IBM UE
      Not necessary to specify the requirements for ‘SCell being activated belongs to FR2 and there is an active serving cell on that FR2 band and the PCell or PSCell is in FR2 and the PCell or PSCell and SCell being activated are in a band pair with independent beam management’

## Slide 4: Agreement on FR2 inter-band CA requirements with IBM
Necessity of clarification on “there is no scheduling restriction if UE uses independent beam”
    The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is no scheduling restriction if UE uses independent beam.
Scheduling restrictions requirements for IBM UE in case 1~3
    Scheduling availability requirement shall not apply for the Case 1 and Case 2
      Case 1 and Case 2 are network configuration errors.
      How to handle those cases is up to UE implementation without any specified requirement.
    There is no scheduling restriction allowed for IBM capable UE when network configures mixed numerology between SSB on one FR2 band and data on the other FR2 band and UE is configured for IBM operation for the band pair.
Measurement restrictions requirements for IBM UE in cases 1 and 2
    Measurement requirement shall not apply for the Case 1
      Case 1 is network configuration error.
      How to handle this case is up to UE implementation without any specified requirement.
    There is no measurement restriction allowed for IBM UE when network configures mixed numerology between SSB on one FR2 band and CSI-RS on the other FR2 band and UE is configured for IBM operation for the band pair.

## Slide 5: For Informations
Cases 1~3 for the scheduling restrictions requirements
    Case 1: network configures simultaneous UL/DL between between two FR2 bands if the UE does not have the capability of supporting simultaneousRxTxInterBandCA.
    Case 2: network configures mixed numerology on two FR2 CCs if the UE does not have the capability of supporting simultaneous reception with two different numerologies between FR2 CCs in DL.
    Case 3: network configures mixed numerology between SSB and data on two FR2 bands if the UE does not have the capability of simultaneousRxDataSSB-DiffNumerology in FR2.
    Cases 1~2 for the measurement restrictions requirements
    Case 1: network configures mixed numerology on two FR2 CCs if the UE does not have the capability of supporting simultaneous reception of with different numerologies between FR2 CCs in DL.
    Case 2: network configures mixed numerology between SSB and CSI-RS on two FR2 bands if the UE does not have the capability of simultaneousRxDataSSB-DiffNumerology in FR2.