## Slide 1: WF on NR Mobility Enhancements RRM
Intel Corporation
3GPP TSG-RAN WG4 Meeting #96-e R4-2012270
Electronic Meeting, 17th – 28th August 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2012209 Email discussion summary for [96e][209] NR_Mob_enh_RRM
Agreements in the last RAN4#95-e meeting can be found in:
  R4-2009020 Email discussion summary for [95e][208] NR_Mob_enh_RRM
  R4-2008585 WF on MR Mobility Enhancements

## Slide 3: Agreement for core requirement maintenance
Issue 1-1: demodulation performance degradation for async intra-frequency DAPS handover and async intra-band inter-frequency DAPS handover
  How to capture the performance degradation for asynchronous cases needs to be further studied

## Slide 4: Agreement for core requirement maintenance (Cont.)
Issue 1-2: requirement applicability
Agreement: update existing applicability to:
  requirements only apply if
    the UE indicates ‘no-gap’ via intraFreq-needForGap for intra-frequency measurement of source cell and intra-frequency measurement of target cell, or
    the SSB of source cell is completely contained in the active DL BWP of the source cell, and the SSB of target cell is completely contained in the active DL BWP of the target cell, or
    the initial DL and UL BWP of source cell is confined within the active DL and UL BWP of the source cell respectively, and the initial DL and UL BWP of target cell is confined within the active DL and UL BWP of the target cell respectively.

## Slide 5
Issue 1-3: new UE capability regarding uplink Tx switching
No agreement in RAN4#96e to introduce the UE capability for UE which doesn’t support simultaneous UL transmission to indicated whether the uplink Tx switching between source cell(s) and target cell(s) for inter-frequency DAPS handover is supported and what switching period is required for UE switching between source and target uplink carriers.
This new UE capability can be considered in future release.
Agreement for core requirement maintenance (Cont.)

## Slide 6: Agreement for test case list
CR owners shall provide CRs in RAN4#97e, following section number below
Test case number | Test purpose | Section number | Responsible company
1 | Intra-frequency sync DAPS handover test in SA for FR1 | A.6.3.1.7 | Qualcomm
2 | Intra-frequency async DAPS handover test in SA for FR1 | A.6.3.1.8 | Qualcomm
3 | Intra-band Inter-frequency sync DAPS handover test in SA for FR1 | A.6.3.1.9 | Intel
4 | Intra-band Inter-frequency async DAPS handover test in SA for FR1 | A.6.3.1.10 | Intel
5 | Inter-band Inter-frequency sync DAPS handover test in SA for FR1 | A.6.3.1.11 | Huawei
6 | Inter-band Inter-frequency async DAPS handover test in SA for FR1 | A.6.3.1.12 | Huawei
7 | Conditional intrafrequency handover test in SA for FR1 | A.6.3.1.13 | Ericsson
8 | Conditional interfrequency handover test in SA for FR1 | A.6.3.1.14 | Ericsson
9 | Inter-frequency sync DAPS handover test in SA for FR1-FR2 | A.6.3.1.15 | Huawei
10 | Inter-frequency async DAPS handover test in SA for FR1-FR2 | A.6.3.1.16 | Huawei
11 | Conditional intrafrequency handover test in SA for FR2 | A.6.3.1.17 | Ericsson
12 | Conditional interfrequency handover test in SA for FR2 | A.6.3.1.18 | Ericsson
RAN4 confirms no need to introduce test case for conditional PSCell change

## Slide 7: Agreement for test applicability
RAN4 agreed to introduce the following test applicability
  The UE capable of asynchronous DAPS handover on any band or band combination needs to be tested only in asynchronous scenario.
  The UE not capable of asynchronous DAPS handover on any band or band combination but capable of synchronous DAPS handover on some band or band combination needs to be tested only in synchronous scenario.
It is FFS whether the above test applicability needs to be split to cover intra-frequency, intra-band inter-frequency and inter-band inter-frequency respectively.

## Slide 8: Agreement for test procedure for DAPS HO
  Issue 2-3-1: DAPS HO test – whether to test a known or unknown target cell
  Agreement: test known target cell
  Issue 2-3-2: DAPS HO test – how to verify source cell release delay
  Agreement: add T5 to verify delay requirement. (TE sends RRC to release source cell in T4. Duration of T4 equals to delay requirement. The source cell reserves CSI reporting in T5. UE shall not report any CSI to source cell in T5)
  Note: above is high level agreement, which can be used as baseline when developing DAPS HO tests.
  Issue 2-3-3: whether async TDD DAPS HO test can be removed
    Agreement: it is agreed to remove TDD DAPS HO tests.