## Slide 1: WF on NR-U BS Tx and Rx remaining requirements for NR-U
ZTE, …
R4-2012607
3GPP TSG-RAN WG4 #96e
17th Aug - 28th Aug. 2020

## Slide 2: Background
  In RAN4#96e, lots of open issues are identified for NR-U BS requirements which needs further discussion, open issues are listed as following:
  1) How to reflect NR-U BS to support AAS BS type;
  2) IBB/OOBB requirements for NR-U BS;
  3) ΔfOBUE and ΔfOOBB for NR-U BS type 1-C and 1-H;
  4) Frequency offset of interferer signal for RX ACS and IMD requirements;
  5) LO leakage exception for NR-U BS Tx
  Note : 1) and 4) has been resolved in the GTW meeting with following agreement:
  Proposal 1: Prated,C,AC used in WF [4] and CR [3] should be updated as Prated,x;
  Proposal 1: to use the following frequency offset for ACS interfering signal in Table 7.4.1.2-2a in R4-2010960;
  Proposal 4: to use the following frequency offset for RX IMD interfering signal in Table 7.7.2-2a in R4-2010960;
  Reference:
  [1]R4-2010738, CR to TS 38.104: Introduction of NR-U into BS core specification,Nokia
  [2]R4-2010743, Discussion on BS core specification drafting ,Nokia
  [3]R4-2010959,NR-U BS Tx requirements, ZTE Corporation
  [4]R4-2010960, NR-U BS Rx ACS, IBB, OOBB, IMD requirements, ZTE Corporation
  [5]R4-2010495

## Slide 3: WF for ΔfOBUE and ΔfOOBB
  For NR-U BS type 1-C for n46:
  For NR-U BS type 1-H for n46:
NR-BS Type 1-C | ΔfOBUE | ΔfOOBB | Supporting companies
Option 1 | 10MHz | 20MHz | ZTE, Nokia, Ericsson
Option 2 | 40MHz | 60MHz | Huawei
Recommend Agreement: option 1 |  |  | 
 | ΔfOBUE | ΔfOOBB | Supporting companies
Option 1 | 10MHz | 20MHz | Nokia
Option 2 | 40MHz | 60MHz | ZTE, Huawei
Recommend Agreement: option 2 |  |  | 

## Slide 4: IBB and OOBB requirements
  For NR-U BS type 1-C and 1-H for n46:
  Note: for background for eLAA BS RX requirement could be found in the following R4-167192, R4-166293.
Operating Band | Centre Frequency of Interfering Signal [MHz] |  |  | Interfering Signal mean power (dBm) | Wanted Signal mean power (dBm) | Interfering signal centre frequency minimum frequency offset to the lower/higher Base Station RF Bandwidth edge or sub-block edge inside a sub-block gap (MHz) | Type of Interfering Signal
n46 | (FUL_low -ΔfOOBB) | to | (FUL_high +ΔfOOBB) | Medium Range BS: -38 Local Area BS: -35 | PREFSENS +6dB (Note 1) | ±30 | 20 MHz DFT-s-OFDM NR signal15 kHz SCS, 100 RBs
 | (FUL_low -500) (FUL_high +ΔfOOBB) | to to | (FUL_low -ΔfOOBB) (FUL_high +500) | -35 | PREFSENS +6dB (Note 1) | ¾ | CW carrier
 | 1 (FUL_high +500) | to to | (FUL_low -500) 12750 | -15 | PREFSENS +6dB (Note 1) | ¾ | CW carrier
Note 1: PREFSENS depends on the channel bandwidth as specified in Table 7.2.2-2a and 7.2.2-3a. |  |  |  |  |  |  | 

## Slide 5: LO leakage for NR-U punctured channels
  An exception to the spectrum emission requirements for the non-transmitted 20 MHz channels allows a single 2 MHz bandwidth to extend to Prated,x-28dB , or -20 dBm, whichever is the greatest.
  Option 1: to define LO leakage exception
  Nokia, Huawei
  Option 2: not to define LO leakage exception
  ZTE
  Note :To define LO leakage exception will degrade the UE performance as there are no LO indication to UE to do the calibration which is different from UE LO leakage where RAN1/2 signaling is supported.