## Slide 1: WF on band combinations for V2X con-current operation
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, 2-13 Nov., 2020
Agenda item: 10.23
Document for: Approval
R4-2016869
CATT, …

## Slide 2: Background
In RAN#88e meeting, the WI, band combinations for con-current operation of NR/LTE Uu bands/band combinations and one NR/LTE V2X PC5 band, was approved.
In the 1st round, several general issues are discussed as follows:
  UE RF architecture
  Shared antenna or separate antenna
  Filter performance for band n47/47
  ΔTIB,c and ΔRIB,c

## Slide 3: UE RF architecture
  The candidate options are listed below:
  Option 1: Capture the RF architecture with separate antennas proposed in R4-2015561 in TR 37.875.
  Option 2: Specify RF architecture based on consensus and capture it in TR 37.875.
  Option 3: No need to capture RF architecture in TR 37.875.
  Recommended WF :
  Study the number of Tx and Rx for both Uu band and SL band and decide RF architecture based on consensus.
  For both Uu band and SL band, 1T2R is considered as a baseline. So Option 1 is agreed.
  The selection of an RF architecture does not preclude the introduction of other RF architectures in the future.

## Slide 4: Shared antenna or separate antenna
  The candidate options are listed below:
  Option 1: Prioritize to use separate antenna architecture like LTE V2X band combinations. The shared antenna architecture can be used for the specific band combination where the bands are closely located.
  Option 2: Decide antenna architecture based on the specific band combination.
  Recommended WF :
  Companies to share views whether to converge to Option 2.
  Generally, Option 2 is agreed. Separate antenna architecture is considered as a baseline when V2X UE supports con-current operation between ITS band and Uu band.

## Slide 5: Filter performance
  The candidate options are listed below:
  Option 1: Capture the filter performance for band 47/n47 proposed in R4-2015561 in TR 37.875.
  Option 2: No need to study the filter performance for band 47/n47.
  Option 3: Study the filter performance for band 47/n47 and capture it based on consensus in TR 37.875.
  Recommended WF:
  Further discuss the filter performance for band 47/n47 based on technical analysis and companies’ input.
  Option 1 is agreed. The filter performance is captured in TR with square brackets. Whether to capture the filter performance for other band is FFS.

## Slide 6: ΔTIB,c and ΔRIB,c
  The candidate options are listed below:
  Option 1: Adopt ΔTIB,c and ΔRIB,c on Uu band instead of SL band.
  Option 2: Adopt shared pain approach for Uu band and SL band.
  Option 3: Adopt either option 1 or option 2 based on specific band combination
  Recommended WF:
  Decide after RF architecture is clear.
  Decide ΔTIB,c and ΔRIB,c based on specific band combination. Whether to adopt fixed rule (e.g. shared pain approach) is FFS.

## Slide 7: Reference
[1] R4-2014421, Discussion on Rel-17 band combinations for Uu and V2X con-current operation, CATT, RAN4#97e
[2] R4-2015561, TP for TR 37.875: adding some UE RF study for NR V2X band combinations, Huawei, HiSilicon, RAN4#97e
[3] R4-2014422, TP on V2X_n40A-n47A coexistence study, CATT, RAN4#97e
[4] R4-2014423, CR for TS 38.101-1, Introduce new band combination of V2X_n39A-n47A and V2X_n40A-n47A, CATT, RAN4#97e
[5] R4-2014424, CR for TS 38.101-3, Introduce new band combination of V2X_39A-n47A, V2X_n39A-47A,V2X_40A-n47A and V2X_n40A-47A, CATT, RAN4#97e