## Slide 1: WF on Coexistence Simulations results for 6.425-7.125 GHz and 10.0-10.5 GHz
Huawei, HiSilicon, CATT, Nokia, Ericsson, ZTE
3GPP TSG-RAN WG4 Meeting # 97-e R4-2016904
Electronic Meeting, 2-13 Nov., 2020

## Slide 2: Background on DL simulation results
 | ACIR (dB) |  |  |  |  | 
Company | 6.425-7.125GHz |  |  | 10.0-10.5GHz |  | 
 | Urban macro uncoord. | Indoor | Dense Urban | Urban Macro uncoord. | Indoor | Dense Urban
CATT | 29.5 |  |  | 28 |  | 
Nokia | 32.7 | 31.7 | 23.7 | 30.7 | 32.2 | 20.7
Huawei | 30.7 |  |  | 29.7 |  | 
Ericsson | 30 |  |  | 29 |  | 
ZTE | 31.7 |  |  | 29.7 |  | 
Qualcomm | 30.9 |  |  | 30.5 |  | 
Average | 30.9 |  |  | 29.6 |  | 
Average after removing highest and lowest values | 30.9 |  |  | 29.5 |  | 
Suggested target value | 30.9 |  |  | 29.5 |  | 
Tentative Agreements in 1st round summary: Targeted ACIR value in DL (indoor excluded): 30.9 for 6.425-7.125 GHz and 29.6 for 10.0-10.5 GHz.

## Slide 3: Background on UL simulation results
 | ACIR (dB) |  |  |  |  |  | 
Company | 6.425-7.125GHz |  |  | 10.0-10.5GHz |  |  | 
 | Urban macro uncoord. | Indoor | Dense Urban | Urban Macro uncoord. | ISD | Indoor | Dense Urban
CATT | 26 |  |  | 26.2 | ? |  | 
Nokia | UE ACLR: 27 BS ACS: 45 ACIR=26.9 | UE ACLR:30 BS ACS: 45 | UE ACLR: 21 BS ACS: 45 | UE ACLR: 26 BS ACS: 45 ACIR=25.9 | ? | UE ACLR: 29.5 BS ACS: 45 | Not conclusive
Huawei | 27.9 |  |  | 25.9 | ? |  | 
Ericsson | 27 |  |  | 23 | 400 |  | 
ZTE | 27.9 |  |  | 24.9 | ? |  | 
Qualcomm | 22 |  |  | 22 / 21.5(*) | 400 |  | 
Average value | 26.3 |  |  | 24.6 |  |  | 
Average after removing highest and lowest values | 27 |  |  | 24.9 |  |  | 
Suggested target value | 26.5 |  |  | 24.6 |  |  | 
Note (*): 22 with 23dBm and 21.5 with 20dBm |  |  |  |  |  |  | 
Tentative Agreements in 1st round summary:
Targeted ACIR value in UL (indoor excluded): 26.5 for 6.425-7.125 GHz and 24.6 for 10.0-10.5 GHz.
In the 2nd round, companies should align on:
If those ACIR values should be weighted to better consider 3 UEs in UL assumption.
If the answer is yes, how to weight those values.
ACIR UL values shall be concluded during the 2nd round, this to be able to answer ITU-R LS before next WP5D meeting next year.

## Slide 4: WF on targeted ACIR
DL
  Targeted ACIR value in DL (indoor excluded): 30.9 dB for 6.425-7.125 GHz and 29.6 dB for 10.0-10.5 GHz.
UL
  Targeted ACIR value in UL (indoor excluded): (26.5-X) dB for 6.425-7.125 GHz and (24.6-X) dB for 10.0-10.5 GHz, where X is to consider 3UEs in UL assumption may lower the targeted ACIR value.
    X= ~0.5 dB

## Slide 5: Work plan for indoor simulation
If RAN accepts the SI extension for 1 meeting, following work plan has been proposed:
  Agree on antenna parameters and other simulation assumptions if any for indoor before Dec. 15th
  Alignment on UE Tx power and SINR cdf for January 10th 2021.
  Run simulations and submit results to next RAN4#98e