## Slide 1: WF on 4Rx requirement for CA_n77(3A) and CA_77(4A)
SoftBank Corp., Skyworks
3GPP TSG-RAN WG4 #97-e
2 – 13 November 2020
Electronic meeting
R4-2016912

## Slide 2: Background
For CA_n77(3A), UE architecture needs to be studied considering the n77 spectrum allocation in Japan.
For CA_n77(3A/4A) for C-band in the US, the combination has to fit in 280MHz spectrum.

## Slide 3: UE architecture assumption
CA_n77(3A)
  3LO may be required considering the frequency separation (up to 600MHz) in Japan.
CA_n77(4A)
  FFS

## Slide 4: WF for the support of 4x4 MIMO
Continue the discussion in the next meeting.
  Option 1: 4x4 DL MIMO is mandatory support for n77(3A) DL CA and all related higher order inter-band DL CA combinations (SoftBank, Huawei):
    No signaling and specification update needed
    Limited support for lower end phones but also potential limitation on how many additional bands are supported in inter-band DL CA
  Option 3: 4x4 DL MIMO is optional support for n77(3A) DL CA and all related higher order inter-band DL CA combinations (QC, OPPO, LGE, Apple, Skyworks):
    Signaling and specification update needed
    Larger support for n77(3A)combination and/or additional bands in related inter-band DL CA

## Slide 5: WF for release independent definition
CA_n77(3A) is introduced with release independence from Release 17.
  Higher order inter-band CA combinations including CA_n77(3A) are also introduced with release independence from Release 17.
CA_n77(4A) is FFS.