## Slide 1: WF on NR support for HST in FR2
Samsung, …
3GPP TSG-RAN WG4#97-e Meeting R4-2016640
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: Way Forward – Deployment Scenario: General
FR2 HST Deployment Scenario:
  RAN4 at least consider the following deployment scenario:
    Ds and Dmin: Take the following 5 scenarios as basic assumption.
      Dmin for [5m, 20, 30 and 50 meters] if found to be necessary
    DRRH_height: 15m as basic assumption;
      [10,20m] if found to be necessary
    DUE_height: 5m.
  Tunnel Deployment Scenario
    RAN4 further study tunnel deployment scenario for FR2 HST.
  Subcarrier Spacing
    Option-1: SCS = 120kHz
    Option-2: Consider both SCS = 120kHz and 60kHz.
Scenario | Ds (meter) | Dmin (meter)
1 | 800 | 10
2 | 650 | 10
3 | 500 | 10
4 | 300 | 50
5 | 200 | 30

## Slide 3: Way Forward – Deployment Scenario: SFN
Unidirectional SFN and Bidirectional SFN
  RAN4 consider unidirectional SFN for FR2 HST, i.e., one panel per RRH pointed to the same direction for all RRHs.
  RAN4 consider bidirectional SFN with
    one panel per RRH, i.e., signals to opposite directions along tracks
    two panels per RRH.
  SFN needs to be further clarified:
    SFN Interpretation-1: All RRHs under one BBU transmit the same signal.
      Selected RRH(s) for TX, depending on DPS Tx mode is used or not.
    SFN Interpretation-2: All RRHs under one BBU in the same cell ID, but for different TCI.
    Other interpretation is not precluded.

## Slide 4: Way Forward – Deployment Scn.: RRH Parameters
Number of RRH sites per BBU:
  [1 to 4]RRHs sites per BBU
    Other values are not precluded;
    Depending on companies’ further feasibility study on SFN deployment scenario.
Number of Analog Beams per panel in RRH:
  [1,2,4] analog beam(s) per panel in RRH
    Other values are not precluded;
    Depending on companies’ further feasibility study on link-budget and mobility
  SSB index to Beam Mapping:
  FFS the impact of following options for SSB index to Beam mapping:
    Option 1:
      All RRHs (connected to one BBU with fiber) share the same cell ID
      All RRHs under the same cell use the same set of SSB indexes, e.g., all RRHs use SSB-0 to SSB-3.
    Option 2:
      All RRHs (connected to one BBU with fiber) share the same cell ID
      RRHs under the same cell use the different sets of SSB indexes, e.g., RRH-1 uses SSB-0 to SSB-3, RRH-2 uses SSB-4 to SSB-7.
  RRH antenna array orientation:
  FFS the impact of following options for RRH antenna array orientation:
    Option 1: RRH panel boresight pointed to the railway in the middle point between 2 RRHs
    Option 2: RRH panel boresight pointed to the railway at the distance of Ds (projection of the neighboring RRH on the railway)
    Other option is not precluded.

## Slide 5: Way Forward – Deployment Scn.: CPE Parameters
Number of panels per CPE:
  FFS the number of panel(s) per CPE:
    To be combined with the analysis on uni-/bi-directional SFN.
  The number for TX panel(s) and RX panel(s) could be discussed separately.
Placement of CPE panel(s):
  FFS the placement of CPE panels, i.e., the bore-sight direction(s) of CPE panel(s)
Number of CPE devices:
  FFS the impact of the number of CPE per train/carriage on RAN4 requirement.

## Slide 6: Way Forward – Evaluation Parameters (1/2)
RRH antenna array parameters for evaluation:
  RAN4 perform FR2 HST feasibility study based on following RRH antenna array parameters for evaluation:
    RAN1 assumption: 2 ports: [Mg, Ng, M, N, P]=[1, 1, 4, 8, 2]
    2 ports: [Mg, Ng, M, N, P]=[1, 1, 8, 8, 2]
    Other options are not precluded.
RRH antenna element parameters for evaluation:
  RAN4 use the following RAN1 assumption for BS evaluation as baseline:
  Other assumptions are not precluded.
Radiation power pattern of a single antenna element for TRP | Vertical cut of the radiation power pattern (dB) | 
 | Horizontal cut of the radiation power pattern (dB) | 
 | 3D radiation power pattern (dB) | 
 | Maximum directional gain of an antenna element GE,max | [8] dBi

## Slide 7: Way Forward – Evaluation Parameters (2/2)
UE antenna array parameters for evaluation:
  RAN4 perform FR2 HST feasibility study based on following UE antenna array parameters for evaluation:
    RAN1 assumption: 2 ports: [Mg, Ng, M, N, P]=[1, 1, 2, 4, 2]
    PC4 assumption: 2 ports: [Mg, Ng, M, N, P]=[1, 1, 4, 4, 2]
    Other options are not precluded.
UE antenna element parameters for evaluation:
  RAN4 use the following RAN1 assumption for UE evaluation as baseline:
Parameter | Values
Antenna element radiation pattern in θ’’ dim (dB) | 
Antenna element radiation pattern in ϕ’’ dim (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 5dBi

## Slide 8: Way Forward – Channel Modeling
Pathloss model used for link budget evaluation:
  RAN4 further study the pathloss model to be used for link budget evaluation:
    Option-1: TR38.901 RMa LoS
    Option-2: free space model
    Option-3: TR38.901 UMa LoS
Channel modelling for performance requirements:
  RAN4 further study the channel modeling for performance requirement:
    Option 1: single-tap per RRH channel model in UL direction and both single- and multi-tap models in DL direction.
    Other options are not precluded, which could depends on deployment scenario discussion.

## Slide 9: Way Forward – FR2 Feasibility Evaluation
RAN4 perform feasibility study on FR2 HST scenario, by at least considering:
  The feasibility of a deployment based the beam dwelling time and measurement period framework.
    How many beams/SSBs per RRH can be deployed (given other deployment parameters such as Dmin, Ds, speed etc) while maintain mobility performance with FR2 BM mechanism?
    How much beam refinement is needed to achieve coverage and mobility?
      How much beam overlapping area is needed (given other deployment parameters such as Dmin, Ds, speed etc) to ensure beam refinement procedure can be executed successfully?
  Study throughput performance and mobility performance.
    More number of analog beams and sharper beam may provide better link budget performance but more challenging on mobility performance.
  Receive timing difference;
  Maximum supported Doppler shift for both UL and DL and maximum supported UE speed;
  Other feasibility study is not precluded.

## Slide 10: Way Forward – UE RF Requirement
Baseline power class for FR2 HST:
  Option-1: PC4 as baseline, and FFS PC4 requirement is applicable to FR2 HST scenario.
  Option-2: To define new PC for FR2 HST.
  Option-2a: To define new PC for FR2 HST, with PC5 requirement as baseline.
Approach to specify UE RF requirement:
  Option-1: Provide an applicability rule of FR2 PC4 for the train-roof-mounted UE for FR2 HST scenario, i.e., the applicable FR2 PC4 requirement set for FR2 HST scenario.
  Option-2: Revisit the full set of UE RF requirements for FR2 PC4 UE.
  Option-3: New RF requirement is defined for FR2 HST UE which is different from PC4, specifically, the min peak EIRP for FR2 HST UE follows the agreement for PC5(new FR2 FWA UE).

## Slide 11: Contributions List in RAN4#97-e
T-doc No. | Title | Company
R4-2014846 | Work plan for NR support for high speed train scenario in FR2 | Samsung, Nokia, Nokia Shanghai Bell
R4-2015880 | TR skeleton for NR support for high speed train scenario in FR2 | Nokia, Nokia Shanghai Bell
R4-2014564 | Views on high speed train deployments scenarios in FR2 | Intel Corporation
R4-2014632 | FR2 HST analysis framework | Qualcomm
R4-2014834 | Discussion on scenarios for FR2 high speed train | Verizon, Samsung
R4-2014847 | Discussion on high speed train deployment scenario in FR2 | Samsung
R4-2015614 | Discussion on high speed train deployment scenario in FR2 | Huawei, HiSilicon
R4-2015860 | Deployment scenarios for FR2 HST | Ericsson
R4-2015859 | General considerations for FR2 HST | Ericsson
R4-2016387 | On the high-speed train deployment scenario in FR2 | Nokia, Nokia Shanghai Bell
R4-2014848 | Discussion on UE RF requirement for FR2 HST | Samsung
R4-2015087 | Power Class 4 for HST | Nokia, Nokia Shanghai Bell
R4-2016058 | On UE Core requirements for FR2 HST | Ericsson
R4-2016538 | On RF requirement for NR FR2 HST | Huawei, HiSilicon

## Slide 12: Reference
[1] R4-2016640, “Email discussion summary for [97e][138] NR_HST_FR2_enh”, Samsung