## Slide 1: WF on R16 RRM enhancement part 3 – Multiple SCell activation, UE specific CBW change and feature list 9-8/9-9/9-10
Apple, …
R4-2017202
3GPP TSG-RAN4 Meeting #97-e
Electronic Meeting, 2 – 13 Nov., 2020
Agenda item: 7.13
Document for: Approval
Agreement in 1st round
Agreement in GTW (Nov. 9th)
Agreement in 2nd round

## Slide 2: Multiple SCell activation – core (1/2)
Issue 2-1: Tx beam assumption of FR1 intra-band contiguous CA
  Agreement:
    RAN4 to revisit one of conditions for multiple SCell activation requirement for FR1 contiguous CA, and update it as follows:
      1) Replace
        “its SSB DL Tx beam is same as the corresponding SSB DL Tx beam at the same SSB position of contiguous FR1 known cell or contiguous FR1 active serving cell” with
        “its RTD with contiguous FR1 known cell or contiguous FR1 active serving cell is smaller than or equal to [CP duration] with respect to the to-be-activated SCell’s SSB numerology and its reception power difference with contiguous FR1 known cell or contiguous FR1 active serving cell is smaller than or equal to XdB”, X is FFS.
      2) Replace
        “its SSB DL Tx beam is different as the corresponding SSB DL Tx beam at the same SSB position of contiguous FR1 known cell or contiguous FR1 active serving cell” with
        “its RTD with contiguous FR1 known cell or contiguous FR1 active serving cell is larger than [CP duration] with respect to the to-be-activated SCell’s SSB numerology or its reception power difference with contiguous FR1 known cell or contiguous FR1 active serving cell is larger than XdB”, X is FFS.

## Slide 3: Multiple SCell activation – core (2/2)
Issue 2-2-1: Extend the assumption in FR1 multiple SCells activation to single FR1 SCell activation
  FFS：
    Option 1 (HW, Ericsson, Apple, ZTE, Nokia):
      Extend the UE requirement (to skip cell detection for unknown FR1 SCell that is intra-band contiguous to active serving cell) to single SCell activation, from Rel-16 onwards.
    Option 2 (MTK, QC):
      FFS on option 1.
Issue 2-2-2: Requirement applicability on the other being-activated SCells during the FR1 multiple SCells activation
  FFS：
    Option 1 (Huawei, Ericsson, Apple, QC, ZTE):
      No requirement applies for other being-activated SCells, if no requirements apply for any of the FR1 unknown SCell activated with the same MAC CE
    Option 2 (MTK, Nokia):
      FFS on option 1.
      Issue 2-2-3: Condition of SMTC configuration to apply multiple SCell activation requirement
  FFS
    Option 1 (Huawei, Apple, MTK, QC):
      Multiple SCell activation requirements apply provided that SMTC offset and periodicity is same for all SCells activated by the same MAC CE
    Option 2 (Ericsson, Nokia):
      Disagree with option 1.

## Slide 4: UE specific CBW change - core
Agreement:
  The UE is not required to transmit UL signals or receive DL signals during the time defined by 𝑇𝑅𝑅𝐶𝑝𝑟𝑜𝑐𝑒𝑠𝑠𝑖𝑛𝑔𝐷𝑒𝑙𝑎𝑦+T𝐶𝐵𝑊𝑐ℎ𝑎𝑛𝑔𝑒𝐷𝑒𝑙𝑎𝑦𝑅𝑅𝐶 on the cell where UE-specific CBW change occurs.

## Slide 5: UE specific CBW change – test case (1/2)
Agreements: Test case list:
Test case list for UE specific CBW change | TC parameters
TC1: UE specific CBW change on FR1 NR PSCell with non-DRX in synchronous EN- DC (A.4.5.x) | offsetToCarrier is changed for TC of UE specific CBW change, while carrierBandwidth is unchanged in this TC (same as RF channel BW defined in each test). Reuse the parameters as much as possible from TC of RRC based BWP switching except the BWP switching parameters.
TC2: UE specific CBW change on FR2 NR PSCell with non-DRX in synchronous EN- DC (A.5.5.x) | 
TC3: UE specific CBW change on FR1 NR PCell with non-DRX in NR SA (A.6.5.x) | 
TC4: UE specific CBW change on FR2 NR PCell with non-DRX in NR SA (A.7.5.x) | 

## Slide 6: UE specific CBW change – test case (2/2)
Agreement: add the following generic section into TS38.133
  Table A.3.x.1-1: DL CBW patterns for UE specific CBW configuration
BWP Parameters | Unit | Values | 
Reference CBW |  | DLCBW.1.1 | DLCBW.1.2
OffsetToCarrier | RB | 0 | RBx Note 1
carrierBandwidth | RB | Same as RF channel defined in each test | Same as RF channel defined in each test
Note 1: RBx is offset in frequency domain between Point A (lowest subcarrier of common RB 0) and the lowest usable subcarrier on this carrier. Note that RBx has to be within the CBW of BS. |  |  | 

## Slide 7: Feature list 9-8/9-9/9-10
Background of Feature list 9-8/9-9/9-10:
Agreement:
  Remove feature groups [9-8], [9-9], [9-10] from the RAN4 UE feature list
    The respective requirements are mandatory to be supported for Rel-16 UEs
    It is RAN4 understanding that the network will know the release of the UE.
    Further check with RAN2 if accessStratumRelease signalling can be used to provide information on the release of the UE.
[9-8] | [Multiple SCell activation] | 1) Support of multiple SCell activation RRM requirement
[9-9] | [UE specific CBW change] | 1) Support of UE-specific CBW change RRM requirement
[9-10] | [Spatial relation switch for uplink] | 1) Support of UL spatial relation switch RRM requirement