## Slide 1: WF on performance requirements of CSI-RS based L3 measurement
CATT/OPPO
3GPP TSG-RAN WG4 Meeting #97e R4-2017224 Electronic Meeting, 2 – 13 Nov., 2020

## Slide 2: CSI-RSRP accuracy requirements
Specify the following L3 CSI-RSRP measurement accuracy requirements
    Case 1: the timing offset between UE’s FFT window and the target CSI-RS is smaller or equal to [CP]
      FFS: Reuse the accuracy requirements of SS-RSRP
      FFS on whether gNB needs to know that the timing offset is smaller or equal to CP and how to provide such information if needed
    FFS: Case 2: the timing offset between UE’s FFT window and the target CSI-RS is larger than [CP]

## Slide 3: Side condition for CSI-RSRP measurement
Reuse the side condition of SS-RSRP, i.e.
  FR1 intra-frequency: Es/Iot≥-6dB
  FR2 intra-frequency: Es/Iot≥-6dB
  FR1 inter-frequency: Es/Iot≥-6dB
  FR2 inter-frequency: Es/Iot≥-4dB

## Slide 4: Report mapping for CSI-RSRP measurement
Reuse the report mapping of SS-RSRP.

## Slide 5: Number of samples for defining CSI-RSRP measurement accuracy requirements
Option 1: 5 samples (MTK, Huawei, Xiaomi, CATT, QC, Intel, OPPO, vivo, Apple, ZTE)
Option 2: 3 samples (Nokia)

## Slide 6: Whether to introduce test case for FDD mode
Option 1: No (MTK, Xiaomi, CATT, Qualcomm, OPPO, vivo)
Option 2: Yes (Huawei, Nokia, ZTE)

## Slide 7: CSI-RSRQ accuracy requirements
Specify the following L3 CSI-RSRQ measurement accuracy requirements
    Case 1: the timing offset between UE’s FFT window and the target CSI-RS is smaller or equal to [CP]
      FFS: Reuse the accuracy requirements of SS-RSRP
      FFS on whether gNB needs to know that the timing offset is smaller or equal to CP and how to provide such information if needed
    FFS: Case 2: the timing offset between UE’s FFT window and the target CSI-RS is larger than [CP]

## Slide 8: Report mapping for CSI-RSRQ measurement
Reuse the report mapping for L3 SS-RSRQ (i.e. from -43 dB to +20 dB with 0.5 dB resolution).

## Slide 9: Side condition for CSI-RSRQ measurement
Reuse the side condition for L3 SS-RSRQ.

## Slide 10: Number of samples for defining CSI-RSRQ measurement accuracy requirements
Follow the conclusion of CSI-RSRP measurement

## Slide 11: CSI-SINR accuracy requirements
Specify the following L3 CSI-SINR measurement accuracy requirements
    Case 1: the timing offset between UE’s FFT window and the target CSI-RS is smaller or equal to [TBD]
      FFS: Reuse the accuracy requirements of SS-RSRP
      FFS on whether gNB needs to know that the timing offset is smaller or equal to CP and how to provide such information if needed
    FFS: Case 2: the timing offset between UE’s FFT window and the target CSI-RS is larger than [TBD]

## Slide 12: Side condition for CSI-SINR measurement
RAN4 to discuss how to handle the upper limit of Ês/Iot in the CSI-SINR accuracy requirement together with the timing offset.
  Companies are encouraged to study the upper limit of Ês/Iot of CSI-SINR measurement together with the timing offset and provide views in RAN4 #98e meeting
The lower bound of side condition(Ês/Iot) for CSI-SINR accuracy requirements can be same as that of L3 SS-SINR measurement

## Slide 13: Report mapping for CSI-SINR measurement
Reuse the report mapping of SSB based L3 measurement (i.e. from -23 dB to 40 dB with 0.5 dB resolution)

## Slide 14: Number of samples for defining CSI-SINR measurement accuracy requirements
Follow the conclusion of CSI-RSRP measurement

## Slide 15: Link-level simulation for CSI-RS based L3 measurement
The link-level simulation assumptions were updated in [R4-2017230]
  Interested companies are encouraged to provide simulation results of CSI-RSRP/RSRQ/SINR measurement in RAN4 #98e meeting

## Slide 16: Test case for CSI-RS based L3 measurement
The test case list was agreed in [R4-2017229]
For test cases with DRX
  FR1: Use long DRX
  FR2: Use short DRX