## Slide 1: WF on System simulation assumptions for deriving side conditions update of R4-2012289
Ericsson
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, November 2-13, 2020
Agenda Item: 7.7.3.3
R4-2017370

## Slide 2: Back round
The Side conditions for gNB accuracy requirements are under discussion [1]
The system simulation assumption [2] was approved in RAN4#96-e.
Several simulation results are available in RAN4#97-e [3] [4].
The results are not direct comparable, the update will solve this problem.
[1] R4-2012048 Email discussion summary for [96e][217] NR_pos_RRM_Part_3
[2] R4-2012289 WF on System simulation assumptions
[3] R4-2015769 System and link level simulation results for gNB measurement requirements; Huawei, HiSilicon
[4] R4-2016109 gNB Positioning UL SRS System Simulation Results; Ericsson

## Slide 3: Frequency independent side conditions for gNB accuracy requirements (1)
Channel model: AWGN, UMa, UMi and InH (Scenarios as defined in 38.855):
  Scenario 1. Indoor Office for FR1 and FR2 (Open office) (ISD 20m)
  Scenario 2. UMi street canyon for FR1 and FR2 (ISD 200m)
  Scenario 3. UMa (ISD 500m) for FR1 only (Macro cell only deployment scenario)
Hexagonal grid, 3 sectors per site, 7 macro sites
  Applicable for UMa and UMi, and the scenario of 19 macro sites can be simulated (optional).
1 and 5 UEs per cell. Equal amount of UEs per cell.
2 UE Tx antenna, 2 BS Rx antenna (uncorrelated with equal gain, no rx beamforming).
The BS with smallest path loss (PL) is the serving BS
Power control on and off.
Antenna model based on: TR 38.855

## Slide 4: Frequency independent side conditions for gNB accuracy requirements (2)
Only one configuration for the system simulation
SRS configurations:
  Symbol size =4
  Comb. Number =4
  Cyclic shift Max. Number =12
  Intra-cell, Offsets in Comb. and Cyclic shift keep orthogonal.
  Inter-cell, Offsets in Comb. and Cyclic shift is randomized.
  The specified SRS offset parameter, to reducing overlap of positioning SRS between cells shouldn't be applied.

## Slide 5: Side conditions for gNB accuracy requirements FR1
FR1: 4GHz carrier
Bandwidth: 5 MHz, 10 MHz, 100MHz
SCS: 30kHz
TA: Perfect, serving BS receive all member UE SRSs at the same time
UE TX power: 23 dBm (max for power control is on)
BS RX noise figure: 5 dB

## Slide 6: Side conditions for gNB accuracy requirements FR2
FR2: 40GHz
Bandwidth: 200MHz, 400 MHz (option 100 MHz)
SCS: 120kHz
TA: Perfect, serving BS receive all member UE SRSs at the same time
UE TX power: 23dBm
BS RX noise figure: 7 dB

## Slide 7: Side conditions for gNB accuracy requirements
Output:
Serving cell and neighboring cell Ês/IoT [dB] CDF figures.
5% and mean Es/Iot seen by the n-th strongest cells
To cope with a differential view on the effects of inter- and intra cell interference three different cell occupancies shall be simulated:
  1UE serving cell, full neighboring cells
  5UE serving cell, empty neighboring cells
  all cells 5UE

## Slide 8: Change history
Basis is R4-2012289 - WF on System simulation assumptions
Channel model:
  AWGN and TDL-B (with a medium delay spread) change to
  AWGN and UMa for FR1 and UMi for FR2
Simplified power control
  The power control extend the calculation time.
  It seems difficult to use a simplified version (MIMO Systems are to complex).
  Proposed to deliver results with and without power control.
Cell size
  According to the channel model (TR 38.855)
Number of UEs per cell
  One UE as ideal solution and 5 UEs to show the degradation.

## Slide 9: Antenna Parameter
Appication | Frequency Range |  | FR1 |  |  |  | FR2 |  |  | 
 | Envirement |  | Scenarion 1 500 m |  | Scenario 2 |  | Scenarion 3 200 m |  | Scenario 4 | 
 | Donor or Service Antenna |  | BS-Rx | UE-Tx | BS-Rx | UE-Tx | BS-Rx | UE-Tx | BS-Rx | UE-Tx
Radiation Element | Front to Back Ratio | Am | 30 dB | 25 dB |  |  | 30 dB | 25 dB |  | 
 | Side lobe suppression | SLA | 30 dB | 25 dB |  |  | 30 dB | 25 dB |  | 
 | Half Power Beam Width Horizontal |  | 65° | 90° |  |  | 65° | 90° |  | 
 | Half Power Beam Width Vertical |  | 65° | 90° |  |  | 65° | 90° |  | 
 | Dirctivity (for information) | DE | 9,2 dBi |  |  |  | 8 dBi | 5 dBi |  | 
Antenna Model Parameter | Antenna configuration (M, N, P, Mg, Ng) |  | 8, 8, 2, 1, 1 | 1, 2, 2, 1, 1 |  |  | 4,8,2,2,2 | 2,4,2,1,2 |  | 
 | Number of ports (for information) |  |  |  |  |  |  |  |  | 
 | Vertical radiating element spacing dV | dV | 0,8 λ | 0,5 λ |  |  | 0,5 λ | 0,5 λ |  | 
 | Horizontal radiating element spacing dH | dH | 0,5 λ | 0,5 λ |  |  | 0,5 λ | 0,5 λ |  | 
 | Down tilt angle electical |  | 10° | 0° |  |  | 0° | 0° |  | 
 | Dow tild angele mechanical |  | 0° | 0° |  |  | 0° | 0° |  | 
Antenna Parameter per Port | Directivity (for information) |  | 20 dBi | 18 dBi |  |  |  |  |  | 
 | Antenna losses |  | 1,8 dB | 1,8 dB |  |  | 1 dB | 1dB |  | 
 | Gain |  | 18 dBi | 0 dBi |  |  | 17 dBi | 27 dBi |  | 
Note: | Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. |  |  |  |  |  |  |  |  | 

## Slide 10: Antenna model