## Slide 1
3GPP TSG-RAN WG4 Meeting #97-e R4-2017549
Electronic Meeting, 2nd – 13th Nov, 2020
Agenda Item: 7.15.3.1
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS
  R4-1915926 WF on UE demodulation for NR HST, RAN4#93
  R4-2002418 WF on UE demodulation for NR HST, RAN4#94-e
  R4-2005532 WF on UE demodulation for NR HST, RAN4#94bis-e
  R4-2008820 WF on UE demodulation for NR HST, RAN4#95-e
  R4-2012668 WF on UE demodulation for NR HST, RAN4#96-e

## Slide 3: Test setup for DPS 1a
Two RRHs of RRH#(2k) and RRH#(2k+1) are assumed, and SSB#0 is transmitted from both TRPs, where k is the RRH number with k=0,1, 2, …
  UE is configured with TCI#(k mod 2) and TCI#((k+1) mod 2) that are associated with TRS#(k mod 2) and TRS#((k+1) mod 2) transmitted from RRH#(2k) and RRH#(2k+1) respectively by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
  All the configured TCI states are known to UE. UE is configured with NZP-CSI-RS resource for L1-RSRP measurements by RRC signaling nzp-CSI-RS-ResourceSet within the CSI-ResourceConfig and periodic CSI reporting by setting reportConfigType to periodic and reportQuantity to cri-RSRP (Note: reported L1-RSRP mesurements are not tested)
TE actives TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE”;
PDSCH associated with TCI #0 is transmitted during the slots from 0 to n+ HARQ needed time + 3ms;
In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
PDSCH associated with TCI #1 is transmitted in slots from n+1 + HARQ needed time + 3ms + first TRS + TRS processing time to N.
Generalized: PDSCH associated with TCI #(k mod 2) (k=0,1,2,…) is transmitted in slot from max((2k-1)n + 1 + HARQ needed time + 3ms + first TRS + TRS processing time, 0) to (2k+1)n + HARQ needed time + 3ms, where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH. And k is the RRH number in the channel model.
NOTE: MAC CE is transmitted in slot n

## Slide 4: Test setup of DPS 1b
Test setup for transmission scheme 1b with 2 active TCI states
      (total 2 active TCI states): PDCCH TCI state switching delay caused by MAC CE, but less than DPS 1a with pre-tracking of second TCI state and only HARQ needed time + 3ms delay is needed, UE tracks 2 active TCI states in advance so that UE can quickly get better Doppler shift estimation for the second TRP compared to DPS 1a.
      UE is configured with two different TCI states (TCI #0 and TCI #1) associated with two different RRHs by RRC signalling tci-StatesToAddModList in the PDSCH-Config and tci-PresentInDCI is not configured;
      TE activates TCI #0 and TCI #1 for PDSCH at the same time by “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” and activates TCI #0 for PDCCH by “TCI State Indication for UE-specific PDCCH MAC CE” command with the field of CORESET ID set to 0;
      TE transmits PDCCH and PDSCH associated with TCI #0 from TRP#1 from slot 0 to n + HARQ needed time + 3ms ;
      In slot n TE start triggering TCI state switching command to TCI #1 by “TCI State Indication for UE-specific PDCCH MAC CE”;
      TE transmits PDCCH and PDSCH associated with TCI #1 from TRP#2 from slot n + 1 + HARQ needed time + 3ms to N. where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH
      Generalized: PDSCH associated with TCI #(k mod 2) (k=0,1,2,…) is transmitted in slot from max((2k-1)n +1 + HARQ needed time + 3ms, 0) to (2k+1)n + HARQ needed time + 3ms, where n slots are equivalent to time that needed to pass middle point between two RRHs, N slots is equivalent to time that needed to pass second RRH. And k is the RRH number in the channel model.
      NOTE: MAC CE is transmitted in slot n

## Slide 5: DPS
  MCS
    MCS 17 based on 64QAM tables
  Scheduling in TDD special slot
    Scheduled PDSCH in TDD special slots and the special slot configuration as S: 6D 4G 4U as baseline based on the assumption that no obvious performance degradation compared to no slots scheduled in special slot.

## Slide 6: DPS
  Number of active TCI states in DPS transmission scheme 1b
    with 2 active TCI states in Rel-16
    RAN4 can decide whether to further discuss test cases with >2 active TCI states in Rel-17 timeframe i.e. in Rel-17 FR1 HST WI
  SSB and TRS transmission
    Every RRH has to transmit QCL’ed SSB and TRS for every TCI state used in the DPS schemes
  Switch command
    The switch command is transmitted via MAC CE, the corresponding PDSCH carrying that MAC CE should be ensured to be decoded successfully and MCS 4 should be used
  PDCCH and PDSCH setting during the transition time for DPS 1a
    For DPS transmission mode 1a, PDCCH/PDSCH are DTXed from the time gNB indicate MAC CE TCI state switch + HARQ processing time + 3ms, to the time UE received and processed the first TRS from the new TRP.
    TE does not consider the transition period for throughput calculation
    OCNG pattern will be applied for DTXed period.

## Slide 7: DPS
  Extra test metric for DPS requirements
    Not define extra test metric in Rel-16

## Slide 8: Test applicable rules for DPS
If UE passed HST-DPS 1a or 1b, Rel-15 HST Single-tap test and Rel-16 HST Single-tap test except for Rel-16 FDD HST Single-tap test can be skipped.
No test applicable rules among HST-SFN and HST DPS schemes 1b
No test applicable rules among HST-SFN and HST DPS scheme 1a
If a UE declared supporting > 1 TCI states, the UE will pass scheme 1b and skipped scheme 1a test cases
If a UE only support 1 TCI state, the UE need to pass scheme 1a and skip scheme 1b test cases

## Slide 9: Applicability rule
Test applicability between HST-SFN and HST single tap
  Skip both Rel-15 and Rel-16 HST single tap test except for Rel-16 FDD HST single-tap, if UE passes the requirements for HST-SFN
Test applicability between HST-SFN and HST multi-path fading
  Do not define any applicability rules between HST-SFN and HST multi-path fading performance test cases

## Slide 10: Applicability rule
Test applicability between different Doppler frequencies for the same channel model
  For FDD
    Not define any applicability rule for TDLC300-100
  For TDD
    Not define any applicability rule for TDLC300-100

## Slide 11: Simulation assumption for DPS transmission scheme
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 17 based on 64QAM table | 
Propagation condition | HST-DPS (Assume two TRPs for HST-DPS transmission scenario) | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 870Hz | 1667Hz
HARQ needed time/slots | 2 | 8,7,6,5,5,4,3,2
TRS processing time | 2ms | 
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15 |  | 

## Slide 12: Simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 870Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 13: Simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1x2; 1x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 972Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 14: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15