## Slide 1: WF on BS demodulation requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 Meeting #97-e
E-meeting, 2nd – 13th Nov., 2020
R4-2017580

## Slide 2: Background
Agreed WFs in previous meetings (Newest first)
  RAN4#96-3
    R4-2012705 WF on BS demodulation requirements for 2-step RACH
  RAN4#95-e
    R4-2008864 WF on BS demodulation requirements for 2-step RACH
  RAN4#94bis-e
    R4-2005555 WF on BS demodulation performance requirements for 2-step RACH
  RAN4#94-e
    R4-2002389 WF on BS demodulation requirements for 2-step RACH

## Slide 3: Agreement (1) – TO cycling level
Only define performance requirements for high level TO cycling but with revised TO values

## Slide 4: Agreement (2) – DMRS configuration for FR1
  Define only one set of requirements for FR1
  Since the performance difference between two DMRS configuration is negligible, the same requirements would apply to both
    When deriving performance requirements, simulation results with both DMRS configurations are treated together
  In the tests, DMRS can be configured to 1+1 or 1+1+1 according to vendor’s declaration under the same core performance requirements

## Slide 5: Agreement (3) – High level TO cycling values
Set TO values (µs)for high level TO cycling as following:
  15 kHz: [0 : 0.2 : 3.8]
  30 kHz: [0 : 0.1 : 2]
  60 kHz: [0 : 0.1 : 0.6]
  120 kHz: [0 : 0.1 : 0.5]

## Slide 6: Agreement (4) – Test metric
  BLER = 0.01

## Slide 7: Agreement (5) – Derivation of BS demodulation performance requirements for 2-step RACH
  Apply the same derivation rule as NR PUSCH

## Slide 8: Way forward (6) - CR work split
 | CRs | Assigned Company
#1 | CR to TS 38.104 BS demodulation requirements for 2-step RACH (Section 8.2.6 and Annex) | ZTE
#2 | CR to TS 38.141-1 BS demodulation requirements for 2-step RACH (Section 8.2.6) | Ericsson
#3 | CR to TS 38.104 BS demodulation requirements for 2-step RACH (Section 11.2.1 and 11.2.2) | Huawei
#4 | CR to TS 38.141-1 BS demodulation requirements for 2-step RACH (Annex) | Nokia
#5 | to TS 38.141-2 BS demodulation requirements for 2-step RACH (Section 8.2.6) | Samsung
#6 | CR to TS 38.141-2 BS demodulation requirements for 2-step RACH (Annex) | Intel

## Slide 9: Simulation setup
Parameter | Values for FR1 | Values for FR2
Preamble format | Free choice | 
Waveform | CP-OFDM | 
Power offset between preamble and MsgA | Free choice | 
Subcarrier spacing for PUSCH | 15kHz, 30kHz | 60kHz, 120 kHz
PUSCH Mapping Type | Type A and Type B | Type B
MCS level | 1 | 2
Number of symbols | 14 | 10
Number of PRBs | 2 | 2
TBS | 56 - 72 bits 72 bits | 
DMRS | Option 1: 1+1+1 Option 2: 1+1 Free to use either 1+1+1 or 1+1 meeting the same demodulation performance requirements | Baseline: 1+1
Antenna configuration | 1T2R | 1T2R
Propagation channel | TDLC300-100 | TDLA30-300
TO values | Medium level cycling values: 15k SCS: [0:0.4:2], 30k SCS: [0:0.2:1] High level cycling values 15k SCS: [0:0.2:3.8], 30k SCS: [0:0.1:2] | Medium level cycling values: 60k SCS: [0:0.1,0.5], 120 SCS: [0:0.05,0.25] High level cycling values: 60k SCS: [0:0.1,0.6], 120 SCS: [0:0.1,0.5]
Test metric (BLER of MsgA when preambles are correctly detected) | Baseline: 0.01 | Baseline: 0.01
Re-transmission | No retransmission considered |