## Slide 1
WF on remaining open issues with the test methodology for high DL power and low UL power test cases
3GPP TSG-RAN WG4 Meeting #97-e R4-2017593
Electronic Meeting, Nov. 2nd – Nov. 13th, 2020
Agenda Item: 13.1.1
Apple Inc.

## Slide 2: Background
RAN4 discussed the following issues related to test methodology for high DL power and low UL power test cases:
  Issue 1-1-1: Simulation assumptions for beam management sensitivity of NF based solutions
  Issue 1-1-2: Results collection for beam management sensitivity of NF based solutions
  Issue 1-2-1: Which NF based solutions are in scope of the SI?
  Issue 1-2-2: For NF based solutions what manufacturer declarations should be considered in scope of the SI?
  Issue 1-3-1: Summary of potential improvements of permitted methods
  Issue 1-3-2: Criteria for consideration of non-permitted methods
Agreements related to Issues 1-1-1, 1-1-2, 1-2-2, 1-3-1 are captured in a revised text proposal to TR 38.884
The remaining open issues are addressed in this WF

## Slide 3: WF1: Which NF based solutions are in scope of the SI?
Proposals
  Alt 1-1: Direct near-field (DNF) system, where a beam peak search is necessary to perform all applicable test case procedures
  Alt 1-2: Combined far-field/near-field (CFFNF) system, where beam peak direction and UE beamlock function (UBF) activation are performed based on the far-field method and then test case procedures are performed based on the near-field method
  Alt 1-3: Coaxial Cone TEM cell approach
Agreement
  At least DNF and CFFNF systems are part of the study, including the beam management sensitivity evaluations
    Whether DNF or NF with transform is used for CFFNF is FFS
  The following aspects related to the coaxial cone TEM cell approach are FFS:
    EM field distribution and impact of stirring effects
    Whether an analysis of beam management sensitivity is needed

## Slide 4: WF2: Criteria for consideration of non-permitted methods
Proposals
  Alt 2-1: For a given test case, non-permitted methods should be only considered if the improvement is better than the potential improvement of the permitted method
  Alt 2-2: In addition to Alt 2-1, test time and test setup complexity can also be considered
Agreement
  For a given test case, non-permitted methods should be only considered if the improvement is better than the potential improvement of the permitted method.
  In addition, test time and test setup complexity can also be considered.

## Slide 5: WF3: Remaining open issues
Related to beam management sensitivity of NF based solutions
  Conclusions based on the simulation results currently available and any additional results are encouraged by the next RAN4 meeting in order to select the enhancement solution
Related to manufacturer declarations
  Whether NF based solutions consider the “black box” or “black & white box” assumptions as a baseline is FFS
Related to enhancement of permitted methods
  Companies are encouraged to share their analysis of the potential potential improvement of permitted methods vs test case by the next RAN4 meeting in order to draw conclusions related to this aspect

## Slide 6: References
Reference | Tdoc | Source | Title
[1] | R4-2014267 | Qualcomm Incorporated | Impact on beam management due to spherical wavefront in DL
[2] | R4-2014919 | Apple Inc. | TP to TR38.884 on High DL and Low UL power test cases
[3] | R4-2015319 | CAICT | On Test methodology for high DL power and low UL power test cases
[4] | R4-2016213 | Keysight Technologies | On Test methodology for high DL power and low UL power test cases
[5] | R4-2016377 | MVG Industries, Sony | Impact of phase variation
[6] | R4-2016562 | Rohde & Schwarz | Views on test methods for high DL power and low UL power TCs