## Slide 1: WF on Irregular channel bandwidths
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, November 2th – 13th 2020
R4-2017833
Ericsson

## Slide 2: Background
R4-2014895, “Non-standard spectrum allocations for NR bands”, Apple
R4-2016456, “Revised SID: Study on Efficient utilization of licensed spectrum that is not aligned with existing NR channel bandwidths”, T-Mobile USA, Ericsson
R4-2014507, “UE Support for Irregular Channel Bandwidths - Options and Constraints”, Skyworks Solutions Inc.
R4-2016111, “Discussion on irregular channel bandwidth for NR system”, ZTE Corporation
R4-2014487, “Handling of Channel Bandwidths That Are Not Multiples of 5MHz”, Qualcomm Incorporated
R4-2015562, “On efficient utilization of licensed spectrum”, Intel Corporation
R4-2015713, “Overlapping UE channel bandwidths”, Huawei, HiSilicon
R4-2016201, “On the use of overlapping channel bandwidths from UE perspective”, Nokia, Nokia Shanghai Bell
R4-2016455, “Use of 5 MHz overlapping channel BWs to cover spectrum blocks between 5 and 10 MHz”, T-Mobile USA

## Slide 3: WF on numerologies considered for SI
Generic solution(s) should be prioritized. Generic solution(s) may not require definition of bandwidth granularity. Study solutions which aim to consider bandwidth inputs should consider integer 1MHz bandwidth granularity up to 13 MHz.
33 MHz not to be considered for n28. 30 MHz should be used instead.
New irregular bandwidth requests to be studied must be approved at the RAN plenary.
Study only 15 kHz SCS for bandwidths < 10 MHz and both 15 kHz and 30 kHz SCS for bandwidths > 10 MHz
Solutions which have low spectral utilization for 30 kHz SCS can be removed from consideration

## Slide 4: WF on Configuring immediately larger DL CBW
Concerns have been raised on how to ensure conformance/regulatory requirements are met for both UE/gNB
Study how to handle much larger channel bandwidths when applying next larger channel bandwidth approach i.e. what is the limiting bandwidth difference from irregular bandwidth to next larger channel bandwidth that may still make selecting larger channel bandwidth feasible.

## Slide 5: WF on overlapping UE CBW approach
Consider a solution for overlapping UE carriers with
  subcarrier alignment
  RB alignment is required FFS
  channel raster constraints should also be considered if otherwise there is considerable specification impact.
  where RAN4 to continue to discuss impact (pros/cons) in next round but also to capture some initial points towards a basis for further study. Companies are encouraged to share their view about whether allowing for other subcarrier grid aligned positions of the UEs’ channel BW than centred around a channel raster frequency would cause an issue, and if so, what exactly the problem would be and whether it would only be related to legacy UEs or also to future UEs.
For overlapping UE carriers, to minimize specification impact, study solutions whereby new channel BW need not be explicitly defined for UE and gNB, irregular channel bandwidths can be supported by overlapping RF carriers. Companies are encouraged to provide analysis from UE DL support only and UE DL+UL support perspective.
As an alternative option to (2) also consider a solution where new channel BW only for gNB, use existing channel BW for UE

## Slide 6: Open issues
Blocking related issues (Issue 2-3) for regulatory requirement
Overlapping CBWs for conformance testing, 2 carriers need to be spent for one irregular CBW (Issue 2-3)
UE DL support only and UE DL + UL support perspective (R4-2016201)
RAN4 needs to check/investigate further whether there are conformance/regulatory issues for overlapping UE channel bandwidths