## Slide 1: WF on DC location reporting for intra-band UL CA
Huawei, HiSilicon
R4-200XXXX
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: Background
Comments from companies in RAN#89-e on the above solutions:
2 solutions provided in approved LS R4-2011906:
Report TX DC location after every activation of BWP’s including CC activation, BWP switching procedure, etc.
Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
Agreement in RAN#89-e for intra-band UL CA DC location:
Proposal: a mechanism of DC location reporting for intra-band UL CA should be specified in Rel-16
• RAN2 is tasked to provide at least one RAN2-based signalling solution for at least 2 UL CCs of intra-band UL CA in FR1 to RAN#90, considering forward compatibility to other combinations (more than 2 UL CCs and/or FR2)
• Other solutions are not precluded and can be discussed in RAN1, RAN2 and RAN4. Selection between solutions can be discussed at RAN#90 or later (if possible).
conclusion: proposal is endorsed
Almost all companies prefer solution 2 for Rel-16 considering the limited time budget and the potential spec impact to RAN1
It can be referred in RP-202018

## Slide 3: Tx DC location for intra-band UL CA
In Rel-16, mechanism of DC location reporting is only defined for intra-band UL CA in FR1
  If no concrete solution for more than 2 UL CCs reached in RAN4 #97-e, mechanism for 2 UL CCs of intra-band UL CA in FR1 should be defined, solution 2 in approved R4-2011906 is adopted for 2UL CCs
Factors affecting UL DC locations of intra-band UL CA in FR1
  lowest and highest CC activated
  active BWPs in lowest and highest CC activated
  configured BWPs in lowest and highest CC activated
Reporting mechanism
  RRC based signaling is adopted
Does DC location need to be reported if it falls into the gap between two CCs
  3300/3301 is still allowed for DC location of intra-band UL CA
In Rel-17, RAN4 further discuss on DC location reporting for FR2
  Dynamic mechanism is not precluded in Rel-17

## Slide 4: Enhancements for RRC based solution in Rel-16
In RAN4#97-e, 4 enhancements based on RRC signaling solution are discussed provided:
  enh1: Network provide a list of likely BWP permutations to UE in advance
  enh2: Default DC location
    UE DC location can be considered by default in the centre calculated by the lower edge of the lowest CC and the higher edge of the highest CC among all the active CCs
    UE DC location can be considered by default in the centre of the lower edge of the lowest active BWP and the higher edge of the highest active BWP among all the active CCs
    UE DC location can be considered by default in the center of following cases and it is up to UE decide which case it belongs to:
      the lower edge of the lowest CC and the higher edge of the highest CC among all the active CCs
      the lower edge of the lowest active BWP and the higher edge of the highest active BWP among all the active CCs
      the lower edge of the lowest configured BWP and the higher edge of the highest configured BWP among all the configured CCs
      Other cases FFS
  enh3: Report possible DC locations for all the 2CCs pairs within the configured CA band combination.
  enh4: gNB may request UE to report. If there is no request from BS, UE doesn’t report its DC location.
RAN4 choose One or multiple enhancement solutions in above used for FR1 intra-band UL CA DC location reporting, the decision is included in LS to RAN2

## Slide 5: Reference