## Slide 1: WF on DC location reporting for intra-band UL CA
Huawei, HiSilicon
R4-200XXXX
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: Background
Comments from companies in RAN#89-e on the above solutions:
2 solutions provided in approved LS R4-2011906:
Report TX DC location after every activation of BWP’s including CC activation, BWP switching procedure, etc.
Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
Agreement in RAN#89-e for intra-band UL CA DC location:
Proposal: a mechanism of DC location reporting for intra-band UL CA should be specified in Rel-16
• RAN2 is tasked to provide at least one RAN2-based signalling solution for at least 2 UL CCs of intra-band UL CA in FR1 to RAN#90, considering forward compatibility to other combinations (more than 2 UL CCs and/or FR2)
• Other solutions are not precluded and can be discussed in RAN1, RAN2 and RAN4. Selection between solutions can be discussed at RAN#90 or later (if possible).
conclusion: proposal is endorsed
Almost all companies prefer solution 2 for Rel-16 considering the limited time budget and the potential spec impact to RAN1
It can be referred in RP-202018
RAN4 introduce UE capability of DC location for intra-band UL CA in FGI 7-5:
7-5 | DC location for intra-band CA | indicate whether UE support Additional DC location reporting for intra-band UL CA |  | Yes | N/A | The gNB cannot correctly calculate the DC location of intra-band CA
CR for TS 38.101-1 on DC location for intra-band UL CA is agreed:

## Slide 3: Tx DC location for intra-band UL CA
In Rel-16, mechanism of DC location reporting is only defined for intra-band UL CA in FR1
  If no concrete solution for more than 2 UL CCs reached in RAN4 #97-e, mechanism for 2 UL CCs of intra-band UL CA in FR1 should be defined, solution 2 in approved R4-2011906 is adopted for 2UL CCs
Factors affecting UL DC locations of intra-band UL CA in FR1
  lowest and highest CC activated
  active BWPs in lowest and highest CC activated
  configured BWPs in lowest and highest CC activated
  PA architecture
    For UE indicates 1PA architecture, the number of DC location is one at an instant
    For UE indicates 2PA architecture, the number of DC location is two at an instant, in which one DC location serves for each PA
    each of the DC location can be reported based on one DC location method(s)
  Include the factors above in the LS to RAN2
Reporting mechanism
  RRC based signaling is adopted
Does DC location need to be reported if it falls into the gap between two CCs
  3300/3301 is still allowed for DC location of intra-band UL CA
In Rel-17, RAN4 further discuss on DC location reporting for FR2
  Dynamic mechanism is not precluded in Rel-17

## Slide 4: Enhancements for RRC based solution in Rel-16
In RAN4#97-e, 4 following enhancements based on RRC signaling solution 2 in R4-2011906 are discussed provided:
  1. Combination of setting up the rule for default DC location for the most likely cases and other reporting method(s)
  NW to identify DC location
    If UE does not support FGI 7-5 additional DC location reporting, is based on txDirectCurrentLocation in UplinkTxDirectCurrent IE in Rel-15 TS 38.331
    if UE report support FGI 7-5 additional DC location reporting, but does not report the values, by default, the location is:
    UE DC location can be considered by default in the centre calculated by the lower edge of the lowest CC and the higher edge of the highest CC among all the active CCs
      UE DC location can be considered by default and/Or in the centre of the lower edge of the lowest active BWP and the higher edge of the highest active BWP among all the active CCs by UE with a capability
      FFS on the default value:
        Down select on above 2 options
    Increase the above capability bit and/or allow UE to report DC location for cases not covered by the default rule such as
        the lower edge of the lowest configured BWP and the higher edge of the highest configured BWP among all the configured CCs
  2. Reporting methods if UE indicates on support FGI 7-5 and report values:
  1) A UE reports each UL DC location per 2CCs pairs permutation for all possible simultaneously activated BWPs pairs. (R4-2016514)
  2) A UE informs a network of UL DC locations by referring to a list including simultaneously activated BWP permutations provided by the NW (R4-2014714)
  Note: in case DC location report is not time critical, gNB may request UE to report.
The above enhancements is included in LS to RAN2

## Slide 5
RAN4 CR on DC location for intra-band UL CA
If RAN2 implements the solution with “rule for default DC location ” in previous slide, RAN4 will revise corresponding RF requirement(s) related to DC loation for TS 38.101-1 in next meeting.