3GPP TSG-RAN WG4 Meeting # 97-e                                                              R4-2014187

# Electronic Meeting, 2– 13 November, 2020

Source: 	MediaTek Inc.

Title: 	Discussion of MSD for 3DL2UL DC_42_n1-n79 and DC_19_n1-n77 due to UL IMD issues

Agenda item:	10.7.2

Document for:	Approval

# Introduction

In this paper, we found that there are IMD issues for ENDC bands combination of DC_19_n1-n77 and DC_42_n1-n79. The contribution is to provide MSD levels for DC_19_n1-n77 and several observations for DC_42_n1-n79.

# 2. Discussion

## Considerations of IMD and MSD for DC_42_n1-n79

Due to frequency of operation, the IMD of 2UL B42 and n79 falls into n1 RX band. There are IMD3 and IMD4 issues as follows.

- IMD3 of UL n79 and B42 : victim frequency range 1800 MHz – 2800 MHz overlaps with n1 RX band

- IMD4 of UL n79 and B42 : victim frequency range 1600 MHz – 3200 MHz overlaps with n1 RX band

Observation 1: There are IMD3 and IMD4 issues of 2UL bands n79 and B42 which causes IMD spur in band n1.

MSD from specification [1] for DC_1A-42A_n79A is shown in Table 1. MSD of Band 1 in Table 2.1-1 can be reused for NR band n1 to accommodate IMD3 and IMD4 issues of 2UL bands B42 and n79 if 2UL configuration DC_42-n79 is needed and allowed.

| CA Configuration | NR band | UL Fc | UL/DL BW | UL | DL Fc | MSD | IMD order |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | (MHz) | (MHz) | LCRB | (MHz) | (dB) |  |
| DC_1A-42A_n79A | 1 | 1977.5 | 5 | 25 | 2167.5 | N/A | N/A |
|  | n79 | 4420 | 40 | 216 | 4420 | N/A | N/A |
|  | 42 | 3490 | 5 | 25 | 3490 | 4.8 | IMD5 |
|  | 42 | 3402.5 | 5 | 25 | 3402.5 | N/A | N/A |
|  | n79 | 4640 | 40 | 216 | 4640 | N/A | N/A |
|  | 1 | 1975 | 5 | 25 | 2165 | 15.5 | IMD3 |
|  | 42 | 3450 | 5 | 25 | 3450 | N/A | N/A |
|  | n79 | 4520 | 40 | 216 | 4520 | N/A | N/A |
|  | 1 | 1950 | 5 | 25 | 2140 | 9.3 | IMD4 |

Table 2.1-1: MSD for DC_1A-42A_n79A

Observation 2: If 2UL configuration DC_42-n79 for DC_1A-42A_n79A or DC_42_n1-n79 is needed and allowed, IMD3 and IMD4 MSD of Band 1 for DC_1A-42A_n79A can be reused for NR n1 MSD DC_42_n1-n79 as shown in Table 2.1-2.

| NR Band / Channel bandwidth / NRB / MSD |
| --- |
| CA Configuration | NR band | UL Fc | UL/DL BW | UL | DL Fc | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB | (MHz) | (dB) |  |
| DC_42A_n1A-n79A DC_42C_n1A-n79A | 42 | 3402.5 | 5 | 25 | 3402.5 | N/A | N/A |
|  | n79 | 4640 | 40 | 216 | 4640 | N/A | N/A |
|  | n1 | 1975 | 5 | 25 | 2165 | 15.5 | IMD3 |
|  | 42 | 3450 | 5 | 25 | 3450 | N/A | N/A |
|  | n79 | 4520 | 40 | 216 | 4520 | N/A | N/A |
|  | n1 | 1950 | 5 | 25 | 2140 | 9.3 | IMD4 |

Table 2.1-2: MSD for DC_42_n1-n79

As for 2UL bands n1 and B42, IMD frequency overlaps with n79 RX band. If TDD bands B42 and n79 do not support simultaneous B42 UL and n79 DL, IMD issues of 2UL bands n1 and B42 do not impact n79 RX band.

Observation 3: The IMD frequency of 2UL B42 and n1 overlaps with n79 RX band and is shown in Table 2.1-3. If TDD bands B42 and n79 do not support simultaneous B42 UL and n79 DL, IMD issues of 2UL bands n1 and B42 do not impact n79 RX band.

| n1 UL | B42 UL | IMD3 of 2*B42-1*n1 | IMD5 of 4*n1-1*B42 | n79 DL |
| --- | --- | --- | --- | --- |
| (MHz) | (MHz) | (MHz) | (MHz) | (MHz) |
| 1920-1980 | 3400-3600 | 4820-5280 | 4080-4520 | 4400-5000 |

Table 2.1-3: IMD frequencies of 2UL B42 and n1

Observation 4: Because n77 and n79 do not support simultaneous TX/RX, there are 2 options for B42 filter selection when B42 co-band with n78 or not [3]. If TDD bands n79 and B42 support simultaneous B42 UL and n79 DL then MSD for IMD is needed. If TDD bands n79 and B42 support simultaneous B42 DL and n79 UL then MSD for this configuration is not needed for DC_42_n1-n79.

## REFSENS Levels and MSD for DC_19_n1-n77

MSD from specification [1] for DC_1A-19A_n77A/n78A is shown in Table below. MSD of B1 in Table below can be reused for NR n1 to accommodate IMD3 issue of 2UL bands B19 and n77 for DC_19_n1-n77.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_1A-19A_n77A DC_1A-19A_n78A | 1 | 1940 | 5 | 25 | 2130 | 17.8 | IMD3 |
|  | 19 | 832.5 | 5 | 25 | 877.5 | N/A | N/A |
|  | n77, n78 | 3795 | 10 | 50 | 3795 | N/A | N/A |

Table 2.2-1: MSD for DC_1-19_n77/n78

Proposal 1: IMD3 MSD of LTE B1 for DC_1A-19A_n77A can be reused for NR n1 MSD for DC_19A_n1A-n77A as shown in Table 2.2-2.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_19A_n1A-n77A DC_19A_n1A-n78A | n1 | 1940 | 5 | 25 | 2130 | 17.8 | IMD3 |
|  | 19 | 832.5 | 5 | 25 | 877.5 | N/A | N/A |
|  | n77, n78 | 3795 | 10 | 50 | 3795 | N/A | N/A |

Table 2.2-2: MSD for DC_19A_n1A-n77A/n78A

MSD from specification [1] for DC_20A_n1A-n78A is shown in Table below. MSD of n78 in Table below may be considered for NR n77 to accommodate IMD3 issue of 2UL bands B19 and n1 for DC_19_n1-n77. Before MSD decision, further reconfirmation of B19 filter rejection capability with respect to B20 is needed.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_20A_n1A-n78A | 20 | 845 | 5 | 25 | 804 | N/A | N/A |
|  | n1 | 1940 | 5 | 25 | 2130 | N/A | N/A |
|  | n78 | 3630 | 10 | 50 | 3630 | 16 | IMD3 |

# Table 2.2-3: MSD for DC_20A_n1A-n78A

Here B19 and B5 share the same filter. B19’s rejection capability for IMD spur of frequency 3655MHz under typical condition is shown below. The MSD analysis result of IMD3 interferer and RX noise is shown in Table 2.2-4.

Figure 1

| Parameter | Value | Unit |
| --- | --- | --- |
| Antenna isolation | 12 | dB |
| PCB isolation from Primary TX to Main RX | 65 | dB |
| PCB isolation from Primary TX to Primary RX | 60 | dB |
| Primary RX front-end and path loss | 4.5 | dB |
| Diversity RX front-end and path loss | 4 | dB |
| Coupling isolation of PA output to PA input | 60 | dB |
| SNR requirement for QPSK | -1 | dB |
| Total interference and noise power referred to antenna | -69.9 | dBm/10MHz |
| MSD after MRC | 21.4 | dB |

Table 2.2-4: MSD for DC_19A_n1A-n78A

The highest IMD3 frequency from IMD of n1 and band 19 is around 3655MHz, thus the MSD could also be used for DC_19A_n1A-n77A.

Proposal 2: IMD3 MSD of NR n78 for DC_19A_n1A-n78A is shown in Table 2.2-5.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_19A_n1A-n77A DC_19A_n1A-n78A | 19 | 840 | 5 | 25 | 885 | N/A | N/A |
|  | n1 | 1975 | 5 | 25 | 2165 | N/A | N/A |
|  | n77, n78 | 3655 | 10 | 50 | 3655 | [21.4] | IMD3 |

Table 2.2-5: MSD for DC_19A_n1A-n78A

# 3. Conclusion

In this contribution, MSD requirements are proposed to accommodate IMD issues of DC_42_n1-n79.

Observation 1: There are IMD3 and IMD4 issues of 2UL bands n79 and B42 which causes IMD spur in band n1.

Observation 2: If 2UL configuration DC_42-n79 for DC_1A-42A_n79A or DC_42_n1-n79 is needed and allowed, IMD3 and IMD4 MSD of Band 1 for DC_1A-42A_n79A can be reused for NR n1 MSD DC_42_n1-n79 as shown in Table 2.1-2.

Observation 3: The IMD frequency of 2UL B42 and n1 overlaps with n79 RX band and is shown in Table 2.1-3. If TDD bands B42 and n79 do not support simultaneous B42 UL and n79 DL, IMD issues of 2UL bands n1 and B42 do not impact n79 RX band.

Observation 4: Because n77 and n79 do not support simultaneous TX/RX, there are 2 options for B42 filter selection when B42 co-band with n78 or not [3]. If TDD bands n79 and B42 support simultaneous B42 UL and n79 DL then MSD for IMD is needed. If TDD bands n79 and B42 support simultaneous B42 DL and n79 UL then MSD for this configuration is not needed for DC_42_n1-n79.

Proposal 1: IMD3 MSD of LTE B1 for DC_1A-19A_n77A can be reused for NR n1 MSD for DC_19A_n1A-n77A as shown in Table 2.2-2.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_19A_n1A-n77A DC_19A_n1A-n78A | n1 | 1940 | 5 | 25 | 2130 | 17.8 | IMD3 |
|  | 19 | 832.5 | 5 | 25 | 877.5 | N/A | N/A |
|  | n77, n78 | 3795 | 10 | 50 | 3795 | N/A | N/A |

Table 2.2-2: MSD for DC_19A_n1A-n77A/n78A

Proposal 2: IMD3 MSD of NR n78 for DC_19A_n1A-n78A is shown in Table 2.2-5.

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA / NR band | UL Fc | UL/DL BW | UL | DL Fc (MHz) | MSD | IMD order |
|  |  | (MHz) | (MHz) | LCRB |  | (dB) |  |
| DC_19A_n1A-n77A DC_19A_n1A-n78A | 19 | 840 | 5 | 25 | 885 | N/A | N/A |
|  | n1 | 1975 | 5 | 25 | 2165 | N/A | N/A |
|  | n77, n78 | 3655 | 10 | 50 | 3655 | [21.4] | IMD3 |

Table 2.2-5: MSD for DC_19A_n1A-n78A

# 4. References:

[1] TS 38.101-3 “NR User Equipment (UE) radio transmission and reception Part 3”

[2] TR 38.717-03-02	“Rel-17 NR inter-band Carrier Aggregation/Dual connectivity for 3 bands DL with 2 bands UL”

[3] R4-2015068, “MSD for CA 3DL2UL n1-n77-n79 for TR 38.717-03-02“