## Slide 1: Way Forward on Release independence for 35 and 45 MHz
T-Mobile USA, TELUS, Bell Mobility, AT&T, Nokia
3GPP TSG-RAN WG4 Meeting #97-e R4-2016862
Electronic Meeting, 2-13 Nov., 2020

## Slide 2: Background: Release options for 35 and 45 MHz
Option 1: The support of 35 MHz and 45 MHz is from Rel-17 onwards
  Supported by ZTE and Apple
Option 2: 35 MHz and 45 MHz is optional support from Rel-15
  Supported by Ericsson, T-Mobile USA, Nokia, AT&T, Bell Mobility, TELUS
Option 3: Release independence shall be discussed cases by case per band and bandwidths.
  Skyworks, OPPO

## Slide 3: Background: 5 Aspects
UE signalling
UE Hardware capability
Backward Compatibility Issues
Band specific work
Commercial implementaiton/deployment aspects

## Slide 4: Aspect 1: Signalling
RAN2 reserved bits for new channel BWs
channelBWs-DL and channelBWs-UL have 10 bits per SCS, used to indicate 5, 10, 15, 20, 25, 30, 40, 50, 60 and 80MHz
channelBWs-DL-v1590 and channelBWs-DL-v1590 have 16 bits
  For FR1, the leading/leftmost bit in channelBWs-DL-v1590 indicates 70MHz, and all the remaining bits in channelBWs-DL-v1590 shall be set to 0.
  channelBWs-DL-v1590 and channelBWs-DL-v1590 therefore have 15 spare bits to be used for new FR1 channel BWs
RAN2 could allocate one bit each for 35 and 45 MHz.
There is no signalling issue for adding 35 and 45 MHz Release-independent for Rel-15

## Slide 5: Aspect 2: Hardware capability
Implementation of new channel BWs may require new filter hardware in the UEs that support the new channel BWs and the gNBs that support the new channel BWs
Optional inclusion of 35 MHz and/or 45 MHz in new Rel-15 and 16 UEs won’t impact the hardware of legacy UEs or gNBs.
Since 45 MHz would be the widest channel BW for n25 and n66, it should be optional for Rel-17
New bands have hardware capability issues also, but are almost always release independent.
Conclusion: Hardware capability shouldn’t impact release independence

## Slide 6: Aspect 3: Backward compatibility issues
Adding the new channel BW doesn’t cause any backward compatibility issues
Compatibility Matrix | gNB does not support new CH BW | gNB supports new CH BW
UE does not support new CHBW(s) | Baseline functionality | UE doesn’t set new capability bit(s), so gNB treats the UE like any UE that doesn’t support a particular channel BW
UE supports new CHBW | gNB ignores the capability bits for the new channel BW(s) | UE can use the new channel BWs if deployed by the gNB

## Slide 7: Aspect 4: Band specific work
Some bands may have band specific work needed, like REFSENS, MSD, A-MPR, etc.
Adding legacy channel BWs to existing bands also can have band specific work like MSD, A-MPR, etc.
Band specific requirements can be established when the WID adds the bandwidth(s) for the particular and made backward compatible with earlier releases.

## Slide 8: Aspect 5: Commercial implementations/deployment aspects
Some vendors have expressed concerns about product plans already being in place for Rel-15 and Rel-16
If we make the new channel BWs optional for Rel-15 and Rel-16, then vendors can choose their own timeline for implementation.
RAN4 can decouple commercial implementation/deployment plans from release independence. This should give both sides the flexibility they need.
  If operators can convince vendors to implement the channel BWs in Rel-15 or Rel-16, great, otherwise they must wait until Rel-17 (or later).
  This approach would let the market decide when the new channel bandwidths are implemented in products, as is with new bands.

## Slide 9: Release independence on a case-by-case basis per band and bandwidth
Release independence is primarily a protocol issue. Since the signalling can support the new channel BWs, they can be release independent to Rel-15.
As we have seen, the discussion of release independence takes a lot of time and is contentious. Delegate time could be better spent on other issues instead of discussing release independence on a case by case basis per band and per bandwidth.
Having the new channel BWs be release independent on a case by case basis per band bandwidth would unnecessarily complicate TS 38.307
Vendors can choose to which release to implement the new channel BWs on a case-by-case basis per band and bandwidth

## Slide 10: Proposals
Proposal 1: 35 and 45 MHz channel bandwidths shall be release independent to Release 15
Proposal 2: 35 and 45 MHz shall be optional in Release 15 and Release 16
Proposal 3: 35 MHz shall be mandatory for Release 17 for n25 and n66. Since 45 MHz would be the widest channel BW for n25 and n66, and 45 MHz shall be optional for these bands in Release 17
Proposal 4: Any additional requests to add 35 and 45 MHz channel BWs to a band shall be added via this WID in Rel-17, not the basket WID.
Proposal 5: The 35 and 35 MHz WID will add a generic example band combination to be used as an example for future band combination requests
Proposal 6: CRs to turn channel BW table pages to landscape mode to allow for the inclusion of 35 and 45 MHz.
Proposal 7: MCC requested to configure band combination tables such that the header appears on each page to make the tables more readable.
Proposal 8: Send an LS to RAN2 asking them to allocate the signalling for 35 and 45 MHz from Rel-15.