## Slide 1: WF on 35MHz 45MHz REFSENS AMPR
Qualcomm, […]
­­­3GPP TSG-RAN WG4 Meeting # 97-e R4-2016864
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: 35MHz and 45MHz REFSENS
Comparison
Agree on UL config of 16RBs for n8, n71 for 35MHz BW??
Agreement for UL configuration for n3 and n25 45MHz BW.
Potential Agreement for UL configuration for n3 and n25 35MHz BW.
Other companies evaluate REFSENS for 20MHz UL/35MHz DL for n71/n8.
Re-evaluate REFSENS with agreed UL configuration.
REFSENS |  |  |  |  |  | 
Company | n3 |  | n25 |  | n8 | n71
 | 35M | 45M | 35M | 45M | 35M | 35M
QCOM | -85.2 | -80.2 | -81.7 | -68.9 | -69 | -69
SWKS |  |  |  |  | -66.3 | -66.3
MURATA | -86 | -84.2 | -85.4 | -70.7 | -62.2 | -67.6
AAPL |  |  |  |  | -62.3 | -62.5
MTK |  |  |  |  | -69.2 | -70.5
UL Config. 15K |  |  |  |  |  | 
Company | n3 |  | n25 |  | n8 | n71
 | 35M | 45M | 35M | 45M | 35M | 35M
QCOM | 50 | 50 | 45 [40] | 40 | 16 | 16
SWKS |  |  |  |  | 25 | 25
MURATA | 50 | 50 | 40 | 40 | 20 | 20
AAPL |  |  |  |  | 8 | 8
MTK |  |  |  |  | 20 | 20

## Slide 3: Issue 3-8: n7 35 MHz A-MPR
Potential agreement using inputs from Skyworks, Apple and Qualcomm
Skyworks/ Apple
Qualcomm
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <[2.7 or 3.42] | >0 | A4
 |  | ≥[2.7 or 3.42], <[15.84] | >max (0, 12*SCS*RBend –[3.06]) | A5
 |  | ≥[15.84], <[22.68] | >[12.6] | A6
 |  | ≥[22.68], <[28.8] | >[9.36] | A7
 |  | ≥[28.8] | >0 | A8
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <2.7 | >0 | A4
 |  | ≥2.7, <13.5 | >max (0, 12*SCS*RBend –2.7) | A5
 |  | ≥13.5, <23.76 | >9.0 | A6
 |  | ≥23.76, <29.52 | >9.0 | A7
 |  | ≥29.52 | >0 | A8
Potential Agreement
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <[3.42] | >0 | A4
 |  | ≥3.42], <[15.84] | >max (0, 12*SCS*RBend –[3.06]) | A5
 |  | ≥[15.84], <[22.68] | >[12.6] | A6
 |  | ≥[22.68], <[28.8] | >[9.0] | A7
 |  | ≥[28.8] | >0 | A8

## Slide 4: Issue 3-9: n25 and n66 NS_03 A-MPR
Tentative agreements
  Agree on the updated NS_03 requirement for 35MHz and 45MHz
  Agree to use same NS_03 AMPR for 35MHz and 45MHz as specified in TS38.101-1
Further study on equation-based requirement to account for future added bandwidths
ΔfOOB MHz | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  |  |  |  |  |  |  |  | Measurement bandwidth
 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 
± 0-1 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 % of channel BW
± 1-6 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 6-10 | -25 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 10-15 |  | -25 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 15-20 |  |  | -25 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 20-25 |  |  |  | -25 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 25-30 |  |  |  |  | -25 | -13 | -13 | -13 | -13 | 1 MHz
± 30-35 |  |  |  |  |  | -25 | -13 | -13 | -13 | 1 MHz
± 35-40 |  |  |  |  |  |  | -25 | -13 | -13 | 1 MHz
± 40-45 |  |  |  |  |  |  |  | -25 | -13 | 1 MHz
± 45-50 |  |  |  |  |  |  |  |  | -25 | 1 MHz

## Slide 5: Issue 3-10: n71/ n8 35 MHz
LB-LB ENDC combination issues
  Agree to limit the supported BW for DC_20A_n8A, DC_13A_n71A, and any future LB-LB combinations
  Or, specify RB position or added crossband noise MSD
Investigate Coexistence Issues
  Cases are n71 -> B29/B12
  Investigate RB restriction or AMPR with new NS flag for n71
  Consider 2 cases with symmetric and asymmetric UL/DL due to uncertainty of 35MHz UL
    20MHz UL, 35MHz DL
    35MHz UL, 35MHz DL
Further measurements and study to determine if large bandwidth is possible for n71 and n8.
  Option 1: ∆MPR not conclusive
  Option 2: ∆MPR = 1dB
Agree on NS_35 SEM requirement for n71 AMPR for 35MHz.
ΔfOOB (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  |  |  |  |  | Measurement bandwidth
 | 5 |  | 10 | 15 | 20 | 35 | 
± 0-0.1 | -15 |  | -18 | -20 | -21 | -23.5 | 30 kHz
± 0.1-6 | -13 |  | -13 | -13 | -13 | -13 | 100 kHz
± 6-10 | -251 |  | -13 | -13 | -13 | -13 | 100 kHz
± 10-15 |  |  | -251 | -13 | -13 | -13 | 100 kHz
± 15-20 |  |  |  | -251 | -13 | -13 | 100 kHz
± 20-25 |  |  |  |  | -251 | -13 | 100 kHz
± 25-35 |  |  |  |  |  | -13 | 100 kHz
± 35-40 |  |  |  |  |  | -25 | 1 MHz
 |  | NOTE 1: The measurement bandwidth shall be 1 MHz |  |  |  |  | 

## Slide 6: References
R4-2016600, “35M_45M AMPR, MPR, REFSENS”, Qualcomm Incorporated, 3GPP TSG-RAN WG4 #97-e, revised from R4-201473
R4-2015432, “REFSENS of n3, n8, n25 and n71 for new channel bandwidth”, Murata Manufacturing Co Ltd., 3GPP TSG-RAN WG4 Meeting # 97-e
R4-2015800, “Specification impact of additional 35&45MHz channel bandwidths”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016010, “n71 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016011, “n8 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016027, “n7 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016060, “Introduction of 35MHz and 45MHz regarding CA, DC, V2x combinations”, Ericsson, 3GPP TSG-RAN WG4 #97-e
R4-2016295, “Introduction of 35 MHz for n8, n66, n71 and 45 MHz for n66”, Apple Inc., 3GPP TSG-RAN WG4 #97-e
R4-2014186, “REFSENS of n8 and n71 for 35MHz channel bandwidth”, MediaTek Inc., 3GPP TSG-RAN WG4 #97-e
R4-2014911, “UE RF requirements tables with channel BW dependency”, Apple Inc., 3GPP TSG-RAN WG4 #97-e