## Slide 1: WF on the proposed operating bands for NR SL operation in FR1
AT&T, FirstNet, […]
­­­3GPP TSG-RAN WG4 Meeting # 97-e R4-2016923
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: Background
One of the objectives of the WI in [1] is to define the new sidelink frequency bands as noted below.
  4. Support of new sidelink frequency bands for single-carrier operations [RAN4]
    Support of new sidelink frequency bands should ensure coexistence between sidelink and Uu interface in the same and adjacent channels in licensed spectrum.
    The exact frequency bands are to be determined based on company input during the WI, considering both licensed and ITS-dedicated spectrum in both FR1 and FR2.

## Slide 3: Way Forward on Proposed Operating Bands for NR SL Operation in FR1
In order to align with the objective in the WI, the following items are adopted
  Based on Operator input, RAN4 specifies the operating bands for SL operation in FR1 including candidate public safety spectrum as part of the WI in [1]
    Before specifying the operating bands, RAN4 can study for co-existence evaluation if needed shall study and conclude on the co-existence scenario between Uu and SL for licensed bands
  RAN4 to collect Operator input for new SL operating bands in FR1 for public safety service
    Requests based on input papers from Operators with justification
    Cut-off for requests to be defined in the Work Plan in [2]
  Future NR SL operating bands for FR1 after Rel-17 cut-off can be managed with the basket WI approach

## Slide 4: Initial NR Operating Band Requests for FR1
NR Band n14
  Operator Request
    R4-2016464 [3], NR Sidelink Operating Bands, AT&T, FirstNet
  NR Band n14 is dedicated for first responder communications in the United States.
  NR Band n14 is included as one of the NR sidelink licensed operating bands in FR1
    Some additional information can be provided for SL operation in n14 by RAN4 #98-e
      PC1 or PC3 for SL operation or both PC1 & PC3 in n14
      Is there any legacy Uu operation in n14 or B14?
Others …

## Slide 5: References
RP-201516, “WID revision: NR sidelink enhancement”, LG Electronics, 3GPP TSG-RAN Meeting # 89-e
R4-2016924, “Work plan for NR sidelink enhancement in Rel-17”, LG Electronics, 3GPP TSG-RAN WG4 #97-e
R4-2016464, “NR Sidelink Operating Bands”, AT&T, FirstNet, 3GPP TSG-RAN WG4 #97-e