## Slide 1: WF on RRM test cases for power saving
Agenda Item: 7.6.2
Document for: Approval
Source: CATT
3GPP TSG-RAN WG4 #97e R4-2017133
Electronic Meeting, 2-13 Nov, 2020

## Slide 2: Background
In the references [1][2][3][4][5][6][7], companies provide their views of how to design the RRM test cases for power saving

## Slide 3: Way forward
Use separate tests for each criterion (low mobility/not-at-cell-edge)
Different priority frequency layers coexist in the same test for different priority frequency layers
Exclude high priority layer cell search for inter-frequency/inter-RAT
[TBD: Design two-rounds (to and back) cell reselection process for inter-frequency/inter-RAT in power saving test cases]
UE gain in FR2 should be considered. [TBD: leave the threshold impacted by G as [TBD] and discuss it in the next meeting]
SSearchDeltaP = [TBD] dB. [TBD: 3dB for FR1 and SSearchDeltaP = 6dB for FR2]
SSearchThresholdP = Srxlev – [TBD] dB [TBD: For FR1, X>4.5 while for FR2, X>6]
Exclude the cell search process from test repetition
Use shorter DRX cycle to improve test efficiency: DRX = [TBD] s TSI-NR = [TBD] s

## Slide 4: References
[1] R4-2014370
[2] R4-2014409
[3] R4-2014657
[4] R4-2014835
[5] R4-2015483
[6] R4-2016147
[7] R4-2016149