# 3GPP TSG-RAN WG4 Meeting #97-e                            R4-2017267

# Electronic Meeting, 2-13 Nov., 2020

Agenda Item:	12.6.1

Source: 	CMCC

Title: 			 Work plan for enhancement for NR high speed train scenario in FR1

Document for:	Approval

# Introduction

This contribution provides work plan for enhancement for NR high speed train scenario in FR1.

# Work plan for RRM part

According to the WID [1], the core part of RRM shall be finalized by Sep.2021 (RAN #93), the performance part of RRM shall be finalized by Mar.2022 (RAN #95).

RAN4#97-e

- Discuss and approve the work plan for RRM part.

RAN4#98-e

- Discuss and identify which RRM requirements need to be enhanced to support carrier aggregation with the target speed of up to 500km/h and carrier frequency of up to 3.6 GHz

  - PSS/SSS detection, time index detection, and measurement period for deactivated SCell

  - PSS/SSS detection, time index detection, and measurement period for activated SCell

  - SCell activation/deactivation delay requirement

  - If needed other requirements are not precluded.

- Discuss the candidate solution for the RRM enhancement

RAN4#98-e-Bis

- Continue to discuss the solution for the RRM enhancement

- Discuss the possible signaling impact (e.g. UE capabilities, network flag)

RAN4#99-e

- Continue to discuss and decide the solution for the RRM enhancement

- Provide draft CR on TS38.133 for the RRM enhancement

- Discuss and agree on the possible signaling impact (e.g. UE capabilities, network flag) and send LS to RAN2

RAN4#100-e

- Approve the CR on TS38.133 for RRM enhancement

RAN4#100-e-Bis (RRM performance part only)

- Discuss and decide test case lists and related parameters

- Discuss and specify the measurement accuracy

RAN4#101-e (RRM performance part only)

•	Provide draft CR on TS38.133 for RRM enhancement

RAN4#102-e (RRM performance part only)

•	Approve the CR on TS38.133 for RRM enhancement

# Work plan for demodulation part

According to the WID [1], the demodulation part shall be finalized by Mar.2022 (RAN #95).

RAN4#97-e

- Discuss and approve the work plan for demodulation part.

RAN4#98-e

- CA scenario

  - Discuss the demodulation performance enhancement to support carrier aggregation with the target speed of up to 500km/h and carrier frequency of up to 3.6 GHz for HST-SFN conditions

- Enhanced transmission schemes for NR HST demodulation

  - Study whether to specify the PDSCH requirements for transmission scheme 2 (PDSCHs are transmitted from two or more adjacent TRPs scheduled by multi-DCI)

RAN4#98-e-Bis

- CA scenario

  - Continue discuss the demodulation performance enhancement to support carrier aggregation with the target speed of up to 500km/h and carrier frequency of up to 3.6 GHz for HST-SFN conditions

  - Discuss the initial simulation assumption for demodulation performance enhancement for CA

- Enhanced transmission schemes for NR HST demodulation

  - Continue study whether to specify the PDSCH requirements for transmission scheme 2 (PDSCHs are transmitted from two or more adjacent TRPs scheduled by multi-DCI)

- Discuss the possible signaling impact (e.g. UE capabilities, network flag)

RAN4#99-e

- CA scenario

  - Continue discuss the demodulation performance enhancement to support carrier aggregation with the target speed of up to 500km/h and carrier frequency of up to 3.6 GHz for HST-SFN conditions

  - Provide initial simulation results for demodulation performance enhancement for CA

- Enhanced transmission schemes for NR HST demodulation

  - Continue study and decide whether to specify the PDSCH requirements for transmission scheme 2 (PDSCHs are transmitted from two or more adjacent TRPs scheduled by multi-DCI)

  - If it is decided to specify the PDSCH requirements for transmission scheme 2, discuss the simulation assumption for alignment

- Discuss and agree on the possible signaling impact (e.g. UE capabilities, network flag) and send LS to RAN2

RAN4#100-e

- CA scenario

  - Decide demodulation performance enhancement to support carrier aggregation with the target speed of up to 500km/h and carrier frequency of up to 3.6 GHz for HST-SFN conditions

  - Discuss and decide the simulation assumption for alignment

- Enhanced transmission schemes for NR HST demodulation

  - If it is decided to specify the PDSCH requirements for transmission scheme 2, discuss and decide the simulation assumption for alignment

RAN4#100-e-Bis

- CA scenario

  - Provide the simulation results for alignment for demodulation performance enhancement for CA

- Enhanced transmission schemes for NR HST demodulation

  - Provide the simulation results for alignment for the PDSCH requirements for transmission scheme 2

RAN4#101-e

- CA scenario

  - Provide the simulation results with impairment for demodulation performance enhancement for CA

  - Provide draft CR for demodulation performance enhancement for CA

- Enhanced transmission schemes for NR HST demodulation

  - Provide the simulation results with impairment for the PDSCH requirements for transmission scheme 2

  - Provide draft CR for the PDSCH requirements for transmission scheme 2

RAN4#102-e

- CA scenario

  - Approve CR for the demodulation performance enhancement for CA

- Enhanced transmission schemes for NR HST demodulation

  - Approve CR for the PDSCH requirements for transmission scheme 2

# Conclusion

This contribution provides work plan for enhancement for NR high speed train scenario in FR1.

# Reference

[1] RP-202106, New WID on enhancement for NR high speed train scenario in FR1, CMCC