## Slide 1: WF on NTN solutions
Moderator, THALES

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [97e][312] NTN_Solutions”
See R4-2017630

## Slide 3: Content
Topic #1: General RAN4 use cases related aspects
Topic #2: System NTN RF core requirements
Topic #3: FR1 proposed Exemplary Frequency band for NTN
Topic #4: FR2 proposed Exemplary Frequency band for NTN
Topic #5: Exemplary Frequency band for HAPS/HIBS
Topic #6: RAN4 Proposed RF core requirements

## Slide 4: Summary
List of proposals for each topics discussed
In “agreements” part
  Proposals with “green” comments are agreeable.
In “open issues” part
  Proposals with “purple” comments not agreeable.
  Proposals with “orange” comments not agreeable:
    Please also note that the “orange” comments are hints towards possible agreements.
  Proposals without any comment were not discussed

## Slide 5
Agreements

## Slide 6: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should consider all the relevant sources (including but not limited to ITU-R Radio Regulations, relevant national regulations, pre-existing Harmonized Standards developed for example in ETSI, coexistence studies approved by regulatory bodies and/or 3GPP specifications) in order to specify NTN RF requirements.
  no concerns raised so far
RAN4 should select appropriate exemplary bands for NTN and to carry the needed adjacent channel coexistence studies in order to specify NTN RF requirements.
  no concern raised so far
Select exemplary bands before going to the detail of RF core requirements.
  no concern raised so far

## Slide 7: Topic #1: General RAN4 use cases related aspects (cont’d)
3GPP RAN4 should provide/conduct relative independent adjacent channel coexistence studies to develop RF requirements for NTN.
  no concern raised so far
NTN RF requirements shall be specified assuming no impact on TN RF requirements.
  no concern raised so far
For coexistence studied, both NTN/NTN and NTN/TN in adjacent channels should be considered.
  no concern raised so far
RAN4 need to consider how to take into account the heterogeneous cell patterns of NTN and TN networks assuming that they serve the same areas.
  no concern raised so far

## Slide 8: Topic #1: General RAN4 use cases related aspects (cont’d)
For exemplary band in FR1, RAN4 should consider at least satellite scenarios C1.1, C2.1 (LEO Earth Fixed Beams and Earth Moving Beams) and A1 (GEO):
  C1.1: LEO @ 600 km altitude, FR1, Earth fixed beams
  C2.1: LEO @ 600 km altitude, FR1, Earth moving beams
  A1: GEO @ 35,786 km altitude, FR1, Earth fixed beams
  no concern raised so far
Further include following scenarios:
  C1.2: LEO @ 1200 km altitude, FR1, Earth fixed beams
  C2.2: LEO @ 1200 km altitude, FR1, Earth moving beams
  no concern raised so far
Use TR 38.821 as a baseline/starting point, as long as HAPS is still included, and NTN study aligns with WID in RAN.
  no concern raised so far

## Slide 9: Topic #1: General RAN4 use cases related aspects (cont’d)
Further discuss if and which HAPS scenarios should be considered by RAN4 as part of the WI NR-NTN-solutions.
  no concern raised so far
TSG-RAN to decide the change from “HAPS” to “HIBS” in the NTN WI
  no concern raised so far
ATG is to be considered for separate WI by RAN.
  no concern raised so far

## Slide 10: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should consider both Earth fixed beam & Earth moving beam.
  no concern raised so far
The simulation scenarios shall be defined based on the permutation and/or combination between NTN/TN or NTN/NTN scenarios.
  no concern raised so far
Networks layout (cell coverage for NTN and TN) and NTN UEs distribution would need to be further aligned.
  no concern raised so far
Further discuss simulation assumptions and the down selection of scenarios for the coexistence studies.
  no concern raised so far

## Slide 11: Topic #2: System NTN RF core requirements
Interfaces between different NTN entities should be clarified.
  no concern raised so far
Do not consider the feederlink from the RAN4 RF perspective in NTN Release-17.
  no concerns raised so far

## Slide 12
Open issues
This includes issues for which no agreement could be reach during #97-e
for which discussion is postponed to next meetings

## Slide 13: Topic #1: General RAN4 use cases related aspects (cont’d)
At least one exemplary frequency band per FR1 should be defined for satellite.
  Still discussion on replacement of “At least” by “Only”
At least one exemplary frequency band per FR2 should be defined for satellite.
  Proposal not agreeable
It may be possible to consider an exemplary band (with similar usage conditions as FR2 band) for which UL or DL or both can be below 24.25GHz.
Although RAN4 will select exemplary band(s) in the current NR-NTN-solutions WI, the definition of additional NR bands for satellite will be part of dedicated RAN4 led Release-17 work items.
  Alternative proposal : “Although RAN4 will select exemplary band(s) in the current NR-NTN-solutions WI, the definition of additional NR bands for satellite can be part of dedicated RAN4 led work items based on TSG-RAN’s decision.”
The frequency ranges considered for satellite should be spectrum allocated by ITU to satellite services should be considered.
  Alternative proposal: “Spectrum allocated by ITU to mobile satellite services shall be considered”

## Slide 14: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN4 should further discuss and decide ACS & ACLR requirements to be considered for TN in the coexistence study with NTN, depending on FR and BW configuration.
  Upon clarification request, Moderator suggest alternative proposal “For the purpose of simulations for the coexistence study between TN & NTN, the TN BS/UE ACLR & ACS parameters need to be further discussed. It may depend on FR and BW configuration”
Further discuss the frequency reuse factor to be considered for the coexistence studies (which could be FR specific).
No impact on IMT network is a pre-requisite.
  Alternative proposal: “No impact on IMT specification is a pre-requisite”

## Slide 15: Topic #1: General RAN4 use cases related aspects (cont’d)
RAN-WG4 may consider the definition of additional NR bands for HAPS as part of dedicated RAN4 led Release-17 work items.
  Proposal not agreeable: More discussion required about HAPS definition and bands
LS to RAN plenary for guideline and the accurate definition for HAPS.
  Proposal not agreeable: One company commented no need to send any LS if the WI is proposed for update in next RAN meeting.
  No need to send LS if discussion for WID update in RAN plenary.

## Slide 16: Topic #1: General RAN4 use cases related aspects (cont’d)
Down-select from a list with approx. 70 coexistence cases (x 2 Frequency Ranges) x 2 scenarios (Earth Fixed Beam, Earth Fixed Beam) x 3-4 BW configurations, from:
Consider only NTN extreme cases e.g. 1 worst case and 1 best case (in terms of Doppler, received power) for x2 type of configurations (Earth Fixed Beam, Earth Moving Beam) x 3-4 BW configurations.
 |  |  | Set 1 |  |  |  | Set 2 |  |  | 
 |  |  | GEO | LEO 600km | LEO 1200km | HIBS | GEO | LEO 600km | LEO 1200km | HIBS
NR / NB-IoT | Rural |  | X | X | X | X | X | X | X | X
 | Urban macro |  | X | X | X | X | X | X | X | X
 | Dense Urban |  | X | X | X | X | X | X | X | X
 | Micro/small cell outdoor |  | X | X | X | X | X | X | X | X
 | Indoor hotspot |  | X | X | X | X | X | X | X | X
NTN | GEO | Set 1 | X | X | X | X | N/A | N/A | N/A | N/A
 | LEO 1200km |  | X | X | X | X | N/A | N/A | N/A | N/A
 | LEO 600km |  | X | X | X | X | N/A | N/A | N/A | N/A
 | HIBS |  | X | X | X | X | N/A | N/A | N/A | N/A
 | GEO | Set 2 | N/A | N/A | N/A | N/A | X | X | X | X
 | LEO 1200km |  | N/A | N/A | N/A | N/A | X | X | X | X
 | LEO 600km |  | N/A | N/A | N/A | N/A | X | X | X | X
 | HIBS |  | N/A | N/A | N/A | N/A | X | X | X | X

## Slide 17: Topic #1: General RAN4 use cases related aspects (cont’d)
“At least for FR1, RAN4 shall consider Handheld UE & VSAT UE with described characteristics:
  Handheld: Omnidirectional antenna, 500 km/h (e.g. on board a high speed train), Linear: +/-45°X-pol, up to 200 mW (UE power class 3)
  VSAT: Directive antenna (up to 60 cm equivalent aperture diameter), Up to 1200 km/h (e.g. mounted UE on a building or moving platforms, e.g., aircrafts, trains, vessels or vehicles. Examples of such UE can be ESIM and VSAT), Circular polarisation, up to 20 W Tx power.”
  Alternative proposal : Remove “ESIM and”.
“Further discuss other UE-types to be considered for FR1 & FR2”.
  Alternative proposal : Remove “& FR2”.
Use 3GPP TS 38.101-1 and 38.101-2 for NTN RF UE requirements.
  Alternative proposal : Remove “and 38.101-2”.

## Slide 18: Topic #1: General RAN4 use cases related aspects (cont’d)
Further discuss “worst case” scenarios in terms of orbit, transmission power, coexistence and Doppler.
FFS the down selection of TR 38.821 scenarios for satellite specific parameters.
For some selected UE RF parameters, it is expected to adopt similar values (e.g. for REFSENS, Tx Power) for NTN to ensure operational compatibility across NTN and TN.
  Proposal not agreeable: Unknown for the time being.
Possible adaptations based on the co-existence studies outcomes (NTN with TN or NTN with NTN) may be considered for NTN RF BS requirements.
  Proposal not agreeable: 2 companies disagree.
Impacts between moving and fixed beam on coexistence study should be clarified. Further discussions are required to identify the respective impact on RF requirements and simulation assumption for Earth fixed beam & Earth moving beam.

## Slide 19: Topic #2: System NTN RF core requirements
Consider NTN Payload+NTNGW as a single entity (e.g. Repeater or Remote Radio Head).
  Alternative proposal: “Consider NTN Payload + feederlink + NTNGW as a single entity (e.g. Repeater or Remote Radio Head)”
Consider only the service link from the RAN4 RF perspective in NTN Release-17.
  Proposal not agreeable: To be further discussed. One company shows interest to clarify NTNGW-gNB interface.
Consider only “BS” RF requirements on the service link i.e. at satellite output for DL and at satellite input for UL.
  Proposal not agreeable: Further discussion required for the interface between NTNGW and gNB.

## Slide 20: Topic #2: System NTN RF core requirements
Further clarify (taking into account coexistence studies) if NTN BS RF parameters could be adapted with respect to TN BS RF values due to specific deployment and operational constraints.
Further clarify (taking into account coexistence studies) if NTN UE RF parameters could be adapted or if additional NTN UE Rx parameters are required. For some selected UE RF parameters, it is expected to adopt same TN values (e.g. for REFSENS, Tx Power) for NTN to ensure operational compatibility across NTN and TN.
RAN4 need to consider NTN-gateway, satellite and gNB is a single component (transparent payload case).

## Slide 21: Topic #3: FR1 proposed Exemplary Frequency band for NTN
Band characteristics (e.g. available BW, UL/DL configuration, maximum configurable BW size, coexistence conditions) of the candidate bands should be considered for comparison purposes. Note that views from operators should be taken into account in priority.
  Proposal not agreeable: further discuss criteria to be used (if any criteria) at RAN4#98e
Agree channel BW size once the exemplary band is selected (and in accordance with the selected exemplary band(s)).

## Slide 22: Topic #4: FR2 proposed Exemplary Frequency band for NTN
Candidate FR2 exemplary band
  Consider an exemplary band which is partially FR2 (i.e. only UL is FR2 OR only DL is FR2).
  RAN4 to use as exemplary band of 17.7 – 20.2 GHz for DL and 27.5 – 30.0 GHz for UL with FDD mode.
  RAN4 should consider coexistence scenarios NTN FDD with TN TDD in adjacent bands.
    Several companies showed disagreement for coexistence scenarios NTN FDD with TN TDD in adjacent bands in FR2.
Candidate FR2 band configurations
  Select the channel BW sizes to be considered for in accordance with the selected exemplary band(s).

## Slide 23: Topic #5: Exemplary Frequency band for HAPS/HIBS
Too early to discuss, postponed to RAN4#98e
Candidate HAPS/HIBS exemplary bands
  LS to RAN plenary for guideline and the accurate definition for HAPS, and HAPS frequency bands.
  Leave this topic for FFS.
Candidate HAPS/HIBS band configurations
  Further discuss on HAPS BW configuration for FFS

## Slide 24: Topic #6: RAN4 Proposed RF core requirements
RAN4 shall define NTN UE RF requirements based on existing UE RF requirements (specified in TS 38.101-1 and 38.101-2).
  Alternative proposal : Remove “and TS 38.101-2”
  38.101-2 cannot be reused as baseline for FDD NTN UE;
Continue discussion with respect to potential NTN UE RF requirements that might be different from TN UE RF.
  Proposal not agreeable: too early for such proposal.
Continue discussion with respect to NTN UE RF parameters (e.g. REFSENS, Maximum Transmitted Power) that should be kept the same as for TN, in order to allow operational compatibility across NTN and TN.
  Proposal not agreeable: Coexistence study and technical analysis required before