## Slide 1: Way Forward on NR-U PUCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, 2 - 13 November 2020
Agenda: 7.1.8.3
R4-2017467
Document for: Approval

## Slide 2: Background
R4-2012542, Email discussion summary for [96e][328] NR_unlic_Demod
R4-2012611, Way Forward on NR-U BS demodulation requirements, Ericsson

## Slide 3: General test configurations
PUCCH formats
  Define the performance requirements for Rel-16 PF 0/1/2/3 with interlace resource allocation
Number of interlaces
  1 interlace for PF 0/1/2/3
Antenna configuration
  1Tx2Rx
Bandwidth
  Define the NR-U PUCCH requirements with 20MHz bandwidth
Frequency hopping
  Not configure frequency hopping
SCS
  Option 1: 30kHz
  Option 2: 15 kHz and 30 kHz
Propagation conditions
  Option 1: TDLA30-10
  Option 2: TDLC300-100

## Slide 4: PUCCH format 0
Parameter | Test
Number of UCI information bits | 1
Number of symbol | 1
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 13
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Test metric | SNR@ SNR@
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Parameter | Test
Number of UCI information bits | 1
Number of symbol | 1
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 13
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Number of symbols
  Only test 1 OFDM symbol for PF0
Test metric
  Option 1: Only Rel-15 PF0 test metric will be used
  Option 2: 3 test metrics will be used
    SNR @Prob(PUCCH DTX→Ack bits) ≤ 10^(−2)
    SNR@Prob(ACK miss)≤10^(−2)
    SNR@Prob(NACK→ACK)≤10^(−3)

## Slide 5: PUCCH format 1
Parameter | Test
Number of information bits | 2
Number of symbols | 14
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 0
Index of orthogonal cover code (timeDomainOCC) | 0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Test metric | SNR@ SNR@
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Parameter | Test
Number of information bits | 2
Number of symbols | 14
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Initial cyclic shift | 0
First symbol | 0
Index of orthogonal cover code (timeDomainOCC) | 0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz if agreed and RBs 0,5,10,…,50 are allocated for 30kHz. | 

## Slide 6: PUCCH format 2
Number of interlaces
  One interlace
Number of OFDM symbols
  One OFDM symbol
Information bits
  Option 1: 4 bits or 22 bits
  Option 2: 22 bits
OCC configuration
  Option 1: Not configure
  Option 2: OCC length n2
Parameter | Value
Modulation order | QSPK
Intra-slot frequency hopping | N/A
Number of symbols | 1
The number of UCI information bits | Option 1: 4 bits or 22 bits Option 2: 22 bits
First symbol | 13
DM-RS sequence generation | NID0=0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note 1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
OCC-Length-r16 | Option 1: Not configured Option 2: n2
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz and RBs 0,5,10,…,50 are allocated for 30kHz. | 
Parameter | Value
Modulation order | QSPK
Intra-slot frequency hopping | N/A
Number of symbols | 1
The number of UCI information bits | Option 1: 4 bits or 22 bits Option 2: 22 bits
First symbol | 13
DM-RS sequence generation | NID0=0
Antenna configuration | 1T2R
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Number of interlaces | 1
Interlace index | 0 Note 1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
OCC-Length-r16 | Option 1: Not configured Option 2: n2
Test metric | 
Note 1: RBs 0, 10, 20,…,100 are allocated for 15kHz and RBs 0,5,10,…,50 are allocated for 30kHz. | 

## Slide 7: PUCCH format 3
Number of interlaces
  One interlace
information bits
  Option 1: 16
  Option 2: 16 and 4 (4 for 14 os)
Number of OFDM symbols
  Option 1: Both 4 and 14
  Option 2: 4
  Option 3: 14
OCC length
  Option 1: n1
  Option 2: n2
  Other values are not precluded.
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | Option 1: both 4 and 14 Option 2: 4 Option 3: 14
The number of UCI information bits | Option 1: 16 Option 2: 16 and 4 (4 for 14 os)
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Index of OCC | n0
Length of OCC | Option 1: n1 Option 2: n2
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. | 
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | Option 1: both 4 and 14 Option 2: 4 Option 3: 14
The number of UCI information bits | Option 1: 16 Option 2: 16 and 4 (4 for 14 os)
Channel bandwidth | 20MHz
SCS | [15kHz]; 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | Option 1: TDLC300-100 low Option 2: TDLA30-10
Index of OCC | n0
Length of OCC | Option 1: n1 Option 2: n2
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. |