## Slide 1: 3GPP TSG-RAN WG4 Meeting #97-e Electronic Meeting, 2nd – 13th Nov, 2020
Huawei, HiSilicon
Way forward on NR-U BS demodulation requirements for general part and PUSCH
R4-2017466

## Slide 2: Background
R4-2012611, Way Forward on NR-U BS demodulation requirements, RAN4#96-e, Ericsson

## Slide 3: General part

## Slide 4: Test scenarios
Only define BS performance requirements for single carrier for both licensed CC (reuse the existing NR Rel-15 requirements) and unlicensed CC
No specific requirements and tests will be defined for scenario B
RAN4 will introduce Test cases/requirements for both scenario A and scenario C
  Define one set of test cases for Scenarios A and C, i.e. one set of requirements for unlicensed CC for Scenario A and C
How to reuse NR Rel-15 performance requirements for licensed CC for Scenario A
  Option 1: Reuse all applicable requirements during the selection of the largest aggregated bandwidth for testing, i.e. consider CA for licensed CCs.
  Option 2: Reuse one applicable requirements defined for one specific bandwidth for testing, such as 20MHz, i.e. only consider single carrier for licensed CC
Bandwidth for performance requirements definition for unlicensed carrier
  Option 1: Define the requirements for single carrier with 20MHz only with the test applicability rule that a BS only has to perform tests for the largest supported bandwidth based on BS vendor’s declaration.(Ericsson, Samsung)
  Option 2: Define the requirements for single carrier with 20MHz,40MHz,60MHz and 80MHz, with the test applicability rule that a BS only has to perform tests for the largest supported bandwidth based on BS vendor’s declaration.(Nokia, Huawei)

## Slide 5: Test Scenarios
Test applicability
  The tests should apply based on BS declaration of supporting Scenario A and/or Scenario C
  If BS declares to support both Scenario A and Scenario C
    Option 1: BS only needs to pass the requirements for Scenario A that include performance requirements for both licensed CC(s) and unlicensed CC(s)
    Option 2: BS only tests the performance requirements for unlicensed CC(s)
How to handle Rel-15 test requirements for BS supporting NR-U
  Option 1: Consider a minimum subset of Rel-15 test cases for NR-U scenario and define proper applicability rules for these requirements. (Ericsson)
  Other options not precluded

## Slide 6: Others
Define requirements that are agnostic to wideband operation 1 and 2
Not consider LBT model for NR-U BS performance requirements definition
Always schedule PRBs between 2 contiguous LBT sub-bands during the test, i.e. not configure guard band

## Slide 7: PUSCH

## Slide 8: PUSCH
Waveform: CP-OFDM
Number of interlace: One interlace
Interlace allocation per slot:
  Option 1: Single interlace that is same for all slots (Nokia, Huawei, Intel)
  Option 2: Single interlace with 10 PRBs that is different per slot. (Ericsson).
    Take following method as an example:
      Frequency domain PRB allocation: single interlace with 10 PRBs in each slot N
      15kHz SCS: N, N+10, N+20, …, N+90, where N=0, 1, 2, …, 9
      30kHz SCS: N, N+5, N+10, …, N+45, where N=0, 1, 2, …, 5
SCS
  Option 1: Both 15kHz and 30kHz
  Option 2: Only 30kHz
Test applicability rule for different SCS (if 15kHz SCS agreed)
  Test performance requirements for 15kHz and/or 30kHz SCS based on BS declaration
  If BS declares to support both 15kHz and 30kHz
    Option 1: Only test performance requirements for 15kHz SCS
    Option 2: Only test performance requirements for 30kHz SCS
    Option 3: Test performance requirements for both 15kHz and 30kHz SCS

## Slide 9: PUSCH
TDD pattern:
  7D2S1U S=6D:4G:4U for 30kHz SCS
  3D1S1U for 15kHz SCS (if 15kHz SCS agreed)
PUSCH mapping type
  Option 1: Only Type A (Ericsson, Huawei)
  Option 2: Only Type B (Ericsson, Samsung, Huawei)
  Option 3: Both Type A and Type B (Nokia)
Number of scheduled symbols for PUSCH transmission: 14 symbols per slot
DM-RS configuration:
  DM-RS configure type 1 with single-symbol and dmrs-AdditionalPosition ‘pos1’
  DM-RS symbol: #2 and #11
MCS
  Option 1: MCS 11(16QAM, R=378/1024) (Huawei)
  Option 2: MCS 2 (QPSK, R=193/1024) and MCS 16 (16QAM, R= 658/1024) (Nokia, Samsung, Intel)
  Option 3: MCS 20 for TDLA30-10. FFS:16 for TDLC300 and 2 for TDLB100 (Ericsson)
Antenna configuration: 1x2
Propagation condition:
  TDLA30-10 as baseline
  FFS additional TDLB100 and TDLC300

## Slide 10: PUSCH
Maximum number of HARQ transmission
  Option 1: 4
  Other options not precluded
RV sequence
  Option 1: 1 bit {0,2,0,2}
  Option 2: 2 bits {0,2,3,1}
Test metric for PUSCH performance requirements:
  SNR@70% max throughput
Performance requirements for CG-UCI multiplexed on PUSCH with interlace allocation
  Option 1: Not introduce
  Option 2: Introduce performance requirements for CG-UCI multiplexed on PUSCH with interlaced resource allocation and without HARQ-ACK, CSI part 1 and CSI part 2 (Huawei, Nokia)
  Option 3: Consider introduce a Rel-15 requirement for HARQ-ACK multiplexing on PUSCH with more than 2 HARQ-ACK information bits and using it to cover CG-UCI multiplexing on CG-PUSCH in NR-U scenario with proper applicability rule. (Ericsson, Nokia)