## Slide 1: Way forward on CA CQI reporting requirements
China Telecom
3GPP TSG-RAN4 Meeting #97e
Electronic Meeting, 2-13 Nov., 2020
Agenda item: 7.16.1.4
draftR4-2017573
Document for: Approval

## Slide 2: Background: WF in previous meetings
RAN4 #94e-Bis
  WF: R4-2005548
  RAN4 #95e
  WF: R4-2008849
  RAN4 #96e
  WF: R4-2012692

## Slide 3: Test Parameters
Duplex mode and SCS combinations
  For the performance requirements:
    FR1: FDD + FDD with 15 kHz SCS, TDD + TDD with 30 kHz SCS, FDD 15 kHz +TDD 30kHz
    FR2: TDD + TDD with 120 kHz SCS
  Test applicability rule for performance requirements definition:
    Test 2 cases for FR1
      Test #1: FDD 15 kHz + TDD 30 kHz > FDD 15 kHz + FDD 15 kHz
      Test #2: TDD 30 kHz + TDD 30 kHz
  Pcell configuration for FDD 15 kHz +TDD 30kHz
    Option 1: Configure both FDD 15kHz as Pcell and TDD 30kHz as PCell. (Ericsson)
    Option 2: (HW)
      Pcell configuration for performance requirements
      Define requirements for both FDD 15kHz Pcell and TDD 30kHz Pcell
      Pcell configuration for the test
      The test coverage can be considered fulfilled if UE passes any one of scenario with one of the CC as PCell for FDD 15 kHz + TDD 30 kHz and FDD 15 kHz + FDD 15 kHz
      If Pcell in both carriers are supported for FDD 15 kHz + TDD 30 kHz, configure TDD 30 kHz cell as Pcell

## Slide 4: Agreements in previous meetings #1
Parameter | Value
Propagation condition | AWGN
TDD pattern | For 30kHZ SCS: 7D1S2U with S=6:4:4 For 120kHZ SCS, 2D1S1U with S=11:3:0
CSI reporting type | Periodic
CSI reporting periodicity | For 15kHz SCS: 5 slots For 30kHz SCS: 10 slots For 120kHz SCS: 8 slots
Antenna configuration | 1T2R and 1T4R for FR1, and 1T2R for FR2
Signal power density for 2Rx and 4Rx requirements | For 4Rx requirements, reduce the signal power density by 3dB compared to that for 2Rx.
CQI Table | For FR1: CQI Table 2 For FR2: CQI Table 1
Test metric general principle | Following the methodology used in LTE, the difference between the wideband CQI indices of Pcell and the first Scell as well as the difference between the wideband CQI indices of the first Scell and the other Scell(s) (if any) shall be not smaller than a threshold, for more than 90% of the time
SNR configuration | For 2DL CA CQI test: SNRPcell = 10dB and SNRScell = 4dB for FR1 and FR2 For 3 or more DL CA CQI test: SNRPcell = 12dB, SNRScell1 = 6dB, SNRScell2, 3,… = 0dB for FR1 and FR2
Delta CQI threshold | thr = 2 for 2 or more DL CA in FR1 and FR2

## Slide 5: Agreements in previous meetings #2
    Channel bandwidth and test applicability rule
  Define CA CQI performance requirements in a bandwidth agnostic way
  For the test applicability rule, use the following
    For each agreed duplex mode and SCS combination for testing
      CA capability where the tests apply: Test any of one of the supported CA capabilities with largest aggregated CA bandwidth combination
      CA configuration from the selected CA capability where the tests apply: Test any one of the supported CA configurations with largest aggregated CA bandwidth combination