## Slide 1: WF on FR2 MIMO OTA simulation assumption
Huawei, HiSilicon, []
R4-200XXXX
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: Background
In WF[1], it is agreed:
  For FR2, simulation approach to define performance requirement is not precluded
    Workplan including detailed simulation assumptions for FR2 simulation campaign need to be defined

## Slide 3: FR2 MIMO OTA simulation assumptions
FR2 MIMO OTA simulation assumptions should take TR 38.827 as baseline, following items still need further alignment in detail for simulation:
Assumption Items | Current status in TR 38.827 | Proposals in RAN4 #97-e | Note
BS antenna beamforming configuration | A code book of 128 fixed beams is constructed to a grid of eight elevation angles from –25 to +25 with ~7.1 step size and 16 azimuth angles from –60 to +60 with 8 step size | 1 strongest transmitting beam out of the 128 beam fixed beam grid is selected for each FR2 channel model, i.e. beam in the boresight direction | 
The direction of Strongest beam from BS | 1 strongest transmitting beam is generated from BS, the direction of this beam towards the strongest cluster of each FR2 channel model. | Rotate the BS antenna array so that the direction of the strongest beam towards the strongest cluster, i.e. Cluster #6 in UMi CDL-C, Cluster #2 in InO CDL-A. | 
Clusters used in chamber for each Channel Model | Not clear | choose 3 or 4 strongest clusters after BS pattern filtering for each channel model that the BS strongest beam toward to , i.e. 3 clusters for CDL-A as cluster #2 #3 #4, 4 clusters for CDL-C as cluster #6 #7 #8 #2 | 
PSP for simulation | PSP validation measurements procedure is provided Target PSP for validation is FFS Not clear how to simulate on PSP validation | compared between above strongest clusters radiated from 6 probes and ideal PAS from the 3 or 4 strongest clusters. | How to emulate PSP in simulation? What is target PSP for simulation
UE antenna array | N/A | antenna array type can be 2x2 patches or 1x4 patches two or three panels is assumed others implementation scenarios are not precluded | 
Companies are encouraged to provide views on above simulation assumptions
  other aspects are not precluded if necessary

## Slide 4: Reference
[1] R4-2012707 “WF on NR MIMO OTA”, vivo, CAICT, Spirent
[2] R4-2017428 “email discussion summary for 97e MIMO OTA ”, CAICT
[3] R4-2014829 “Proposal of FR2 MIMO OTA simulation approach workplan”, MediaTek
[4] R4-2016539 “Simulation assumptions for NR FR2 MIMO OTA”, Huawei, HiSilicon