## Slide 1
WF on solutions to minimize the impact of polarization basis mismatch between the TE and DUT on the RF testing
3GPP TSG-RAN WG4 Meeting #97-e R4-2017594
Electronic Meeting, Nov. 2nd – Nov. 13th, 2020
Agenda Item: 13.1.2
Samsung [, …]

## Slide 2: Background
EIRP measurement
  In RAN4#96e meeting, methods to enhance EIRP measurement were down selected (R4-2012714) to 5 methods
  Focus on 3 methods which have been captured in WID (RP-201862)
    TPMI side condition method
    DL polarization scan method
    test mode to trigger TX diversity
  Check feasibility of 2 methods
    power up command to trigger TX diversity
    2-port CSI-RS method
UL demodulation
  In RAN4#96e meeting, dual polarization coherent receiver topology was agreed as a starting point
In this meeting, above topics are further discussed in email thread 331 and GTW session.

## Slide 3: WF1: EIRP measurement - TPMI side condition method
Proposals
  Alt 2-1-1-1a: TPMI side condition method (option 1 in WF R4-2012714) to enhance UE EIRP measurement has been adopted by the standard, and the testability enhancement “TPMI side condition method” can be considered adopted
  Alt 2-1-1-1b: Alt 2-1-1-1a with further clarification that “Practical TPMI” shall be further applied for “TPMI side condition method”
  Alt 2-1-1-1c: Alt 2-1-1-1a only if clarification is provided whether RAN1’s definition of TPMI indices 2-5 forcing single-layer transmission using two antenna ports corresponds to the UE enabling two transmit chains at all times
  Alt 2-1-1-1d: Alt 2-1-1-1a only if chipset and OEM manufacturers can confirm whether Rel-15 nonCoherent UE’s and Rel-16 nonCoherent without full power transmission mode1 (ul-FullPowerTransmission = fullpowerMode2 or fullpower) are still affected by this DL polarization mismatch issue.
  Alt 2-1-1-2: TPMI side condition method is only applicable for EIRP measurement for UL MIMO operation for partial UEs. Other methods to enhance EIRP measurement need to be investigated for non-MIMO cases in clause 6.2 of TS 38.101-2
Agreement
  TPMI side condition method is agreed as applicable method to enhance EIRP measurement for partial UEs
    This method can be applied for:
      Rel-15 coherent UEs
      Rel-16 coherent UEs
      Rel-16 nonCoherent UEs which support uplink full power transmission
    This method is not applied for Rel-15 nonCoherent UEs and Rel-16 nonCoherent UEs which do not support full power transmission
  TPMI side condition method shall be further refined under the umbrella of the hybrid methods in WF6.

## Slide 4: WF2: EIRP measurement - DL polarization scan method
Proposals
  Alt 2-1-5-1: DL pol. Scan is not valid (Anritsu, Qualcomm, Samsung, vivo, R&S, OPPO, Sony, Ericsson) (8)
  Alt 2-1-5-2: RAN4 to further consider the DL pol. Scan (LG, Keysight, Huawei, Apple) (4)
Agreement
  Alt 2-1-5-1: The DL pol. scan method is not a valid method to enhance UE EIRP measurement
  The agreements are based on the assumption that the adopted hybrid test method(s) which described in WF 6 can ensure the test coverage for all UEs.

## Slide 5: WF3: EIRP measurement - Test mode to trigger TX diversity
Proposals
  Alt 2-1-3-1: remove test mode from list of candidate solutions (Qualcomm, Sony, Huawei, Ericsson, Apple)
  Alt 2-1-3-2: confirm test mode as a solution (Anritsu, Samsung, LG, Keysight)
  Alt 2-1-3-3: RAN4 should not go with test mode unless this is the only solution (vivo, R&S, OPPO)
Agreement
  Test mode to trigger TX diversity can be considered as a backup method under the umbrella of the hybrid methods in WF6 (Qualcomm comment to be deleted before final version: We do not think it is the TE’s burden to ‘trigger Tx diversity’ in a way that the network cannot. The transition between single chain and Tx diversity should be an autonomous UE function and transparent to the network).
  (alt.) FFS if test mode to trigger TX diversity can be considered as a backup method under the umbrella of the hybrid methods in WF6
Notes: Apple : we have strong concern on test mode solution.
Keysight: This is comprise solution included in the package as backup solution.
Sony: We understand the solution applied UEs which not support TPMI side condition. What’s condition such TX divercity to be used in real network?
Samsung: We agree with Keysight, it’s backup and reliable solution. Transparent Tx diversity can be UE implementation, the limitation just for test issue.
LG: Similar view as Samsung. This is backup solution as test mode for beam lock.
QC: Test mode only can be used for practical issue in TE side. We should not use test mode which real NW not used.
E///: Similar view as QC for void test mode as much as possible. Similar view as Sony.
R&S: We agree with Samsung and LGE. Now this is practical and reliable solution.
Apple: We can minute the conclusions and the candidate solutions in TR.

## Slide 6: WF4: EIRP measurement – power up command to trigger TX diversity
Proposal
  Test enhancement for EIRP shall focus on the power command as it is the only command that the network can use to control the UE output power in the field
Agreement
  The power up command to trigger TX diversity is not a feasible method to enhance the UE EIRP measurement

## Slide 7: WF5: EIRP measurement – Configuration of 2-port CSI-RS
Proposal
  “2-port CSI-RS” shall be provided in EIRP test procedure; it can be provided simultaneously or sequentially
Open issues
  Simultaneous vs. sequential configuration and whether sequential is feasible
  Mapping between ports and polarizations in the test equipment and whether this is feasible for test equipment
  Applicability to Rel-16 beam correspondence capabilities
  Whether phase coherency between ports at the test equipment side is needed
  Whether this configuration can actually help to trigger TX diversity behavior at the UE
Agreement
  further discuss 2-port CSI-RS method under the umbrella of the hybrid methods in WF6 if above issues could be addressed

## Slide 8: WF6: EIRP measurement – hybrid methods
Proposal
  select the method based on manufacturer declaration:
    a. If UE declares codebookSubset = fullyAndPartialAndNonCoherent, TPMI index is set to [2]. This is applicable to UE’s from Rel.15 onwards.
    b. If UE declares codebookSubset = nonCoherent and ul-FullPowerTransmission-r16 = fullpowerMode1, TPMI index is set to [2]. This is applicable to UE’s from Rel.16 onwards.
    c. Otherwise, an alternate method TBC (can elaborate?) is to be used (e.g. 2-port CSI-RS, test mode or other).
Agreement
  Different approaches can be adopted based on UE capability, detailed applicability rule can be further discussed
    Option 1: Introduce TPMI side condition test method only
      FFS whether additional test methods need to be introduced
    Option 2: Introduce TPMI side condition + DL scan / test mode to trigger TX diversity (backup method up to OEM declaration )
    Option 3: Introduce TPMI side condition +test mode to trigger TX diversity (backup method)
  TPMI method is applicable for EIRP measurement test cases for 1 layer transmission with 2 SRS ports configured.
  UE supporting transparent TX diversity shall be considered in the applicability rule of hybrid methods if there is EIRP measurement test case for 1 layer transmission with 1 SRS port configured.
Notes: Qualcomm: Option 2 and 3 are covered by FFS of option 1
Qualcomm: Tx diversity UEs also are covered by FFS of option 1
Qualcomm: There is no mandate that every category of UE must be assigned a new method under this SI.

## Slide 9: WF7: UL demodulation
Proposal
  It is proposed to confirm the dual polarization coherent receivers measurement setup as the enhancement which addresses the UE demodulation part of the polarization mismatch objective
Agreement
  RAN4 confirms the dual polarization coherent receivers measurement setup as the enhancement which addresses the UE demodulation part of the polarization mismatch objective

## Slide 10: Reference
R4-2014266, FR2 testability enhancement for polarization mismatch, Qualcomm
R4-2014275, Discussion on FR2 EIRP measurement enhancement,
R4-2014827, Analysis on practical TPMI and 2-port CSI-RS for EIRP measurement, MediaTek
R4-2014920, Views on polarization mismatch, Apple
R4-2015871, Views on testability enhancement for UE FR2 test, Sony, Ericsson
R4-2016212, On minimizing the impact of polarization basis mismatch between the TE and DUT, Keysight
R4-2016568, Views on polarization basis mismatch, Rohde & Schwarz
R4-2017429, Email discussion summary for [97e][331] FR2_enhTestMethods, Moderator(Apple)