## Slide 1: WF on general aspects for UE RF requirements
Skyworks Solutions Inc., Apple
R4-2016863
3GPP TSG-RAN WG4 Meeting #97-e
Electronic meeting, 2 – 13 November 2020

## Slide 2: Scope
Capture agreeable content from 1st round discussion on:
Equation based requirements and how to introduce 35/45MHz channel BW in tables for bands: WF in slide 4-10
UL configuration limitations based on UL BW or UL RB allocation: WF in slide 14-16
How to introduce 35/45MHz channel BW in tables for band combination is not in scope of this WI but the process is worth clarifying. Slide 12
References of contributions covering these topics are in last slide.

## Slide 3: Background on entering 35/45MHz channel BW in UE requirements for bands in the WI:
For 38.101-1 the affected generic requirements are:
  5.3.2 Maximum transmission bandwidth configuration
  6.2.2 UE maximum output power reduction (DMPR for BW criteria)
  6.5.1 Occupied bandwidth => may be simplified since occupied channel BW = BWchannel
  6.5.2.2 Spectrum emission mask => can use equation based approach
  6.5.2.4.1 NR ACLR => ACLR measurement BW
  7.4 Maximum input level
  7.5 Adjacent channel selectivity => can use equation based approach
  7.7 Spurious response => can use equation based approach
  7.8.2 Wide band Intermodulation => equation based approach FFS
  Reference measurement channels
For 38.101-1 the affected band specific requirements are:
  5.3.5 UE channel bandwidth per operating band
  5.3.6 Asymmetric channel bandwidths if UL BW is limited and for n66 and n71
  5.3E.2 Channel bandwidth for V2X concurrent operation for n71?
  5.4.4 TX–RX frequency separation if asymmetric UL/DL is adopted
  6.2.3 UE additional maximum output power reduction: adding 35/45MHz BW where necessary
  A-MPR for NS_03 and NS_03U, NS_46 and NS_35 and associated requirements. => SEM requirements can use equation based approach
  7.3.2 Reference sensitivity power level: tables for REFSENS and UL configuration are already wider than the page

## Slide 4: WF: R17 Equation based SEM from [1]
ΔfOOB MHz | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  | Measurement bandwidth
 | 5 | 10, 15, 20, 25, 30, 35, 40, 45 | 
± 0-1 | -13 | -13 | 1 % of channel BW
± 1-6 | -13 |  | 1 MHz
± 6-10 | -25 |  | 
± 1-BWChannel |  | -13 | 
± BWChannel-(BWChannel+5) |  | -25 | 
ΔfOOB (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  |  |  |  | Measurement bandwidth
 | 5 | 10 | 15 | 20 | 35 | 
± 0-0.1 | -15 | -18 | -20 | -21 | -23.5 | 30 kHz
± 0.1-6 | -13 |  |  |  |  | 100 kHz
± 0.1-BWChannel |  | -13 |  |  |  | 
± 6-10 | -25 |  |  |  |  | 1 MHz
± BWChannel-(BWChannel+5) |  | -25 |  |  |  | 
NOTE 1: Void |  |  |  |  |  | 
Equation based approach is adopted for general SEM like table on the right
Band specific SEM for NS03 and NS_35 adopts the same approach as in respective tables below. Addition of 35MHz and or 45MHz may not be needed depending on UL BW
ΔfOOB (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  |  | Measurement bandwidth
 | 5 | 10, 15, 20, 25, 30, 35, 40, 45 | 50, 60, 70, 80, 90, 100 | 
± 0-1 | -13 | -13 |  | 1 % of channel BW
± 0-1 |  |  | -24 | 30 kHz
± 1-5 | -10 | -10 |  | 1 MHz
± 5-6 | -13 |  |  | 
± 6-10 | -25 |  |  | 
± 5-BWChannel |  | -13 |  | 
± BWChannel-(BWChannel+5) |  | -25 |  | 
NOTE 1: Void |  |  |  | 
Table 6.5.2.2-1: General NR spectrum emission mask
Table 6.5.2.3.1-1: Additional requirements for "NS_35"
Table 6.5.2.3.3-1: Additional requirements for "NS_03" and "NS_21"
First row could be further simplified with an equation

## Slide 5: WF: R17 Equation based maximum input power
Equation based approach is adopted for maximum input power like in above table
Rx Parameter | Units | Channel bandwidth (MHz) |  |  |  |  |  |  | 
 |  | 5, 10, 15, 20 | 25 | 30 | 35 | 40 | 45 | 50 | 60, 70, 80, 90, 100
Power in Transmission Bandwidth Configuration | dBm | -252 | -242 | -232 | -22.52 | -222 | -21.52 | -212 | -202
 |  | -273 | -263 | -253 |  | -243 |  | -233 | -223
NOTE 1: The transmitter shall be set to 4 dB below PCMAX_L,f,c at the minimum uplink configuration specified in Table 7.3.2-3 with PCMAX_L,f,c as defined in clause 6.2.4. NOTE 2: Reference measurement channel is A.3.2.3 or A.3.3.3 for 64 QAM. NOTE 3: Reference measurement channel is A.3.2.4 or A.3.3.4 for 256 QAM. |  |  |  |  |  |  |  |  | 
Table 7.4-1: Maximum input level

## Slide 6: WF: R17 Equation based ACS from [1]
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
ACS1 | dB | 33 | 30 | 27 – 10log10(BWChannel /20)
NOTE 1: ACS value is rounded to the next higher 0.5dB value |  |  |  | 
RX parameter | Units | Channel bandwidth (MHz)
 |  | 10, 15, 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
ACS | dB | 33
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | REFSENS + 14 dB |  | 
Pinterferer1 | dBm | REFSENS + 45.5 dB | REFSENS + 42.5 dB | REFSENS + 39.5 – 10log10(BWChannel /20)
BWinterferer | MHz | 5 |  | 
Finterferer (offset) | MHz | BWChannel /2 + 2.5 / -(BWChannel /2 + 2.5) |  | 
NOTE 1: Pinterferer value is rounded to the next higher 0.5dB value |  |  |  | 
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration1 | dBm | -56.5 | -53.5 | -50.5 + 10log10(BWChannel /20)
Pinterferer | dBm | -25 |  | 
BWinterferer | MHz | 5 |  | 
Finterferer (offset) | MHz | BWChannel /2 + 2.5 / -(BWChannel /2 + 2.5) |  | 
NOTE 1: Power in transmission bandwidth configuration value is rounded to the next higher 0.5dB value |  |  |  | 
RX parameter | Units | Channel bandwidth (MHz)
 |  | 10, 15, 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | REFSENS + 14 dB
Pinterferer | dBm | REFSENS + 45.5 dB
BWinterferer | MHz | BWChannel
Finterferer (offset) | MHz | BWChannel / -BWChannel
RX parameter | Units | Channel bandwidth (MHz)
 |  | 10, 15, 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | -56.5
Pinterferer | dBm | -25
BWinterferer | MHz | BWChannel
Finterferer (offset) | MHz | BWChannel / -BWChannel
Table 7.5-1: ACS for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
Table 7.5-2: ACS for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz
Table 7.5-3: Test parameters for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz, case 1
Table 7.5-4: Test parameters for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz, case 2
Table 7.5-5: Test parameters for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz, case 1
Table 7.5-6: Test parameters for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz, case 2

## Slide 7: WF: R17 Equation based Blocking from [1]
Equation based approach is adopted for in-band and out of band blocking like in above tables
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration1 | dBm | REFSENS + 6 dB | REFSENS + 7 dB | REFSENS + (9 + 10log10(BWChannel /20)) dB
BWinterferer | dBm | 5 |  | 
FIoffset, case 1 | MHz | 7.5 |  | 
FIoffset, case 2 | MHz | 12.5 |  | 
NOTE 1: Power in transmission bandwidth configuration value is rounded to the next higher 0.5dB value |  |  |  | 
Table 7.6.2-1: In-band blocking parameters for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
RX parameter | Units | Channel bandwidth (MHz)
 |  | 10, 15, 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | REFSENS + 6 dB
BWinterferer | dBm | BWChannel
FIoffset, case 1 | MHz | (3/2) BWChannel
FIoffset, case 2 | MHz | (5/2) BWChannel
Table 7.6.2-3: In-band blocking parameters for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration1 | dBm | REFSENS + 6 dB | REFSENS + 7 dB | REFSENS + (9 + 10log10(BWChannel /20)) dB
NOTE 1: Power in transmission bandwidth configuration value is rounded to the next higher 0.5dB value |  |  |  | 
Table 7.6.3-1: Out-of-band blocking parameters for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | REFSENS + 6 dB | REFSENS + 7 dB | REFSENS + 9 dB
Table 7.6.3-3: Out-of-band blocking parameters for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz

## Slide 8: WF: R17 Equation based Blocking from [1]
Equation based approach is adopted for narrow band blocking like in above table
Band | RX parameter | Units | Channel bandwidth (MHz) |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
n1, n2, n3, n5, n7, n8, n12, n14, n18, n20, n25, n26, n28, n30, n34, n38, n39, n40, n41, n48, n50, n51, n53, n65, n66, n70, n71, n74, n75, n76n | Pw | dBm | REFSENS + channel BW specific value below |  |  |  | 
 |  |  | 16 | 13 | 14 | 16 | 16
 | Puw (CW) | dBm | -55 |  |  |  | 
 | Fuw (offset, SCS = 15 kHz)1 | MHz |  |  |  |  | NA
 | Fuw (offset, SCS = 30 kHz)1 | MHz | NA |  |  |  | 
NOTE 1: rounded to half of SCS |  |  |  |  |  |  | 
Band | RX parameter | Units | Channel bandwidth (MHz) |  |  |  | 
 |  |  | 5 | 10 | 15 | 20 | 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
n1, n2, n3, n5, n7, n8, n12, n14, n18, n20, n25, n26, n28, n30, n34, n38, n39, n40, n41, n48, n50, n51, n53, n65, n66, n70, n71, n74, n75, n76n | Pw | dBm | REFSENS + channel BW specific value below |  |  |  | 
 |  |  | 16 | 13 | 14 | 16 | 16
 | Puw (CW) | dBm | -55 |  |  |  | 
 | Fuw (offset, SCS = 15 kHz)1 | MHz |  |  |  |  | NA
 | Fuw (offset, SCS = 30 kHz)1 | MHz | NA |  |  |  | 
NOTE 1: rounded to half of SCS |  |  |  |  |  |  | 
Table 7.6.4-1: Narrow Band Blocking

## Slide 9: WF: R17 Equation based spurious response from [1]
Equation based approach is adopted for spurious response like in above tables
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 5, 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration1 | dBm | REFSENS + 6 dB | REFSENS + 7 dB | REFSENS + (9 + 10log10(BWChannel /20)) dB
NOTE 1: Power in transmission bandwidth configuration value is rounded to the next higher 0.5dB value |  |  |  | 
Table 7.7-1: Spurious response parameters for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
RX parameter | Units | Channel bandwidth (MHz) |  | 
 |  | 10 | 15 | 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100
Power in transmission bandwidth configuration | dBm | REFSENS + 6 dB | REFSENS + 7 dB | REFSENS + 9 dB
Table 7.7.1-1a: Spurious response parameters for NR bands with FDL_low ≥ 3300 MHz and FUL_low ≥ 3300 MHz

## Slide 10: WF on tables where equation based approach can’t apply
For TX BW, guard bands, occupied BW and ACLR measurement BW:
  Two additional columns for 35 and 45MHz fit in the pages and will be updated once SU is confirmed. Occupied BW is basically = BWchannel
For tables with channel configurations:
  Tables are already just fitting the page some improvement is needed
For REFSENS tables:
  Tables are already wider than the page and in some case it is difficult to find the associated channel BW with a column
Options:
  Swapping columns and rows have been proposed to reduce width
  Reducing rows per SCS by introducing coding instead of “yes” but it does not apply to RESENS tables
  Instead of “yes” the BW value could be repeated or a list of BW is used
  Using page in landscape mode
  Other

## Slide 11: Background on adding 35/45MHz channel BW for bands-combinations:
For 38.101-1 the affected band combination specific requirements are:
  5.5A Configurations for CA
  5.5B Configurations for DC
  5.5C Configurations for SUL
  Associated AMPR
  SEM tables already uses equation based approach
  7.3A.2.4 Reference sensitivity power level for SDL bands
  Associated REFSENS exceptions for UL harmonics, harmonic mixing and cross band isolation
  7.3C.2 Reference sensitivity power level for SUL
  Blocking and ACS for CA are already equation based
Some of WF for band specific requirements can apply to band combinations

## Slide 12: Adding 35/45MHz channel BW for bands-combinations
For introduction of 35MHz and 45MHz BW in existing band combinations the following rules should apply
35/45MHz BW can only be added to a band combination if the related band specific work is completed in NR_FR1_35MHz_45MHz_BW WI
Even if 35/45MHz BW are added to an existing FR1 band combination, it can only be introduced with a TR and not directly as a CR as for any band combination even if >3 band combination. This is because the MSD of its lower order constituents up to 3 should be verified and specified for these new channel BW.
  If there is existing MSD for the band where the new BWs are introduced is a victim of an UL harmonic or harmonic mixing issue, the MSD values need to be added to the new victim channel BW
  If there is existing MSD for the band where the new BWs are introduced is a victim of a cross band isolation issue, the MSD values need to be added to the new victim channel BW
  If there is existing MSD for the band where the new BWs are introduced is an aggressor of a cross band isolation issue, the UL configuration values need to be added to the new victim channel BW.
  In the case where the new introduced channel BW is the largest one even if cross band isolation issue does not exist for lower channel BW, it should be studied if the issue could exist as an aggressor or a victim.
  In the case of adding new BW to intra-band UL/DL CA MSD and AMPR issues also need attention.
Although this process for the 35/45MHz introduction in band-combination is discussed as an outcome of completion of a band in NR_FR1_35MHz_45MHz_BW WI it could also apply for completion of a band in NR_bands_R17_BWs WI.
To crystalize and finalize this process it is proposed that an example combination is studied within either NR_FR1_35MHz_45MHz_BW or NR_bands_R17_BWs or other WI to develop a template.

## Slide 13: Background on UL configuration and UL BW limitation :
There are a few aspects where UL BW play a role:
  DMPR when FDD BW >3% or TDD BW>4%, This is the case for n8 and n71
  The new BW becomes the larger BW:
    MSD related to cross band isolation may have to be considered
    Same for some band protection
    Larger A-MPR may be required
    Beyond BB capability there may be BW limitations on the transmitter on legacy devices
For FDD bands with small duplex, large MSD and large A-MPR have laready been observed by measurements
For n8 and n71 all of the above aspects are relevant as discussed in [2]
For n25 45 MHz is the largest UL channel BW and has ACLR1 overlap with DL channel => large MSD

## Slide 14: WF on n8 and n71 UL BW:
Option1: UL BW is limited to 20 MHz
  No need for DMPR, NS_43 and NS_35 A-MPR and associated SEM requirements
  No issue with other band protection
  Low MSD can be specified using current 20MHz UL configuration:
    Option 1a: Worst case 20MHz UL closest to DL
    Option 1b: Best case 20MHz UL furthest to DL
    Option 1c: both 1b and 1c are specified
  Limited impact to band combinations
Option2: 35MHz UL BW is supported
  Need for DMPR, NS_03 and NS_35 A-MPR and associated SEM requirements
  Large MSD with further reduced UL configuration and A-MPR are specified which does not help the link throughput
  Potential additional work for band combinations with n8 or n71 UL
WF: Option 1 is chosen and exact 20MHz UL configuration can be part of WF R4-2016864 by selecting sub options a, b or c

## Slide 15: WF on n25 UL BW:
Option1: UL BW is limited to 40 MHz
  No need for NS_03 and associated SEM requirements for 35MHz
  Low MSD can be specified using current 40MHz UL configuration:
    Option 1a: Worst case 40MHz UL closest to DL
    Option 1b: Best case 40MHz UL furthest to DL
    Option 1c: both 1b and 1c are specified
  Limited impact to band combinations
Option2: 45MHz UL BW is supported
  Need for NS_03 and associated SEM requirements
  Large MSD with further reduced UL configuration are specified which does not help the link throughput
  Potential additional work for band combinations with n25 UL
WF: Option 1 and Option 2 can be further discussed and selected in WF R4-2016864

## Slide 16: References:
[1] R4-2014911 UE RF requirements tables with channel BW dependency Apple Inc.
[2] R4-2015800 Specification impact of additional 35&45MHz channel bandwidths Skyworks Solutions Inc.
[3] R4-2014173 35M_45M AMPR, MPR, REFSENS Qualcomm Incorporated
[4] R4-2016010 n71 35MHz AMPR and MSD Measurements Skyworks Solutions Inc.
[5] R4-2016011 n8 35MHz AMPR and MSD Measurements Skyworks Solutions Inc.
[6] R4-2016027 n7 35MHz AMPR and MSD Measurements Skyworks Solutions Inc.
[7] R4-2016295 Introduction of 35 MHz for n8, n66, n71 and 45 MHz for n66 Apple Inc.
[8] R4-2016060 Introduction of 35MHz and 45MHz regarding CA, DC, V2x combinations Ericsson
[9] R4-2015044 On UE RF requirement for new channel bandwidth of 35MHz and 45MHz ZTE Corporation