## Slide 1: WF on Test cases for MR-DC Idle mode CA measurements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #97e
E-meeting, November 2nd – 13th, 2020
R4-2017122
Document for: Approval

## Slide 2: Topic #3: Performance – accuracy requirements
Issue 3-10-1: Confirm conclusion from round 1 discussion (was: Sub-topic 3-1 and 3-2)
  Agreement 1 (related to Sub-topic 3-1). RAN4 will define accuracy requirements for MR-DC EMR for the newly introduced core requirement cases listed:
    36.133:
      NR inter-RAT:
        FR1
        FR2
    38.133:
      NR inter-frequency:
        FR1
        FR2
      LTE inter-RAT
  Agreement 2 (related to sub-topic 3-2): RAN4 will re-use of existing connected mode accuracy requirements as baseline for developing EMR idle mode CA measurement accuracy requirements
      Note: RAN4 has already agreed to define EMR accuracy requirements more relaxed compared to connected mode inter-frequency accuracy requirements in RAN4#96.
(conclude based on 2nd round discussion)

## Slide 3: Topic #3: Performance – accuracy requirements
Issue 3-10-2: Measurement accuracy relaxation compared to existing connected mode requirements (was: Sub-topic 3-3)
  More discussion is needed.
    Discuss the CR content further and try to agree on the principle of capturing the measurement accuracy requirements.
    Leave numbers in [] in this meeting.
    Assign the draft Big CR
  (conclude based on 2nd round discussion)

## Slide 4: Topic #4: Test cases for MD-DC EMR
Time plan for developing MR-DC test cases:
  RAN4#97-e (November 2020):
    Agree on high-level list for test cases.
    Agree on work split between interested companies.
  RAN4#98-e (January 2021):
    Provide draft CRs for test cases.
    Provide big CR by collecting draft CRs
(conclude based on 2nd round discussion)

## Slide 5: Topic #4: Test cases for MD-DC EMR
Sub-topic 4-11: Test Case Coverage:
  Issue 4-11-1: Which serving carrier scenarios to consider
    Recommended WF
      define test cases including with NR FR1 serving carrier, with an NR FR2 serving carrier and an LTE serving carrier
  (conclude based on 2nd round discussion)
  Issue 4-11-2: Which target carrier scenarios to consider.
    Recommended WF
      define test cases including with NR FR1 target carrier, with an NR FR2 target carrier and an LTE target carrier.
  (conclude based on 2nd round discussion)
  Issue 4-11-3: Which target carrier type (configured for mobility or not configured for mobility) to consider.
    Recommended WF
      define test cases with a target carrier which is configured for mobility and a target carrier which is not configured for mobility.
  (conclude based on 2nd round discussion)

## Slide 6: Topic #4: Test cases for MD-DC EMR
Sub-topic 4-11: Test Case Coverage:
  Issue 4-11-4: Which target cell type (detected cell at connection release or not) to consider.
    Recommended WF
      define test cases with for both detected target cell and new target cell
  (conclude based on 2nd round discussion)
  Issue 4-11-5: Beam level measurements.
    Recommended WF
      define test cases with for both scenarios where Idle mode CA measurement report is requested with beam level measurements and Idle mode CA measurement report is not requested with beam level measurements
  (conclude based on 2nd round discussion)
  Issue 4-11-6: s-NonIntraSearch thresholds configured.
    Recommended WF
      define test cases with for both scenarios where Idle mode CA measurement report and s-NonIntraSearch thresholds are configured and Idle mode CA measurement report is configured and s-NonIntraSearch thresholds are not configured.
  (conclude based on 2nd round discussion)

## Slide 7: Topic #4: Test cases for MD-DC EMR
Sub-topic 4-11: Test Case Coverage:
  Issue 4-11-7: Cell detected status.
    Recommended WF
      more discussion needed
  (conclude based on 2nd round discussion)

## Slide 8: Topic #4: Test cases for MD-DC EMR
Sub-topic 4-12: Test Case List for discussion:
  (conclude based on 2nd round discussion)
TC# | Serving Carrier [LTE, NR (FR1, FR2)] | Target Carrier [LTE, NR (FR1, FR2)] | Target Carrier type [mobility carrier or not] | Target Cell type [New cell, Detected cell] | Beam level Measurements [yes, no] | s-NonIntraSearch thresholds configured [yes, no] | Summary | 
 |  |  |  |  |  |  | yes | No
1 | NR FR1 | NR FR1 | mobility | detected | Yes | Yes |  | 
2 |  | NR FR2 | not mobility | not detected | No | Yes |  | 
3 |  | LTE | mobility | detected | N/A | No |  | 
4 | NR FR2 | NR FR1 | not mobility | not detected | Yes | No |  | 
5 |  | NR FR2 | mobility | detected | No | No |  | 
6 |  | LTE | mobility | detected | N/A | No |  | 
7 | LTE | NR FR1 | mobility | detected | No | Yes |  | 
8 |  | NR FR2 | not mobility | not detected | Yes | No |  |