## Slide 1: WF on RRM test cases for power saving
Agenda Item: 7.6.2
Document for: Approval
Source: CATT
3GPP TSG-RAN WG4 #97e R4-2017133
Electronic Meeting, 2-13 Nov, 2020

## Slide 2: Background
In the references [1][2][3][4][5][6][7], companies provide their views of how to design the RRM test cases for power saving

## Slide 3: Agreements
Use separate tests for each criterion (low mobility/not-at-cell-edge)
Different priority frequency layers coexist in the same test for different priority frequency layers
Exclude high priority layer cell search for inter-frequency/inter-RAT
Use two round (to and back) cell reselection process for intra-frequency power saving test cases
FR1: Use two round (to and back) cell reselection process for inter-frequency/ inter-RAT in power saving test cases
FR2: Use two round (to and back) cell reselection process for inter-frequency in power saving test cases. Further check on TE feasibility for FR2
UE gain in FR2 should be considered. FFS: Leave the threshold impacted by G as [TBD] and discuss it in the next meeting
SSearchDeltaP can be configured to 3dB for FR1 and 6dB for FR2
SSearchThresholdP can be configured to (Srxlev – X) dB, X = 6dB for FR1 while7.5dB for FR2
Exclude the cell search process from test repetition
Use shorter DRX cycle to improve test efficiency: DRX = 0.64 s TSI-NR = 1280ms

## Slide 4: References
[1] R4-2014370 Discussion on performance part for cell reselection , MediaTek Inc.
[2] R4-2014409 Discussion on RRM test cases for power saving, CATT
[3] R4-2014657 Discussion on test cases for power saving RRM, Xiaomi
[4] R4-2014835 Considerations on test cases for UE power saving RRM, vivo
[5] R4-2015483 Discussion on test cases for measurement relaxation in power saving, Huawei, HiSilicon
[6] R4-2016147 Discussions on UE power saving performance requirements, Ericsson
[7] R4-2016149 Discussions on cell reselection to FR2 inter-freq. case under power saving, Ericsson