## Slide 1: WF on gNB positioning measurement requirements
Ericsson
3GPP TSG-RAN WG4 Meeting # 97-e
Electronic Meeting, November 2-13, 2020
Agenda: 7.7
R4-2017159

## Slide 2: Selection of option for gNB measurement accuracy requirements
Define measurement accuracy requirements for
  SRS-RSRP
  gNB Rx-Tx time difference
FFS: UL RTOA
  Further investigate whether the accuracy requirements for gNB Rx-Tx can be reused. If there are no technical issues to reuse gNB Rx-Tx time difference requirements, then the UL RTOA requirements will be defined.
Further study the impact from non-guaranteed SRS transmission for different methods

## Slide 3: Optionality of gNB accuracy requirements
gNB shall meet accuracy requirements for supported positioning measurement for the test configurations (e.g. CBW, SRS configurations, etc) declared by the manufacturer

## Slide 4: Side conditions for gNB measurement accuracy
Accuracy is defined for two different side conditions (two sets of Es/Iot)
  High SNR side condition (Es/Iot1) which corresponds to for example typical serving cell conditions or low interference neighbor cell conditions
  Low SNR side condition (Es/Iot2) which corresponds to for example typical neighbor cell conditions
Es/Iot1 and Es/Iot2 are to be derived based on system simulations
Values of Es/Iot1 and Es/Iot2 are FFS.

## Slide 5: Beam configuration for gNB measurement accuracy
Antenna beam configuration assumption for gNB positioning measurement accuracy follows the approach used in BS specifications: TS 38.104 and TS 38.141-1/2.
FFS: which of following options correspond to antenna beam configuration assumption in BS specifications for defining gNB positioning measurement accuracy:
  Option 1:
    Fixed antenna beams are assumed in gNB for deriving accuracy
  Option 2:
    Accuracy does not depend on antenna beam configuration in gNB i.e. do not assume fixed gNB antenna beams
  Option 3:
    gNB antenna beam configuration is not needed in the requirement definition
Candidate options if the above option 1 is adopted:
  Option 1:
    Accuracy applies provided beam peak/main beam lobe is directed towards the UE in FR1 and FR2.
  Other options not precluded

## Slide 6: SRS configurations for gNB measurement accuracy
Accuracy is defined only for subset of suitable SRS configurations and is met for only subset of SRS configurations declared by the manufacturer.
Subset of suitable SRS configurations are derived based on link simulations (uphold earlier agreement at RAN4#96-e in R4-2012140).

## Slide 7: SRS configuration parameters for gNB measurement accuracy
FFS: Other/remaining SRS configuration parameters:
  Candidate options for other SRS parameters:
SRS configuration parameters | Value
Number of SRS Resource sets | 1
Number of SRS resources within one SRS resource set | 1
SRS repetition factor | 1
SRS frequency hopping | OFF
SRS configuration parameters in the following table are agreed for FR1 and FR2:
Option 1:
FR | Bandwidth SRS [MHz] / SCS [kHz] | SRS comb size | No. of SRS symbols | SRS resource periodicity TSRS [slots]
FR1 | 5 / 15 | Com4 | 4 | 160
FR1 | 20 / 15 | Com2 | 2 | 160
FR1 | 20 / 30 | Com4 | 4 | 160
FR1 | 20 / 30 | Com8 | 8 | 40
FR1 | 20 / 60 | Com8 | 8 | 40
FR1 | 100 | Com4 | 4 | 40
FR2 | 50 / 60 | Com8 | 8 | 40
FR2 | 50 / 120 | Com8 | 8 | 40
FR2 | 200 / 60 | Com8 | 8 | 40
FR2 | 400 / 120 | Com8 | 8 | 40
Option 2:
  SRS resource periodicity is excluded. Other parameters are FFS
Other options not precluded

## Slide 8: Factors impacting timing measurement accuracy for different gNB types
Study impact of factors impacting timing measurement accuracy for different gNB types (1-C, 1-H, 1-O, 2-O).
Candidate options:
  Study impact of calibration error for the group delay between the antenna and the baseband on gNB timing measurement accuracy,
  Study whether calibration error for the group delay between the antenna and the baseband differs for different gNB types and
  Study other impairments impacting gNB timing measurement accuracy.

## Slide 9: Factors impacting SRS-RSRP measurement accuracy for different gNB types
Study impact of factors impacting SRS-RSRP measurement accuracy for different gNB types (1-C, 1-H, 1-O, 2-O).
Candidate options:
  Study impact of RF calibration error on SRS-RSRP measurement accuracy,
  Study whether RF calibration error differs for different gNB types and
  Study other impairments impacting SRS-RSRP measurement accuracy.