## Slide 1: Way forward on FR2 inter-band CA RRM
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #97-e
Online, 2nd– 13th November, 2020
Agenda: 7.13.1.5, 7.13.2.2.
R4-2017201

## Slide 2
Issue 1-1: Necessity of SCell activation requirement with existing serving cell on different FR2 band.
Agreement: Not necessary to specify the requirements for ‘SCell being activated belongs to FR2 and there is an active serving cell on that FR2 band and the PCell or PSCell is in FR2 and the PCell or PSCell and SCell being activated are in a band pair with independent beam management’
Issue 1-2: Beam management resources for IBM UE
Agreement: IBM UEs shall be able to add/configure/activate cells on both FR2 inter-band CCs only when beam management resources are configured in the both bands
Agreements on core requirements maintenance

## Slide 3
Issue 8-1: TC list for inter-band CA requirement for FR2 UE measurement capability of independent Rx beam.
Agreements: TC list for inter-band CA requirement for FR2 UE measurement capability of independent Rx beam
Agreements on test case list
Test case number | Test purpose
Test 1 | SCell Activation and deactivation for FR2+FR2 inter-band

## Slide 4
Issue 8-2: TC configurations for inter-band CA requirement for FR2 UE measurement capability of independent Rx beam.
Agreements:
  For SCell activation and deactivation delay test in FR2 inter-band CA, it is suggested that the test consists of three time period. (add a note to clarify that bands 1 and 2 are inter-band CA operating bands in FR2 as specified in Table 5.2A.2-1 in TS38.101-2)
    Before the test starts, the UE is connected to Cell 1 (PCell) on FR2 band 1.
    At the beginning of T1, the UE receives an RRC message to add Cell 2 as SCell on FR2 band 2. The time duration T1 is the preparation period for the test.
    At the beginning of T2, the UE receives a MAC message for SCell activation. During time duration T2, the SCell activation delay and interruptions to PCell need to be tested.
    At the beginning of T3, the UE receives a MAC message for SCell deactivation. During time duration T3, the SCell deactivation delay and interruptions to PCell need to be tested.
  FFS on how to configure AoAs for Cell1 and Cell2
Agreements on test procedure