## Slide 1: Way forward on NR-U PRACH demodulation requirements
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, 2 – 13 Nov., 2020
Agenda: 7.1.8.4.3
R4-2017468
Document for: Approval
Nokia, Nokia Shanghai Bell

## Slide 2: Background
Agreed WFs for in previous meetings
  RAN4 #96-e
    R4-2012611, Way Forward on NR-U BS demodulation requirements
    R4-2012610, Way Forward on NR-U UE demodulation requirements
Corresponding Email summary in RAN4#97-e
    R4-20xxxxx Email discussion summary for [97e][316] NR_unlic_Demod_BS
      The issues related to PRACH are:
        Issue 4-1-1: PRACH formats
        Issue 4-1-2: Antenna configuration
        Issue 4-1-3: Propagation conditions
        Issue 4-1-4: Frequency offset
        Issue 4-1-5: Ncs
        Issue 4-1-6: Time error estimation tolerance
        Issue 4-1-7: Test metric

## Slide 3: PRACH performance requirements
PRACH formats
  A2, B2, and C2

## Slide 4: PRACH performance requirements
Test scenario parameters
  Antenna configuration
    1x2
  Propagation conditions
    AWGN
    Fading channel
      Option 1: TDLC300-100
      Option 2: TDLA30-10
  Frequency offset
    400Hz

## Slide 5: PRACH performance requirements
Test scenario parameters
  Ncs
    Option 1:127 for LRA=1151 and 63 for LRA=571
    Option 2:164 for LRA=1151 and 190 for LRA=571
    Option 3: FFS
  Test metric
    Reuse existing test metrics: the false alarm probability shall be less than or equal to 0.1%, the probability of detection shall be equal to or exceed 99% and time error tolerance requirements FFS

## Slide 6: PRACH performance requirements
Test scenario parameters
  Time error estimation tolerance
    Option 1: New values:
    Option 2: Reuse the Table 8.4.2.1-1 of TS 38.104 for the moment, and encourage companies to bring analysis on the scaled tolerance for the next meeting.
    Other options are not precluded
PRACH preamble | PRACH SCS (kHz) | Time error tolerance | 
 |  | AWGN | [TDLA30-10 or TDLC 300]
[A2,] B4, C2 | 15 | [0.065us] | FFS
 | 30 |  | FFS