## Slide 1: WF on Rel-16 NR IAB demodulation requirements
3GPP TSG-RAN WG4 Meeting #97-e
Electronic Meeting, 2 – 13 Nov., 2020
Agenda: 7.4.8
R4-2017492
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
The following WFs were approved previously
  R4-2012644, WF on Rel-16 NR IAB demodulation requirements, RAN4#96-e.
Corresponding Email summary in RAN4#97-e
  R4-2017618 Email discussion summary for [97e][319] NR_IAB_Demod, RAN4#97-e.

## Slide 3: General
The following slides pertain to IAB Demod - General

## Slide 4: Workplan
Suggested workplan
  RAN4#97-e:
    Finish discussions on work plan and performance impact.
    Start discussions for requirements per physical channel.
    Start Simulation configuration alignments and FRCs.
  RAN4#98:
    Finish discussions per physical backhaul channel.
    Simulation results collection and alignment.
    Present draftCRs to decide skeletons for IAB demodulation requirements/conformance tests.
  RAN4#98-bis:
    Present draftCRs to introducing IAB demodulation requirements/conformance tests; some numbers can be in [] or TBD.
    Final round of simulation results collection and alignment.
  RAN4#99:
    Final draftCRs for TS 38.174 NR; Integrated Access and Backhaul (IAB) radio transmission and reception
    Final draftCRs for TS 38.xxx NR; Integrated Access and Backhaul (IAB) conformance testing

## Slide 5: Other
Connections between IAB-DU and IAB-MT testing
  Explicit test passing
    Both IAB-DU and IAB-MT requirements are passed explicitly
  Test environment
    Strive to ensure that the same test environment can be used to test both IAB-DU and IAB-MT.
Connection to IAB RF [GtW agreement - informative]
  Co-ordinate the decisions on IAB demod and IAB RF testing to the extent necessary to ensure that the approach to testing is consistent
Suggested bigCR work split
  Following chair guidance, do not further discuss for now and wait for bigCR split to be decided by specification rapporteur.

## Slide 6: IAB-DU
The following slides pertain to IAB Demod – IAB-DU

## Slide 7: General requirement scope
IAB DU backhaul and access link differences [GtW agreement - informative]
  RAN4 will introduce IAB-DU demodulation requirements covering UL access and backhaul links.
  No need to discriminate the test cases for these two links in the specification.
Additional requirement configurations on top of BS ones [GtW agreement - informative]
  There is no need to introduce any new performance requirements for IAB-DU in addition to already existing BS requirements.
Basis for requirement re-use [GtW agreement - informative]
  Based on Rel-15 gNB performance requirements to discuss IAB-DU performance requirements definition.

## Slide 8: General requirement scope
Applicability rule re-use
  Check and adapt the BS applicability rules to reduce the number of tests. For example, test only the highest number of supported antennas.

## Slide 9: Channel agnostic - Details of BS requirement re-use
General SCS/CBW combinations
  [GtW agreement - informative]
    In principle, reuse the existing BS requirements as generic approach meanwhile the exceptions for the specific test cases not excluded pending on further discussion.
    Using existing applicable rules for CHBW, SCS and number of RX antenna configuration as starting point, further refinement not precluded.
  Keep existing full set of requirements, w.r.t. SCS/CBW combination. Test applicability rules can be updated, to reduce to number of tests required.
General channel models
  Option 1: Skip cases with TDLB100-400 Low and TDLC300-100 Low for FR1 and TDLA30-300 Low for FR2. If there are no cases with other propagation conditions, replace the propagation conditions with TDLA30-10 Low for FR1 and TDLA30-75 Low for FR2.
  Option 2: No new channel models shall be introduced. Skip cases with TDLB100-400 Low and TDLC300-100 Low for FR1 and TDLA30-300 Low for FR2, if there are alternatives.
  Option 3: No new channel models shall be introduced. All channel models used in Rel-15 BS testing should be re-used for IAB-DU and applicability rules can be introduced/modified to allow reduction of testing load.

## Slide 10: Channel agnostic - Details of BS requirement re-use
Inclusion of Rel-16 HST requirements
  Do not include existing Rel-16 HST requirements (including UL TA).
Other Rel-16 BS demod requirements
  Do not include Rel-16 BS demod requirements, i.e., the following (HST discussed separately)
    30% TPUT requirements for PUSCH with transform precoding disabled.
    2-step RACH
    NR-U
    URLLC 0.001% BLER
    URLLC high reliability
    URLLC low latency

## Slide 11: Channel agnostic - Details of BS requirement re-use
Inclusion of CA notes
  Option 1: Do not include performance requirements or text related to CA.
  Option 2: Follow Rel-15 approach and clarify that CA can be operated but is tested per carrier.
General RX demodulation branches
  [GtW agreement - informative] Using existing applicable rules for CHBW, SCS and number of RX antenna configuration as starting point, further refinement not precluded.
  All existing antenna configurations shall be kept, when re-using BS demod requirements. An applicability rule shall be defined to test only maximum number of antennas declared to be supported by the manufacturer for the respective BS type, i.e., up to 8Rx in conducted/hybrid testing and up to 2Rx in OTA testing.
Conducted and OTA requirements
  Specify both conducted and OTA tests for IAB-DU.

## Slide 12: PUSCH - Details of BS requirement re-use
PUSCH MCS
  Option 1: Do not use QPSK and 16QAM MCS.
  Option 2: Keep all MCS from BS demodulation requirements.
  Option 3: Keep all MCS for BS demodulation requirements, but with applicability rule that IAB-DU only needs to pass the test with the supported highest modulation order based on BS declaration.
PUSCH mapping type
  Copy existing requirements and apply BS demod like applicability rule for testing.
PUSCH transform precoding
  Option 1: Re-use only requirements for PUSCH with transform precoding disabled.
  Option 2: Include requirements for PUSCH with transform precoding enabled.
  Option 3: Include requirement for PUSCH with transform precoding enabled and define applicability rule for it.
Copying of all Rel-15 PUSCH BS demod requirements
  Option 1: Copy all Rel-15 PUSCH BS demod requirements and discuss applicability rule inclusion or adaptation to reduce the number of tests.
  Option 2: Discuss each Rel-15 PUSCH BS demod requirement configurations separately.

## Slide 13: PUCCH - Details of BS requirement re-use
PUCCH DM-RS configuration
  Keep existing BS demodulation based DM-RS configurations.
PUCCH multi-slot
  Option 1: Skip cases for multi-slot PUCCH.
  Option 2: Include multi-slot PUCCH cases and keep or modify existing BS demodulation-based test applicability rule.
PUCCH number of test cases
  Keep all the PUCCH requirements and related test applicability rule, if BS declares to support more than one PUCCH formats, limit the number of tests chosen by the manufacturer using applicability rule. FFS: Exact limiting of tests.
Copying of all Rel-15 PUCCH BS demod requirements
  Option 1: Copy all Rel-15 PUCCH BS demod requirements and discuss applicability rule inclusion or adaptation to reduce the number of tests.
  Option 2: Discuss each Rel-15 PUCCH BS demod requirement configurations separately.

## Slide 14: PRACH - Details of BS requirement re-use
PRACH formats
  Option 1: Only keep format 0 with 1.25kHz SCS and C2 with 30kHz and 120kHz SCS for PRACH performance requirements
  Option 2: Keep all PRACH formats and discuss applicability rule.
  Option 3: Only copy-paste TDLC300-100/TDLA30-300 cases (currently TDLC300-100/TDLA30-300 and AWGN) for FR1 and FR2 respectively.
    For BS declares to support more than one PRACH formats, limit the number of tests to any two cases chosen by the manufacturer using applicability rule.
Copying of all Rel-15 PRACH BS demod requirements
  Option 1: Copy all Rel-15 PRACH BS demod requirements and discuss applicability rule inclusion or adaptation to reduce the number of tests.
  Option 2: Discuss each Rel-15 PRACH BS demod requirement configuration separately.
  Option 3: Only copy-paste TDLC300-100/TDLA30-300 cases (currently TDLC300-100/TDLA30-300 and AWGN) for FR1 and FR2 respectively.
    For BS declares to support more than one PRACH formats, limit the number of tests to any two cases chosen by the manufacturer using applicability rule.

## Slide 15: IAB-MT
The following slides pertain to IAB Demod – IAB-MT

## Slide 16: Conformance testing setup
General approach
  Option 1: Define IAB-MT demodulation tests in the same manner as BS demodulation tests in RAN4. Strive to not preclude (but also not necessitate) UE style testing
  Option 2: Consider IAB-MT as a part of a network node with test setup and performance requirements based on the BS approach.
  Option 3: The IAB-MT demodulation test setup needs to be a mix of the BS setup and the UE setup.
DUT placement reference point and orientation [GtW agreement - informative]
  Coordinate reference point and orientation of the IAB-MT under test is for manufacture declaration.
DUT feedback [GtW agreement - informative]
  HARQ/RV feedback done via an error-free digital feedback, the feedback linkage to TE still FFS.
KPI deriving entity [GtW agreement - informative]
  No need to be specified in the specification for KPI deriving entity.

## Slide 17: Conformance testing setup
Detailed test setup
  Option 1: Use a test setup that offers the possibility for testing with a unidirectional Uu interface. The DUT being allowed to knowingly be in a L1/L2 test mode with hardcoded RRC and using TDD pattern independent FRC-like requirements to describe the KPI relevant channel structure. Time synchronization can be provided either via the digital feedback link from the tester or by a common (e.g., GNSS) source, or by Uu interface
  Option 2: Reuse the existing test setup for BS approach.
  Option 3: Reuse the existing test setup for BS approach, do not preclude Uu interface as alternative.
  Option 4: Use a test setup that offers the possibility for testing with a unidirectional Uu interface. The DUT being allowed to knowingly be in a L1/L2 test mode with hardcoded RRC and using TDD pattern independent FRC-like requirements to describe the KPI relevant channel structure.
  Other options not precluded
Questions on performance aspects
  Q1: Which configurations of the Uu interface (i.e., channels and signals) are required for performance testing, that are not the channel/signal under test?
    E.g., in PDSCH demodulation testing with TPUT KPI, is there a meaningful difference between running the test with T-RS/SSB as configured in UE demod, and using optimal synchronization without transmitting T-RS/SSB?
    This question also partially encompasses enquiries and responses regarding the rationale behind the manifold proposals to remove test parameters from UE demod derived requirements.

## Slide 18: General requirement scope
Basis for requirement re-use
  Use Rel-15 UE demodulation requirements as a basis for requirement development.
  FFS:
    Option 1: Define IAB MT performance requirements solely based on Rel-15 UE performance requirements. Configurations cannot be changed, only removed.
    Option 2: Define IAB MT performance requirements based on Rel-15 UE performance requirements; Rel-16 requirements can be added according to operator request. Configurations cannot be changed, only removed.
    Option 3: Define IAB MT performance requirements as a strict down selection from Rel-15 and 16 UE performance requirements. Only channel models can be changed.
    Option 4: Define IAB MT performance requirements solely based on Rel-15 UE performance requirements. Test cases can be further down selection, the related test configurations (in test parameter table) can be further discussed to remove or update. Configurations (in minimum performance table) cannot be changed, only removed.
Applicability rule for different SCS/CBW
  Define test applicability rule for IAB-MT supporting different CBW&SCS.
Requirements for MT types and classes
  Type
    Only conducted performance requirements shall be defined for type 1-H (no duplication of conducted and radiated test). Radiated performance requirements shall be defined for type 1-O and 2-O.
  Class
    Option 1: The same requirements apply for all classes (local and wide area).
    Option 2: The requirements to test differ by class (local and wide area).

## Slide 19: Requirement agnostic - Details of UE requirement re-use
Conducted and OTA requirements
  Specify both conducted and OTA tests for IAB-MT.
CBW/SCS
  Specify requirements for 40MHz for 30kHz, 50MHz for 60kHz, and 100MHz for 120kHz. The applicability rule used in existing BS demodulation requirements for testing of larger bandwidths than the specified one should be reused. I.e., the tests shall be done by using performance requirement for the closest channel bandwidth lower than this widest supported bandwidth; the tested PRBs shall then be centered in this widest supported channel bandwidth.
  Note: 40MHz/15kHz requirements are not present in TS 38.101-4 and 10MHz/15kHz is for FDD only.
TDD pattern
  FFS: Specify requirements with one TDD pattern configuration and declare the requirements to be applicable for any configuration

## Slide 20: Requirement agnostic - Details of UE requirement re-use
HARQ
  Number of HARQ process and k1 configurations can be ignored.
TDRA
  K0 configurations can be ignored.
High speed scenarios
  Skip test cases that are related to high speed scenario such as cases with TDLB100-400 Low, TDLC300-100 Low, HST for FR1 and TDLC60-300 Low, TDLA30-300 Low for FR2.
General RX demodulation branches
  4Rx for conducted test only and 2Rx for radiated test only for FR1 and 2RX for FR2

## Slide 21: Requirement agnostic - Details of UE requirement re-use
FDD and TDD requirements
  Do not specify FDD requirements.
Testing in both conducted and radiated testing
  Option 1: Only conducted performance requirements are defined for FR1 in the existing UE demodulation requirements in TS 38.101-4, it is not necessary to repeat to test the same performance requirements for both conducted and radiated testing.
  Option 2: Other options not precluded.
Inclusion of Rel-16 requirements
  Do not include Rel-16 UE demod requirements, i.e., the following (HST is excluded)
    FR2 256 QAM
    URLLC 0.001% BLER
    URLLC high reliability
    URLLC low latency

## Slide 22: PDSCH - Details of UE requirement re-use
MCS
  QPSK shall not be tested.
  64QAM shall be tested
  16 QAM
    Option 1: 16QAM shall be tested.
    Option 2: 16QAM shall not be tested.
PRB bundling size
  Only keep requirements with PRB bundling size 2.
Mapping type
  Option 1: Only keep PDSCH performance requirements for mapping Type-A
  Option 2: Include requirements for mapping type A and B. Use applicability rule to reduce testing load.
HARQ soft combining
  Skip PDSCH cases for HARQ soft combining.

## Slide 23: PDSCH - Details of UE requirement re-use
Enhanced receiver
  Option 1: Skip PDSCH cases for enhanced receiver Type 1.
  Option 2: Include requirements for enhanced receiver Type 1 but allow to declare support.
CSI-RS overlapped with PDSCH
  Option 1: Skip PDSCH cases for CSI-RS overlapped with PDSCH.
  Option 2: Keep a down scoped set of PDSCH cases for CSI-RS overlapped with PDSCH.
Relative TPUT and slot configuration
  FFS: Investigate further how dependent the SNR for achieving relative throughput (e.g. 70%) is on the slot configuration (in particular for high SNR).
Test parameters specification simplification
  Option 1: Remove the following parameters from the UE demod PDSCH requirements and leave them up to implementation:
    PDCCH configuration,
    CSI-RS for tracking,
    ZP CSI-RS.
  Other options not precluded

## Slide 24: PDSCH - Details of UE requirement re-use
PDSCH co-existence with LTE CRS
  Option 1: Skip PDSCH cases for co-existence with LTE CRS.
  Option 2: Keep PDSCH cases for co-existence with LTE CRS.

## Slide 25: PDCCH - Details of UE requirement re-use
Aggregation level
  Option 1: Only keep PDCCH performance requirements with AL 8.
  Option 2: Include all requirements but declare which is supported and/or use applicability rule.
  Option 3: The MT has to support all aggregation levels and there is no capability to inform the parent about support.
Test parameters specification simplification
  Option 1: Remove the CSI-RS for tracking parameters from the UE demod PDCCH requirements and leave them up to implementation.
  Option 2: Keep the CSI-RS for tracking parameters from the UE demod PDCCH requirements. Since the link is configured by the parents this cannot be left to implementation. The MT is supposed to work with different parents.

## Slide 26: SDR - Details of UE requirement re-use
Inclusion of SDR requirements
  Option 1: Do not include SDR requirements in IAB-MT demodulation.
  Option 2: Include SDR requirements in IAB-MT demodulation.

## Slide 27: CSI - Details of UE requirement re-use
Inclusion of CSI requirements
  Option 1: Heavily down scope CSI reporting requirements
  Other options not precluded
  Proposed WF: Please detail what is to be down scoped with reasoning behind it.
CSI-RS resource type
  Option 1: Only keep periodic NZP CSI-RS resource type for CQI/PMI/RI reporting cases.
  Option 2: Keep all UE demod configuration for NZP CSI-RS resource types for CQI/PMI/RI reporting cases.
CQI reporting granularity
  Option 1: Only keep wideband CQI reporting granularity for CQI/PMI/RI reporting cases.
  Option 2: Keep wideband and subband CQI reporting granularity for CQI/PMI/RI reporting cases
CQI/PMI/RI reporting type
  Option 1: Only keep periodic CSI reporting type for CQI/PMI/RI reporting cases.
  Option 2: Keep periodic and aperiodic CSI reporting type for CQI/PMI/RI reporting cases.

## Slide 28: CSI - Details of UE requirement re-use
Test parameters specification simplification
  Option 1: Remove the following parameters from CSI reporting requirements and leave them up to implementation: PDCCH configuration, CSI-RS for tracking, ZP CSI-RS.
  Option 2: Do not remove the following parameters from CSI reporting requirements and leave them up to implementation: PDCCH configuration, CSI-RS for tracking, ZP CSI-RS. It cannot be left to implementation, as the MT will not configure this link.
CQI two tap channel model
  Option 1: Skip two tap channel model for CQI test cases.
  Option 2: Keep two tap channel model for CQI test cases.

## Slide 29: Interworking - Details of UE requirement re-use
Inclusion of interworking requirements
  Option 1: Skip LTE-NR coexistence/DC/etc. requirements.
  Option 2: Keep LTE-NR coexistence/DC/etc. requirements and allow to declare support.