## Slide 1: Use of 5 MHz overlapping channel BWs to cover spectrum blocks between 5 and 10 MHz
T-Mobile USA
3GPP TSG-RAN4 Meeting #97-e R4-2016455
Online, , 2 - 13 Nov 2020

## Slide 2: Overlapping channel Bandwidths
It may be possible to use two overlapping channel bandwidths that are smaller than the operator channel bandwidth to cover the operator’s licensed spectrum.
While any individual UE cannot use the entire licensed bandwidth, the network could use the entire bandwidth.
New gNB channel BWs may be needed. Some believe the gNB can use overlapping channel BWs, but this could be an implementation issue.
For overlapping channels, both channels need to cover the SSB.
A 5 MHz carrier has 4.5 MHz of RBs, so two 5 MHz channels can only be offset by a maximum of 900 kHz and still cover the 3.6 MHz SSB. Therefore overlapping 5 MHz channels with a shared SSB can cover 5.9 MHz of spectrum, but cannot cover 7 MHz of licensed spectrum. There is only 3 MHz of overlap (2.5 MHz of overlapping RBs) for two 5 MHz carriers covering 7 MHz
Overlapping channel BWs
7 MHz license (and BS CH BW)
5 MHz UE CH BW
5 MHz UE CH BW

## Slide 3: Overlapping channel Bandwidths
Since two adjacent SSBs would require 40 RBs (7.2 MHz), it is not possible to have two time aligned adjacent SSBs in 7 MHz of spectrum
In order that each 5 MHz carrier contains an SSB, the SSBs would need to be offset in time.
Overlapping SSBs would unfortunately increase overhead %, but 0.189% (4 symbols per 20 ms) -> 0.377% (worst case)
Overlapping channel BWs
7 MHz license (and BS CH BW)
5 MHz UE CH BW
5 MHz UE CH BW
Question: Are there any Issues caused by overlapping SSBs that are offset in time?
SSB1
SSB2
Frequency
Time
5 MHz UE CH BW
5 MHz UE CH BW

## Slide 4: Time offset SSBs?
If the SSBs are offset in time and the gNB wants to move a UE from one carrier to another for load balancing, does the UE need to resync to find the SSB on the other carrier or is there signaling for the network to tell the UE the offset of the SSB in the other carrier?
The UE may not be able to receive on the one carrier and scan for the SSB on the other carrier, so resync would disrupt service.
SSB1
SSB2
Frequency
Time
5 MHz UE CH BW
5 MHz UE CH BW

## Slide 5: Overlapping channel Bandwidths for 8-10 MHz of licensed spectrum
Adjacent SSBs occupy 7.2 MHz of spectrum.
With 242.5 kHz minimum guardband, at least 7.685 MHz of spectrum is required for adjacent (time-aligned) SSBs
Time aligned SSBs may work for operator licensed bandwidths of 8 or 9 MHz depending on the SSB raster alignment.
Overlapping channel BWs
8 MHz license (and BS CH BW)
5 MHz UE CH BW
5 MHz UE CH BW
SSB1
SSB2

## Slide 6: Summary comments/questions
To align SCSs, the two carriers need to be offset by the least common multiple of 100 kHz and 15 kHz, so multiples of 300 kHz.
  5.3, 5.6, 5.9, 6.2 MHz, …
To align RBs, overlapping channel BWs can only be frequency offset by multiples of 900 kHz, the least common multiple of the 100 kHz raster and 180 kHz RB BW
  Available BWs: 5 MHz, 5.9, MHz, 6.8 MHz, 7.7 MHz, 8.6 MHz, 9.5 MHz
In order to support other channel BWs (multiples of 300 kHz instead of 900 kHz), would it be possible to blank partial RBs between allocations in the two offset carriers? The inefficiency of a guard RB might be more than offset by flexibility of supporting other BWs
If the SSBs are offset in time between the overlapping carriers, does that cause any problems if the network wants to have the UE switch from one of the overlapping carriers to the other? Does it need to re-sync, or would is there signalling to tell the UE the time location of the SSB for the overlapped carrier?

## Slide 7: Conclusions
Observation 1: With 6 MHz of licensed spectrum it is possible that a single SSB can be used for two overlapping 5 MHz carriers, but the frequency position would be limited by the SSB raster
Observation 2: With 8 or 9 MHz of licensed spectrum, overlapping 5 MHz carriers can use separate SSBs that are time aligned, although frequency position for covering 8 MHz might be limited by the SSB raster
Observation 3: With 7 MHz of licensed spectrum, separate SSBs that overlap in frequency but not in time will be required.
Proposal 1: RAN4 needs to decide if subcarrier alignment or RB alignment is required.
Proposal 2: Any potential issues for overlapping carriers need to be addressed including increased overhead and handover issues when the gNB moves UEs from one carrier to the overlapping carrier.