## Slide 1: WF on DC location reporting for intra-band UL CA
Huawei, HiSilicon
R4-2016816
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: Background
Comments from companies in RAN#89-e on the above solutions:
2 solutions provided in approved LS R4-2011906:
Report TX DC location after every activation of BWP’s including CC activation, BWP switching procedure, etc.
Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
Agreement in RAN#89-e for intra-band UL CA DC location:
Proposal: a mechanism of DC location reporting for intra-band UL CA should be specified in Rel-16
• RAN2 is tasked to provide at least one RAN2-based signalling solution for at least 2 UL CCs of intra-band UL CA in FR1 to RAN#90, considering forward compatibility to other combinations (more than 2 UL CCs and/or FR2)
• Other solutions are not precluded and can be discussed in RAN1, RAN2 and RAN4. Selection between solutions can be discussed at RAN#90 or later (if possible).
conclusion: proposal is endorsed
Almost all companies prefer solution 2 for Rel-16 considering the limited time budget and the potential spec impact to RAN1
It can be referred in RP-202018
RAN4 introduce UE capability of DC location for intra-band UL CA in FGI 7-5:
7-5 | DC location for intra-band CA | indicate whether UE support Additional DC location reporting for intra-band UL CA |  | Yes | N/A | The gNB cannot correctly calculate the DC location of intra-band CA

## Slide 3
Tx DC location for intra-band UL CA
In Rel-16, mechanism of DC location reporting is only defined for intra-band UL CA for two CCs in FR1
  If no concrete solution for more than 2 UL CCs reached in RAN4 #97-e, mechanism for 2 UL CCs of intra-band UL CA in FR1 should be defined, solution 2 in approved R4-2011906 is adopted for 2UL CCs
  RAN4 needs to find a solution for 2UL CCs in R16 at least
Factors affecting UL DC locations of intra-band UL CA in FR1
  CC and BWP factors:
    lowest and highest CC activated
    active BWPs in lowest and highest CC activated
    configured BWPs in lowest and highest CC activated
    There are other factors such as “Active BWP in the CCs other than lowest and highest CC activated” or “DL and UL LO dependency”, but they can be further studied in Rel-17
  PA architecture
    For UE indicating 1PA architecture, the number of DC location is one at an instant
    For UE indicating 2PA architecture, the number of DC location is two at an instant, in which one DC location serves for each PA
    each of the DC location can be reported based on one DC location method(s)

## Slide 4
Tx DC location for intra-band UL CA-con’d
Reporting mechanism
  RRC based signaling is adopted in Rel-16
If DC location falls into the gap between two CCs, reporting of 3300/3301 in R15 is still allowed for DC location of intra-band UL CA
In Rel-17, RAN4 will further discuss enhancements of DC location reporting for more than 2 CC case FR2(maybe also for FR1)
  Dynamic mechanism is not precluded in Rel-17