## Slide 1: WF on FR2 FWA RF requirements
SoftBank Corp.
3GPP TSG-RAN WG4 #97-e
2 – 13 November 2020
Electronic meeting
R4-2016874

## Slide 2: Background
Capture the open issues as follows:
  Minimum peak EIRP
  MBR
  MPR
  Beam Correspondence
  REFSENS

## Slide 3: Min. peak EIRP
Agreement in GTW session:
  30.0 dBm for n257, 30.4 dBm for n258

## Slide 4: MBR
Agreement in GTW session:
  Option 1: 0.7dB

## Slide 5: MPR
Agreement in GTW session:
  Option 2: MPR requirements reuse PC3 values

## Slide 6: Beam Correspondence
Option 1: Define bit-0 requirement (OPPO, MediaTek, Huawei, DOCOMO)
Option 2: Not define bit-0 requirement (QC, Nokia, Samsung, Sony, Ericsson, DOCOMO)
Option 3: Follow PC1 approach, i.e. no requirement defined in RAN4. No plan to specify in the future.
Notes: Qualcomm: It appears that there are strong and immediate concerns shared by many companies regarding agreement made in the online session for beam correspondence (GTW) . We echo multiple companies’ views that option 2 is appropriate (no bit 0 UE will be defined), but this view is also not agreeable. We have therefore replaced with FFS.

## Slide 7: REFSENS
Agreements in GTW session:
  -92.6dBm (n257)
  -92.8dBm (n258)
  Note: the values are under the condition of CBW=50MHz.