## Slide 1: Way forward on UE power imbalance requirements for FR1 CA and EN-DC
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #97-e
E-meeting, 2 – 13 November 2020
Agenda Item: 7.16.1.3
R4-2017570

## Slide 2
RAN4 # 95-e
  WF: R4-2008848
RAN4 # 96-e
  WF: R4-2012691
Background: WF in previous meeting

## Slide 3: Wayforward
For FR1 intra-band contiguous CA
MCS
  2Rx: MCS 26
  4Rx: MCS 27
Test applicability rule
  Reuse the following applicability rule from LTE CA power imbalance
    For FDD or TDD CA power imbalance tests, if they are tested with FDD or TDD intra-band contiguous CA configurations with 2 DL CCs, the test coverage can be considered fulfilled with FDD or TDD intra-band contiguous CA configurations with 3 or more DL CCs supported by the UE.
    For FDD or TDD 2 DL CCs, only test the supported intra-band contiguous CA configurations covering the lowest and highest operating bands.

## Slide 4: Wayforward
For intra-band contiguous and non-contiguous EN-DC
LO position
  “LO in middle” only
  Note: the LO position assumption is only for the purpose of defining demodulation requirements, and will not be specified in the spec. The exact implementation is up to UE.
Carrier for LTE in the test
  Consider the aggregated contiguous carriers for LTE if UE supports it and test scenario support it. The actual number of aggregated LTE carriers are up to RAN5 test setup.
PRB for NR carrier
    When the CBW of NR carrier is smaller than or equal to LTE carrier(s), test full PRBs;
    When the CBW of NR carrier is larger than LTE carrier(s), test partial PRBs, and the PRB number for testing equals to the PRB number in the full bandwidth of E-UTRA MCG carrier(s).
      If frequency of NR carrier is higher than LTE carrier, then the test RBs will be allocated on the highest part of NR carrier.
      If frequency of NR carrier is lower than LTE carrier, then the test RBs will be allocated on the lowest part of NR carrier.

## Slide 5: Wayforward
For intra-band contiguous and non-contiguous EN-DC
Channel bandwidth combination for testing
  Option 4A:
    Step 1: First select the CBW combinations with the same BWs between LTE carrier(s) and NR carrier. If there is no such CBW combination, go to Step 1a. Otherwise go to step 2.
    Step 1a: Select the CBW combinations that the BW of NR carrier is smaller than the BW of LTE carrier(s). If there is no such CBW combination, go to Step 1c.
    Step 1b: Among the CBW combinations selected from Step 1a, select the CBW combinations with the smallest CBW difference between NR carrier and LTE carrier(s). Go to step 2.
    Step 1c: select the EN-DC combinations with smallest CBW difference between the NR carrier and LTE carrier(s). Go to step 2.
    Step 2: Among the CBW combinations selected from Step 1, select the EN-DC combination with the largest aggregated CBW
Limitation on frequency separation for non-contiguous EN-DC
  No limitation in RAN4 requirements, test set-up up to RAN5

## Slide 6: Wayforward
For intra-band non-contiguous EN-DC
Test applicability rules
 | Inter-band scenarios are not supported | UE indicates “interBandContiguousMRDC” | UE does not indicate “interBandContiguousMRDC”
Intra-band scenarios are not supported | N/A | Requirement for intra-band contiguous EN-DC for inter-band scenarios | Requirement for intra-band non-contiguous EN-DC for inter-band scenarios
UE does not indicate “intraBandENDC-Support” | Requirement for intra-band contiguous EN-DC for intra-band scenarios | Requirement for intra-band contiguous EN-DC for intra-band and inter-band scenarios | Requirement for intra-band contiguous EN-DC for intra-band scenarios
UE indicates “both” in “intraBandENDC-Support” | Requirement for intra-band contiguous EN-DC for intra-band scenarios | Requirement for intra-band contiguous EN-DC for intra-band and inter-band scenarios | Requirement for intra-band contiguous EN-DC for intra-band scenarios
UE indicates “non-contiguous” in “intraBandENDC-Support” | Requirement for intra-band non-contiguous EN-DC for intra-band scenarios | Requirement for intra-band contiguous EN-DC for inter-band scenarios | Requirement for intra-band non-contiguous EN-DC for intra-band and inter-band scenarios

## Slide 7: Wayforward
For intra-band contiguous and non-contiguous EN-DC
Other test parameters
  MCS
    use the same MCS for 2Rx and 4Rx as that for FR1 intra-band contiguous CA.